## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for SRM IE and TPC PIB in Technical Guidance Document]
Date Submitted: [7 November, 2015]
Source: [Hidetoshi Yokota, Ruben Salazar and Chris Calvert] Company [Landis&Gyr]
Address: [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan,
30000 Mill Creek Av., Alpharetta, GA 30022, USA ]
Voice: [+81 3-5532-7455, +1 678 258 3165, +1 678 258 1516], E-Mail:[hidetoshi.yokota@landisgyr.com, ruben.salazar@landisgyr.com, chris.calvert@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-06-004s]
Abstract: [This contribution proposes Information Elements for SRM and PIB for Transmit Power Control that should be considered in the Technical Guidance Document for measuring spectrum resources in WPAN.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal for SRM IE and TPC PIB in Technical Guidance Document
Authors:

## Slide 3: Outline of the proposal
Propose SRM Information Element
Propose TPC for WPAN
Discussion
  Handling of existing MAC metrics IEs
References [1] IEEE802.15.4-REVc-D00

## Slide 4: SRM Information Element in Header IEs (IEEE802.15.4-REVc-D00[1])
Element ID | Name | Subclause
0x2a | SRM IE | 7.4.2.18
Bits:0-5 | 6-7 | Octet: 0-126
SRM Metric ID | Scope | Value
Format of SRM Metric ID
Attribute name | SRM Metric ID b5b4b3b2b1b0
macED | 000000
MacTxFailTime | 000001
… | …
SRM Metric ID
Measured range | Scope ID b1 b0
Link | 00
Path | 01
Network | 10
Reserved | 11
Scope
on the link of the transmitting device
on the path to/from PAN coordinator
over the entire PAN
Attribute represents the performance:

## Slide 5: Use case (1) Scope-based Performance Metric
Bits:0-6 | 7-14 | 15 | Octets:0-127 |  | 
Length | Element ID=0x2a | Type=0 | Bit:0-5 | 6-7 | Octet:0-126
 |  |  | Metric ID=0x12 | Scope=01 | Value=100
Attribute name | SRM Metric ID b5b4b3b2b1b0
… | …
macTxFailCount | 010010
… | …
SRM Metric ID
device
PAN
coordinator
device
device
device
device
device
device
Link-scope(00)
Path-scope(01)
Network-scope(10)
Enhanced Beacon
Header IE
how path-scope and network scope performance is calculated is outside the scope of the specification

## Slide 6: Transmit Power Control
Benefits
  Enable efficient spatial re-use of the radio spectrum reducing interference by minimizing transmit power while still maintaining stable links
  Contributes to network performance-aware applications
  Alleviates the well-known "hidden" and "exposed" node problems that are encountered in wireless networks
Node-by-node and/or communication type-based TPC will provide optimized control
phyBroacastTxPower
phyUnicastTXPower
peersTXPower (for specific peer devices)

## Slide 7: PIB description for Transmit Power Control (IEEE802.15.4-REVc-D00[1])
10.1.5 Transmit power
The Maximum Transmit Power, phyMaxTxPower, may be included in enhanced beacons to notify joining devices of the nominal transmit power level allowed on a network (e.g., based on the local regulation).
A compliant device shall have its nominal transmit power level indicated by its PHY parameter, phyTXPower, as defined in 11.3. This value shall not exceed phyMaxTxPower and may be adjusted by the information from the peer device.
The transmit power can further be set individually according to the communication type indicated by phyBroadcastTxPower, phyUnicastTXPower, peersTXPower, MinSNR and MinLinkMargin.
  Transmit power could be optimized by considering the minimum SNR and minimum link margin.
* Proposed text is in red

## Slide 8: Use case (2) Max Transmit Power in Enhanced Beacon
Max Transmit Power value is set by the PAN coordinator and included in each enhanced beacon transmitted. Joined devices receiving this value also include it in each enhanced beacon for joining devices.
Bits:0-6 | 7-14 | 15 | Octets:0-127 |  | 
Length | Element ID=0x2a | Type=0 | Bit:0-5 | 6-7 | Octets:4
 |  |  | Metric ID=0x06 | Scope=10 | Value=+10(dBm)
Attribute name | SRM Metric ID b5b4b3b2b1b0
… | …
phyMaxTXPower | 000110
… | …
SRM Metric ID
Device
Advertiser
Enhanced Beacon
Header IE
Set phyTxPower, etc.
Enhanced Beacon
Header IE

## Slide 9: PIB attributes for TPC
11.3 PHY PIB attributes
Table 181 - PHY PIB attributes
Attribute | Type | Range | Description
phyTXPower | Signed Integer | － | Nominal transmit power of the device in dBm using the Maximum Transmit Power IE or predefined. See Table 181.
phyMaxTXPower | Signed Integer | － | Nominal transmit power level allowed on a network. See Table 181.
phyBroadcastTxPower | Signed Integer | － | Transmit power in dBm while broadcasting. This value is managed by an upper layer but shall be lower or equal to phyTXPower.
phyUnicastTXPower | Signed Integer | － | Transmit power in dBm while sending a unicast. This value is managed by an upper layer but shall be lower or equal to phyTXPower.
phyPeersTXPower | List of phyPeerTXPower as defined in Table 181a | － | List of exceptions to the phyUnicastTXPower while transmitting to specific peer devices.
phyMinSNR | Signed Integer | － | Minimum SNR in dB
phyMinLinkMargin | Signed Integer | － | Minimum Link Margin in dB
Existing

## Slide 10: PIB attributes for TPC (continued)
Table 181a - Elements of phyPeersTXPower
Attribute | Type | Range | Description
deviceAddrMode | Enumeration | SHORT_ADDRESS, EXTENDED_ADDRESS | 
deviceAddress | As specified by the deviceAddrMode Parameter |  | Address of the peer device.
TXPower | Signed integer |  | Transmit power in dBm while transmitting to this peer. This value is managed by an upper layer but shall be lower or equal to phyTXPower.
 |  |  | Bits:0 | 1-7 | Octets:2/8 | 4
Length | Element ID | Type | Device AddrMode | Reserved | deviceAddress | TxPower
Figure - Format of phyPeersTXPower

## Slide 11: Use case (3) Signal quality related IEs
when multiple channels are used, the channel on which the measurement is executed needs to be specified
Device address for which the measurement is executed may also be needed to be specified
Possible attributes to which this rule can be applied
RSSI
Channel number
Address Mode
Attribute
macEd
macLqi
macRcpi
macRsni
macRssi
macNoiseHistogram
Device Address
Channel page
Channel used for the measurement
Device that sent the measured frame
Measured attribute
Required set of attributes

## Slide 12: Proposal of additional MAC PIB
5.2.3 SRM metrics specific MAC PIB
Attribute | Type | Range | Description
macChannelPage | Integer | Any valid channel page | Channel page for measurement
macChannelNumber | Integer | Any valid channel number | Channel number for measurement
macRxAddrMode | Enumeration | SHORT, EXTENDED | 
macRxDeviceAddress | As specified by the macRxAddrMode Parameter |  | Source address of the received frame that is used for measurement

## Slide 13: Discussion
Handling of existing MAC metrics IEs
  MAC Metrics IE (Sub-ID=0x1f) and All MAC Metrics IE (Sub-ID=0x20) are defined in Payload IE:MLME IE:Nested IE (7.4.4.1 Table 19)
    10 Attributes (macCounterOctets,…) are assigned Metric Count ID (0x00-0x0a) (7.4.4.7 Table 21)  all reused by SRM
  Should these IEs be obsoleted?