## Slide 1: What is the purpose of the randomly changing DevID?

## Slide 2: Usage of Next DEVID
Next DEVID indicates the DEVID value which will be assigned to the next associating device.
When PPC creates a new session, PPC sends a Beacon with the new “Next DEVID. A device which wishes to associate to the PPC shall set its DEVID with the “Next DEVID” value.

## Slide 3: The purpose of randomly changing DevID
If DevID is NOT changed, the previous DEV may continue to send frames to the PPC at any time even after the PPC has started a new P2P structure with new beacons.
 DevID needs to change per session.
How to change the DevID
  At random, with the value always changing.
  Incremented by 1.
    What initial value shall be set? Only initial value shall be set randomly?
   Randomly changed DevID is better.

## Slide 4: Beacon interval setting

## Slide 5: Superframe Structure
Beacon
PPAP
Associated
Phase
Unassociated
Phase
DEV
PPC
Beacon
Setup Time < 2ms
Association
Response
-Stop Beacon
-Send Association Response instead.
PPAP
Beacon
Association
Request command
Stk-Ack
Access
Slot
SIFS
Disassociation
Request
SIFS
or
RIFS
PPC can send Beacon
with new Next DEVID
Unassociated
Phase
SIFS
Access
Slot
Access
Slot
Multiple transmission of
Disassociation Request
under Np-Ack policy
are allowed.

## Slide 6: Beacon Interval
Beacon Interval consists of a SIFS and N AccessSlots.
Time length of AccessSlot is basically defined as time length of an Association Request command plus a SIFS.
DEV
PPC
Beacon
Beacon
Access
Slot
SIFS
Access
Slot
Access
Slot
SIFS
Association
Request command
Access
Slot
SIFS
Access
Slot
Access
Slot
Beacon

## Slide 7: Time duration
Long Preamble
FCS
(4 oct)
Beacon payload (14 oct + IE)
Association Req (15 oct + IE)
MAC Header
(10 oct)
2.328 us
MCS0, w/PW =2.2587Gbps
about 0.1 us
SIFS(default) :
  2.5 us
AccessSlot:
  about 5.7 us
Beacon, Association Request command:
  about 3.2 us
PHY header
0.69 us

## Slide 8: Collision Probability of Association Request command (1/2)
Assumption
  2 DEV’s which want to connect to a PPC are near the PPC.
    No need to consider case of more than 2 DEV’s.
  Collision avoidance probability should be kept above 90%.
DEV1
DEV2
PPC
less than 10cm
2) 2DEV’s are near a PPC
DEV1
PPC
1) a DEV is near a PPC
Collision does not occur

## Slide 9: Example
PPC
Beacon
Beacon
Access Slot
SIFS
Access Slot
Beacon
Access Slot
Beacon
SIFS
SIFS
DEV1
DEV2
1) K =1
no collision
PPC
Beacon
Beacon
Access Slot
SIFS
Access Slot
Beacon
Access Slot
Beacon
SIFS
SIFS
DEV1
DEV2
2) K =2
collision
DEV1
DEV2
no collision
Expected Duration
Expected Duration
no collision probability = (N-1) / N
collision probability = 1 / N
no collision probability = (N-1) / N

## Slide 10: Collision Probability of Association Request command (2/2)
Relation between K and N to bring collision probability below 10%,
  where N= number of AccessSlot
  K = minimum number of Beacons necessary to bring collision probability below 10%.
Expected Duration(ED(K,N)) to bring collision probability below 10%,
ED(K,N) = K ×(Beacon + SIFS) +K×N×AccessSlot.
∑(1/N)i-1((N-1)/N) >= 90%
i=1
K

## Slide 11: Conclusion
Calculation Results
Conclusion
N=4 is optimum, where the expected duration becomes shortest.
When the number of AccessSlots per Beacon is set 4, then Beacon interval equals about 28.5us.
K | N | Expected duration (CP is less than 10%) | Value[us]
1 | 10 | 1 × (Beacon + SIFS) +10 × Access Slot | 62.7
2 | 9 | 2 × (Beacon + SIFS) + 18 × Access Slot | 114
2 | 5～8 | 2 × (Beacon + SIFS) + (10～16) × Access Slot | 68.4～102.6
2 | 4 | 2 × (Beacon + SIFS) + 8 × Access Slot | 57
3 | 3 | 3 × (Beacon + SIFS) + 9 × Access Slot | 68.4
4 | 2 | 4 × (Beacon + SIFS) + 8 × Access Slot | 68.4

## Slide 12: Define a MAC/PHY interface for the OOK and SC PHYs.

## Slide 13: PHY SAP service Primitives
PHY-CCA primitives are not required, since HRCP does not use Carrier Sense mechanism.
Remove

## Slide 14: PHY SAP service Primitive Parameters
CCA Status parameter is not required.
LQI (Link Quality Indication) is not required, since HRCP does not support TCM coded QAM mode using an SNR estimation.
SC, MIMO and OOK parameters may be added after completing
PHY discussion.
Remove
Remove

## Slide 15: What is Link Quality indication?

## Slide 16: Correcting the use of MLME Association.indication

## Slide 17: Remove second MLME Associate.ind
DEV-1
DME
DEV-1
MAC/MLME
PPC
MAC/MLME
PPC
DME
Unassociated
MLME-ASSOCIATE.req
Beacon
NEXT DEVID = 0xZZ
Association Request command
DEVID = 0xZZ
DEV addr =DEV-1 addr
MLME ASSOCIATE.ind
DEVID = 0xZZ
DEV addr =DEV-1 addr
MLME ASSOCIATE.rsp
DEVID = 0xZZ
DEV addr =DEV-1 addr
Stop Beacon
Association Response command
DEVID = 0xZZ
DEV addr =DEV-1 addr
Stk-Ack
SrcID= 0xZZ
MLME-ASSOCIATE.cfm
- DEVID= 0xxZZ
AssocTimout
MLME ASSOCIATE.ind
DEVID = 0xZZ
DEV addr =DEV-1 addr
AssocTimout
KEY
req=request
ind=indication
rsp=response
cfm=confirm
addr=address
Remove

## Slide 18: 802.15.3 MLME Associate.ind process
DEVID= UnassocID
DEVID= 0xZZ