## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Optimum length of subframe for TG3e]
Date Submitted: [12 November 2015]
Source: [Makoto Noda]
Company: [Sony Corporation]
Address1: [1-7-1 Konan, Minato-ku, Tokyo 108-0075]
E-Mail1: [MakotoB.Noda at jp.sony.com]
Abstract: This document presents evaluation results of optimum length of subframe for TG3e.
Purpose: For supporting to determine the maximum length of subframe in TG3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
In TG3e proposal, the maximum length of subframe in MAC layer has been T.B.D., see 15-0663/r02.
For supporting to determine the maximum length of subframe in TG3e, this document provides the optimum length of subframe calculated by using the TG3e-frame format.
For obtaining the optimum length, an effect of subframe-error rate has been incorporated into a calculation of a data throughput in this work.

## Slide 3: Fragmentation and aggregation
(b) Frame aggregation
A MAC-SAP data unit (MSDU) is divided and allocated into m subframes.
fragmented
MSDU
This work evaluates the optimum Ls in a frame fragmentation
v3
fragmented
MSDU
v1
fragmented
MSDU
v2
fragmented
MSDU
vm
subframe #1
vi: i-th subframe overhead consisting of FCS and the subframe header
subframe #2
subframe #3
subframe #m
an MSDU
(a) Frame fragmentation
Each subframe includes an MSDU.
1st
MSDU
v3
2nd
MSDU
v1
3rd
MSDU
v2
m-th
MSDU
vm
subframe #1
subframe #2
subframe #3
subframe #m
Ls
length of a fragmented MSDU

## Slide 4: Definition of Data_Throughput
Data_Throughput is defined as a data throughput transferred from the MAC to the PHY across the PHY-SAP as following:
T_PLD + 2*(T_PAS + T_BHD + T_SIFS)
α·B_PLD
Data_Throughput =
preamble
(short)
PHY
Header
MAC
Header
payload
HCS
payload
overhead
1
T_PAS
416B
1.891 µs
2
T_BHD
16B
0.691 µs
3
T_PLD
preamble
(short)
PHY
Header
MAC
Header
HCS
4
T_SIFS
2.5 µs
preamble
(short)
4
T_SIFS
2.5 µs
data frame
ACK frame (2.582 µs)
Data frames and ACK frame
T_PLD = m(Ls + B_FCS + B_SHD)/r = (Ls + 64)m/r
α: a frame efficiency depending on a data-error rate and an ACK scheme employed
r: a PHY-SAP payload-bit rate between 2258.7 and 13141 Mb/s
m: number of subframes, B_FCS: bit length of FCS, B_SHD: bit length of subframe header

## Slide 5: Analysis of efficiency for Stack ACK
In TG3e proposal, Stack ACK (Stk-ACK) is employed as the ACK scheme.
A probability that i-consecutive (0<i ≤ m–1) subframes with a subframe-error probability of ps are correct and that (i+1)-th subframe is incorrect is (1 – ps)i·ps.
Therefore, a frame efficiency α for Stk-Ack, αstk, which is a ratio of an expected number of correct subframes to all subframes in a frame, is:
subframe
#1
subframe
#2
subframe
#k
subframe
#k+1
subframe
#m–1
Figure of k-th subframe error occurred in a frame consisting of m subframes
subframes regarded as errors for Stk-Ack
subframe
#k–1
subframe
#m
Here we assumed:
bER: bit-error rate

## Slide 6: MCS table for SC-PHY in TG3e proposal
Index of MCS identifier, i | single-carrier modulation | FEC Rate | PHY-SAP payload-bit rate, ri (Gb/s) |  | bit-rate ratio, ri/ri+1
 |  |  | w/o PW | w/ PW | 
0 | π/2 QPSK | 11/15 | 2.5813 | 2.2587 | 0.7857
1 | π/2 QPSK | 14/15 | 3.2853 | 2.8747 | 0.6364
2 | 16QAM | 11/15 | 5.1627 | 4.5173 | 0.7857
3 | 16QAM | 14/15 | 6.5707 | 5.7493 | 0.8485
4 | 64QAM | 11/15 | 7.7440 | 6.7760 | 0.7857
5 | 64QAM | 14/15 | 9.8560 | 8.6240 | 0.7500
6 | 256QAM | 14/15 | 13.1413 | 11.4987 | -
Data-rate loss defined as DATA_Throughput/ri has been evaluated

## Slide 7: Evaluation to obtain the optimum subframe length (1)
Length of a Fragmented MSDU, Ls (Octets)
Data-rate Loss (%)
Length of a fragmented MSDU dependence of data-rate loss
optimum
Chart: 
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288
bER = 1e-7 | -99.9957 | -99.9785 | -99.902 | -99.5809 | -98.2729 | -93.1259 | -75.1499 | -45.1397 | -28.2945 | -22.9571 | -21.6268 | -21.5036 | -21.9176 | -22.9134 | -24.9257 | -28.8556 | -36.2875
bER = 1e-8 | -99.953 | -99.7742 | -98.9968 | -95.7587 | -82.704 | -48.3246 | -19.8996 | -9.2902 | -6.2609 | -5.4441 | -5.2292 | -5.1911 | -5.2302 | -5.3458 | -5.5904 | -6.0837 | -7.0677
bER = 1e-10 | -95.2508 | -78.0298 | -42.0067 | -17.7844 | -8.4351 | -5.1899 | -3.996 | -3.5126 | -3.2999 | -3.2009 | -3.1533 | -3.1303 | -3.1193 | -3.1148 | -3.1145 | -3.1181 | -3.1276
no fragmentation
PHY-SAP payload-bit rate: 13.14 Gb/s
(MCS6/256QAM without pilot word)
an MSDU length = 219 = 524,288 Octets
the maximum length in the latest draft

## Slide 8: Evaluation to obtain the optimum subframe length (2)
Chart: 
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144
bER = 2e-7 | -99.9915 | -99.9569 | -99.8042 | -99.1634 | -96.5726 | -86.6682 | -59.85 | -34.7567 | -24.8742 | -22.1464 | -21.6456 | -21.9586 | -22.9263 | -24.9302 | -28.8573 | -36.2882
bER = 1e-7 | -99.982 | -99.9116 | -99.6031 | -98.3157 | -93.1224 | -74.0248 | -40.4768 | -21.2067 | -14.9962 | -13.3575 | -13.0432 | -13.2025 | -13.7345 | -14.8532 | -17.0805 | -21.4223
bER = 1e-10 | -81.6144 | -47.6572 | -22.2183 | -11.0406 | -6.5736 | -4.702 | -3.865 | -3.4721 | -3.2821 | -3.1888 | -3.1427 | -3.12 | -3.1092 | -3.1047 | -3.1044 | -3.108
Data-rate Loss (%)
the maximum length in the latest draft
optimum
no fragmentation
PHY-SAP payload-bit rate: 6.57 Gb/s
(MCS3/16QAM without pilot word)
an MSDU length = 218 = 262,144 Octets
Length of a Fragmented MSDU, Ls (Octets)
Length of a fragmented MSDU dependence of data-rate loss

## Slide 9: Discussions and conclusion
Decreasing bER, increasing the optimum length of fragmented MSDU to the MSDU length. Therefore, the maximum length of a fragmented MSDU should be the same as the maximum length of MSDU for maximizing the data throughput.
However, a data throuput is almost saturated at a length larger than 8,196 Octets, which is the value in the latest TG3e draft, when bER is sufficiently small. Moreover, the value of 8,196 Octets is very close to the optimum values in many cases when bER is relatively large.
Therefore, a maximum length of fragmented MSDU of 8,196 Octets would be reasonable if one want to restrict the maximum length for some other reasons.

## Slide 10: END