## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Motion for teleconference on December 21st]
Date Submitted: [ December 21st, 2015 ]
Source: [Marco Hernandez, Huan-Bang Li, Igor Dotlić, Ryu Miura ]
Company: [NICT]
Address: [3-4 Hikarino-oka, Yokosuka, 239-0847, Japan]
Voice:[+81 46-847-5439] Fax: [+81 46-847-5431] E-Mail:[]
Re: [In response to call for technical contributions TG8]
Abstract: [ ]
Purpose: [Material for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC command frames clause
5.7 is the current clause for MAC command frames in the Draft v0.16.1.
It seems to be a contribution of long time ago, because there are some issues:
  In page 65, line 17: “MAC commands shall not be transmitted in the CFP”, which is incorrect.
  In Table 21, there is a command for re-peering, but in clause 6 MAC services, there is not re-peering (request/response), because we decided to repeat peering (request/response) in case of re-peering for simplicity.
  In Table 21, there is a command for de-peering (request/response), but in clause 6, we decided to use de-peering notification only.

## Slide 3: MAC command frames clause
Moreover, there is an issue in the description of clause 5.7 “MAC Command Frames”:
  The reason is we have unicast and multicast (one-to-many and many-to many) cases for source and destination addresses in the MHR.
  However, the payload field is independent of these addressing.
  There is no reason to have clauses for one-to-one peering command, one-to-many peering command, many-to-many peering command for instance, as the current clause 5.7 suggests.
  So that clause 5.7 “MAC Command Frames” should describe the payload fields for MAC command frame: Command ID field and Content field, and relevant MHR fields except addressing fields.

## Slide 4: MAC command frames clause
MAC command frame (peering case):
Associated to:
one-to-one
one-to-many
many-to-many
Non applicable
Applicable

## Slide 5: MAC command frames clause
That is, clause 5.7 should not include the cases for one-to-one, one-to-many, etc., but only the description for Command ID field and Content field, and relevant MHR fields except addressing fields.
  MHR fields for addressing: unicast and multicast, that is one-to-one, one-to-many, many-to-many addressing cases should be described in clause 5.1 “MAC Functional description”, no in Clause 5.7
Thus, a harmonized text is presented in DCN 15-987r1

## Slide 6: Motion to accept MAC commands text
Marco moves a motion to accept the harmonized text on MAC commands text in DCN 15-987r1 to replace the text in clause 5.7 of the Draft Standard v.0.16.1.
  Second:
  Vote: