## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: pureLiFi 802.15.7r1 proposal for High Speed PD OWC communications
Date Submitted: January 2016
Source: Dr. Nikola Serafimovski Company: pureLiFi Ltd.
Address: pureLiFi Ltd. ETTC, Max Born Crescent, Edinburgh, EH9 3BF, UK
Voice: +44-131-472-4704, E-Mail: nikola.serafimovski@purelifi.com
Re:
Abstract:
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: pureLiFi 802.15.7r1 proposal for High Speed PD OWC communications

## Slide 3: PHY Frame Structure

## Slide 4: PHY Modulation-dependent Parameters

## Slide 5: PHY Modulation-dependent Parameters

## Slide 6: PHY OFDM preamble structure

## Slide 7: PHY SIGNAL field bit arrangement

## Slide 8: PHY Modulation-dependent Parameters (PHY MOD Choice)
 | Table 5: Modulation-dependent Parameters |  |  |  | 
 | R1-R4 | Data rate (Mb/s) (20 MHz channel) | Data rate (Mb/s) (15 MHz channel) | Data rate (Mb/s) (10 MHz channel) | Data rate (Mb/s) (5 MHz channel)
OFDM | 1101 | 6 | 4.5 | 3 | 1.5
 | 1111 | 9 | 6.75 | 4.5 | 2.25
 | 0101 | 12 | 9 | 6 | 3
 | 0111 | 18 | 13.5 | 9 | 4.5
 | 1001 | 24 | 18 | 12 | 6
 | 1011 | 36 | 27 | 18 | 9
 | 0001 | 48 | 36 | 24 | 12
 | 0011 | 54 | 40.5 | 27 | 13.5
eU-OFDM | 1100 | 5.25 | 3.93 | 2.62 | 1.31
 | 1110 | 7.87 | 5.9 | 3.93 | 1.96
 | 0100 | 10.5 | 7.87 | 5.25 | 2.62
 | 0110 | 15.75 | 11.81 | 7.87 | 3.93
 | 1000 | 21 | 15.75 | 10.5 | 5.25
 | 1010 | 31.5 | 23.62 | 15.75 | 7.87
 | 0000 | 42 | 31.5 | 21 | 10.5
 | 0010 | 47.25 | 35.43 | 23.62 | 11.81

## Slide 9: PHY SERVICE field bit arrangement

## Slide 10: PHY Scrambler

## Slide 11: PHY Convolutional Encoder

## Slide 12: PHY Puncturing
Same as 802.11
  Enables 2/3 Rate encoding
  Enables ¾ Rate encoding

## Slide 13: PHY Data interleaver used from the 802.11
pureLiFi implementation
  64-bit interleaver for a 64 sub-carrier OFDM modulation

## Slide 14: PHY Mapping
pureLiFi implementation
  Subcarrier modulation mapping
    Gray mapping of bits with:
      1 bit – BPSK
      2 bit – QPSK
      4 bit – 16 QAM
      6 bit – 64 QAM
  Standard OFDM modulation
  Subcarrier 7 and 21 are Pilot subcarriers to help determine:
    Phase changes that may exist on a frame-per-frame basis coming from the oscillation drift from the Tx and Rx clocks

## Slide 15: PHY Transmit PLCP

## Slide 16: PHY Transmit State Machine

## Slide 17: PHY Receiver PLCP

## Slide 18: PHY Receiver State Machine

## Slide 19: MAC Frame Format (pureLiFi and 802.11)

## Slide 20: MAC Frame Format (pureLiFi and 802.11)

## Slide 21: MAC Type & Subtype fields

## Slide 22: MAC Ack Info field
Support up to 16 devices per light, easily extendable to more if necessary
  Fixed field size is necessary
“Duration” field is always fixed to a constant value, therefore, the Ack Info field size can be changed to support more devices

## Slide 23: MAC Sequence Control field
Support up to 16 devices per light, easily extendable to more if necessary
  Fixed field size is necessary
“Queue Number” field is irrelevant for higher layer, therefore, the Sequence Control field size can be changed to support more devices

## Slide 24: MAC Frame Check Sequence (FCS)

## Slide 25: MAC Format of individual frame types
All frame types and structures are the same as in 802.11a
The Beacon frame is sent periodically to check which Stations are connected to the Access Point.
  No ACK can be sent in this frame.
  Every Station must respond within a given period with an ACK (either during management or data frame) to the Beacon frame
Data frame same as 802.11a with support for ACK to Beacon
Null frame only used for ACK to Beacon with no other data

## Slide 26: MAC Association

## Slide 27: MAC Association and Polling
The Mac works by having a “listen-then-talk” process
Stations wait for permission from the Access Point to transmit information
Use of different frequencies on the PHY for uplink and downlink means that Full Duplex functionality can be achieved
Random Back-off if Station is not polled from Access Point within a given period
Station is assumed Disconnected if it does not reply within a given period to a Poll Request

## Slide 28: MAC AP failing to recognize poll response

## Slide 29: MAC Example: Error Free Communications

## Slide 30: MAC Example: Communications with Errors

## Slide 31: Unipolar-OFDM

## Slide 32: Enhanced Unipolar-OFDM

## Slide 33: eU-OFDM Spectral Efficiency

## Slide 34: eU-OFDM BER
BPSK
4-QAM
8-QAM
16-QAM

## Slide 35: eU-OFDM BER more energy efficient & improves with constellation size

## Slide 36: eU-OFDM BER with Scenario 1 CIRs

## Slide 37: eU-OFDM BER with Scenario 1 CIRs

## Slide 38: eU-OFDM BER with Scenario 1 CIRs

## Slide 39: eU-OFDM BER with Scenario 1 CIRs

## Slide 40: eU-OFDM BER with Scenario 1 CIRs

## Slide 41: eU-OFDM BER with Scenario 1 CIRs

## Slide 42: eU-OFDM BER with Scenario 1 CIRs

## Slide 43: eU-OFDM BER with Scenario 1 CIRs

## Slide 44: I-V curves for a typical Illumination Light (Lucicup 22W – used in Simulations)