## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Kookmin University Color Transmission PHY sub-proposal for ISC
Date Submitted: January 2016
Source: Yeong Min Jang, Trang Nguyen, Mohammad Arif Hossain [Kookmin University]
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: This is a PHY sub-proposal for ISC using Color Transmission. The compatibility in image sensors is supported.
Purpose: Call for Proposal Response
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-16- 0012 -01-007a
Submission

## Slide 2
Submission
Content
PHY design considerations
  Frame rate variation
  Compatible to both shutter types
  Perspective distortion and Rotation mitigation
  Color-channels interference
System designs
  Transmitter and encoding
  Image processing and Decoding
  Compatibility features
PHY format and PHY modes
Error correction
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 3
Submission
PHY design considerations
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 4
Submission
Frame rate variation
… | symbol i | symbol (i+1) | …
Symbol clock out
Camera sampling
(varying frame rate)
Majority Voting
symbol i voting
symbol (i+1) voting
Clock interval > Max{sampling interval}
Camera frame rate range | Symbol rate
> 20 fps | 5/10/15 (symbol/sec)
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 5
Submission
Compatible to shutter types
… | symbol 1 | symbol 2 | …
Symbol clock out
Global sampling type
Rolling effect
Rolling sampling type
How to mitigate rolling effect?
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 6
Submission
Perspective Distortion and Rotation
Perspective Distortion
Rotation
How to mitigate perspective distortion and rotation?
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 7
Submission
Channels Interference
Interference between color channels due to the Bayer filter of image sensor
A fixed threshold may cause error.
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 8
Submission
System Design
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 9
Submission
System Architecture
Transmitter side
Receiver side
clock information (of a data packet/symbol): The information represents the state of a symbol clocked out. The clock information is transmitted along with a symbol to help a receiver in identifying an arrival state of new symbol under presence of frame rate variation.
… | symbol i | symbol (i+1) | …
Symbol clock out
Clock information
bit = 1
Clock information
bit = 0
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 10
Submission
A design of 16x16 LEDs transmitter
Transmitter Design
Reference LEDs (4 LEDs at 4 corners):
  Transmit clock information to help a varying-frame rate receiver in performing asynchronous decoding
  To mitigate the rolling shutter effect
4 Surrounding lines (high gradient difference):
  To help a receiver in detecting and extracting LEDs in real-time
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 11
Submission
3 bits-Input | Color-Output
000 | Black
100 | Red
010 | Green
001 | Blue
110 | Yellow
101 | Magenta
011 | Cyan
111 | White
Multi-colors encoding true table
Reference LEDs | Red channel | Clock infor. bits (0 1 0 1 …) | 
Data LEDs |  | data bit “0” | data bit “1”
 | Red channel | 0 | 1
 | Greem channel | 0 | 1
 | Blue channel | 0 | 1
Encoding table for reference LEDs and data LEDs
Colors Encoding (Flicker mode)
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 12
Submission
LEDs extraction matrix using line detection under perspective distortion
LEDs extraction under Perspective Distortion and Rotation
Step 1: 4-Edges detection
  Edges are detected by using Hough transform
  The position of 4 corners and matrix positions of LEDs
Step 2: 16x16 LED-positions Matrix forming
  Input: 4-corner positions Ai(w, h)
  Output: 16x16 matrix of LED-positions
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 13
Submission
Rolling effect Detection and Cancellation
A state-Matrix of 4 reference LEDs at the sample #k:
Detect the rolling effect in an image:
- If (Mk != 0 && Mk != 1) then (the image has rolling effect)
Notice: The detection is still true under rotation!
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 14
Submission
Frame rate variation Cancellation (Asynchronous Decoding)
When at least one sample is captured on an interval of a symbol, a majority voting is applied
Clock information bit is helpful to identify the group of samples for a symbol voting.
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 15
Submission
PHY frame format
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 16
Submission
PHY frame format
Preamble and training: a symbol s and an inverse symbol
MCS ID: Modulation and Coding Scheme ID
PSDU: PHY Service Data Unit
HCS: Header-Check Sequence
Preamble and training | MCS ID | PSDU length | Reserved | HCS | PSDU
Symbols: 2 | 1 | 1 | 1 | x | Variable
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 17
Submission
symbol 1
HCS
MCS ID
PSDU length
Reserved
PSDU
symbol 2
s
Spatial-MIMO
(resolution mode 1)
spatial-MIMO
(resolution mode 2)
SHR
PHR
SHR and PHR design:
On a low resolution to ensure compatibility to different resolutions versus distance.
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 18
Submission
Preamble design:
Symbol s and are inverse forms to provide DC balance.
Preamble symbols are at low spatial-resolution among spatial-MIMO PHY modes.
Although the resolution can be increased at PSDU, the symbol rate does not change throughout the frame between preamble, header, and payload. Any symbol rate should be pre-noticed
PHY header design:
SHR and PHR are at the same resolution (lowest among spatial-MIMO PHY modes).
Although the resolution can be increased at PSDU, the symbol rate does not change throughout the frame between preamble, header, and payload. Any symbol rate should be pre-noticed
symbol s
Preamble
HCS
MCS ID
PSDU length
Reserved
PSDU
constant symbol rate
resolution mode 1
resolution mode 2
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 19
Submission
 | MCS indication | PHY modes | Data rate | Unit | Note
14 | 0000 1110 | I.11 | 2.5 | kbps | Flicker (16 x 16)
16 | 0001 0000 | I.12 | 5 |  | Flicker (16 x 16)
17 | 0001 0001 | I.13 | 7.5 |  | Flicker (16 x 16)
18 | 0001 0010 | I.14 | 40 |  | Flicker (64 x 64)
19 | 0001 0011 | I.15 | 80 |  | Flicker (64 x 64)
20 - 256 |  | reserved |  |  | 
PHY modes
Notice
Data rate is counted at 10 symbol/sec
Preamble symbols are at low spatial-resolution among spatial-MIMO PHY modes.
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 20
Submission
Error due to frame rate drops unexpectedly
  A transmitted symbol is missed on sampling when the camera frame rate drops to lower than the symbol rate unexpectedly. Line coding can be used to correct this type of error
  If this type of error happens frequently, a reduction of image resolution can achieved a higher frame rate.
Error due to interference/noise
  A electronics noise/ or noise comes from environment/ or noise comes from an incorrect threshold
  If this type of error can be mitigated by using spatial coding as following slide.
PHY Error Corrections
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 21
Submission
Spatial Error Correction Coding to reduce BER
(TBD)
doc.: IEEE 802.15-16- 0012 -01-007a
Example: 15x15 LEDs transmitter
  A fixed threshold
  => 15x15 = 225 bits per frame
  Use 3x3 spatial blocks to define 2x2 bits
  10x10 = 100 bits per frame
Advantages:
  A reference point (a middle point) provides a reliable intensity threshold for the whole block to reduce error
  A spatial code additionally reduces error 2nd time
3x3 LEDs block with error correction
For a high-MIMO transmitter, what kind of error correction is needed?
Reference point

## Slide 22
Submission
PHY Summary
The system design supports those functionalities:
  Frame rate variation
  Compatible to both shutter types
  Perspective distortion and Rotation mitigation
  Color-channels interference
The PHY design modes
  PHY modes for color transmission C-CSK (2.5kbps - 80kbps)
  Compatibility support in SHR and PHR design is highly considered. The lowest data mode among available PHY modes is used for both SHR and PHR.
    Low-resolution is used for SHR and PHR frames in spatial scheme.
    The DPSU can use the same PHY mode or upgrade to higher PHY mode among available PHY modes. The notice of DPSU PHY mode is MCS ID frame.
Two types of error correction:
  Line coding
  Spatial coding
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 23
Submission
Appendix: QR-ISC Code
(Integrating dynamic data into color-QR code)
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 24
Submission
Integration of ISC into QR code
Block Diagram of QR-ISC Tag in Transmitter side
QR-ISC Tag is color modulation in Image Sensor Communications (ISC) integrated into QR code. The ISC uses three channels of Red, Green and Blue to transmit data, along with that is the asynchronous symbols to support varying-frame-rate camera receivers.
We borrow the format and error correction from QR code standard.
How data is transmitted was already presented in our PHY above.
doc.: IEEE 802.15-16- 0012 -01-007a

## Slide 25
Submission
Considerations
Block Diagram of QR-ISC Tag in Transmitter side
There are some consideration in integrating dynamic data into color QR code:
The size of QR code
The symbol rate of transmission
The decoding does not require to be real-time; however the processing of an image should finish before a new image comes to sequence.
doc.: IEEE 802.15-16- 0012 -01-007a