## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Kookmin PHY sub-proposal for ISC using Temporal Scheme (C-OOK)
Date Submitted: January 2016
Source: Yeong Min Jang, Trang Nguyen [Kookmin University]
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: This is a PHY sub-proposal of ISC using OOK based modulation scheme for rolling shutter camera receiver. Being compatible to image sensors, it is called Compatible-OOK scheme (C-OOK).
Purpose: Call for Proposal Response
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-16- 0013 -00-007a
Submission

## Slide 2
Submission
Content
PHY design considerations
  Frame rate variation
  Different sampling rates
  Different rolling exposure time
System designs
  System architecture
  Frequency band in use
  Data packet structure
  Asynchronous Decoding
  Packet recovery
PHY format and PHY modes
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 3
Submission
PHY design considerations
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 4
Submission
Frame rate variation
… | symbol i | symbol (i+1) | …
Symbol clock out
Rolling camera sampling
(at high frame rate)
Packet Fusion (Recovery)
symbol i voting
symbol (i+1) voting
Clock interval ≥ Max{sampling interval}
Rolling camera sampling
(at low frame rate)
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 5
Submission
Different sampling rates
rolling exposure
Sampling
interval
Source: http://www.onsemi.com/pub_link/Collateral/NOIV1SN1300AD.PDF
Rolling shutter Operation
The sampling rate of a Smartphone rolling image sensor is different from the other’s, and typically larger than 15 kHz.
The light modulation and demodulation of a frequency will need to be compatible to different cameras those have different sampling rates.
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 6
Submission
Different rolling exposures
… | symbol i | symbol (i+1) | …
Symbol clock out
Data Fusion
symbol i
Rolling camera sampling
(at low frame rate)
rolling exposure time
rolling exposure time
rolling exposure time
symbol (i+1)
The rolling exposure time decides how much the amount of data is recorded per a rolling image.
Under presence of frame rate variation, different rolling exposure time is challenging.
losing information
losing information
Packet Recovery
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 7
Submission
System Design
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 8
Submission
System Architecture
Transmitter side
Receiver side
clock information (of a data packet): In this scheme, asynchronous bits (Ab) are in form of clock information.
… | data packet i | …
Symbol clock out
Clock information
Ab = 1
Clock information
Ab= 0
Merger
Ab=1
data packet i
Ab=1
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 9
Submission
Modulation frequency
The modulation frequency is constant on a frame.
The upper threshold of frequency band in use is less than the shutter speed of camera (Currently, Smartphone has a shutter speed of 8kHz).
The practical response of a long-exposure-camera (A webcam)
Frequency | Compatibility
2 kHz | Webcams, Smartphone cameras (Auto-exposure is OFF)
4 kHz | Smartphone cameras (Auto-exposure is OFF)
In-band
Camera
shutter speed
Eye cut-off
Camera cut-off
~8 kHz
~200 Hz
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 10
Submission
Data packet Structure
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 11
Submission
SF
Ab
Ab
Data packet i
DS i (1)
DS i (2)
DS i (N)
packet (i-1)
packet i
packet (i+1)
DS: Data Sub-Packet; SF: Start Packet-Frame Symbol; Ab: Asynchronous bit(s)
A packet is multiple times repeat of one data symbol.
A complete DS has a very-low-header symbol (SF), two similar asynchronous bits (which is a form of the clock information)
Data packet structure
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 12
Submission
Data packet structure: The purpose of repetition
DS i (1)
DS i (2)
DS i (N)
packet (i-1)
packet i
packet (i+1)
Problem of losing repeated ones
(is mitigated by using our frame structure)
recorded a complete DS
Repetition is to avoid losing any data when camera makes sampling discretely.
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 13
Submission
Data packet structure: The SF symbol
SF symbol | Ab | Data | Ab
011100 | bit 1/0 | Manchester coding | bit 1/0
0011111000 |  | 4B6B coding | 
000011111111100000 |  | 8B10B coding | 
SF #n
Backward decoding
Forward decoding
A SF symbol is detectable. When the frame rate is varying irregularly, the position of the SF symbol on the rolling image is also varying. The detection of SF becomes indispensable for the decoding (forward and backward parts) and recovering data.
The length of SF is different for each RLL code (in order to be low-overhead and detectable).
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 14
Submission
Asynchronous Decoding
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 15
Submission
Decoding Procedure
SF detection: to detect the position of SF on a rolling image.
Asynchronous decoding: From the position of SF, two tasks are performed
  Forward decoding: Decode the forward part of the image
  Backward decoding: Decode the backward part of the image
Packet recovery: To recover a complete data packet from the incomplete parts decoded, forward and backward part of one (two) data packet(s):
  Data fusion: to group parts (forward and backward parts) those belong to one packet. This is indispensable because a camera has a rolling exposure time different from the other camera’s and not equal to DS interval.
  Majority voting: to get a complete packet from several discrete-parts of the packet.
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 16
Submission
SF
SF
SF
Asynchronous Decoding: Rolling exposure time >> (DS interval)
Oversampled Asynchronous decoding
This happens when the DS interval is short to be compatible to different rolling exposure times
The majority voting is applied between several images or within an image (using asynchronous bits) to enhance BER.
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 17
Submission
SF
1
1
4B6B-Data (Forward)
4B6B-Data (Backward)
Data (Forward)
Data (Backward)
Data Fusion
Packet recovery
Asynchronous Decoding: Rolling exposure time ~ (DS interval)
Forward decoding and Backward decoding
When the rolling exposure time is almost equal to DS interval, forward and backward are both used to get 100% information of an image.
The fusion of forward part and backward part (of a data packet) is performed to output a complete data packet.
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 18
Submission
Packet Recovery
Packet 1: Ab(s)=1
Packet #2
Packet #1
SF
Packet 2: Ab(s)=0
Packet 3: Ab(s)=1
Ab=1
Inter-frame fusion
intra-frame fusion
Packet #1
Packet #2
Two cases may happen at different sampling time:
Case 1- Inter-frame data fusion: Fusing two sub-parts of a packet at two different images into a complete packet.
Case 2- Intra-frame data fusion: Recovering a complete packet from an image.
Ab=1
Ab=0
Ab=0
Ab=1
Ab=0
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 19
Submission
PHY frame format
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 20
Submission
PHY Frame Format
Preamble and training | PHY header | HCS | PSDU
SHR | PHR |  | PHY payload
SF
Ab(1)
Ab(2)
Data packet i
DS i (1)
DS i (2)
DS i (N)
packet (i-1)
packet i
packet (i+1)
Data rate related (TBD)
Packet rate : 5/10/15 (packet/sec)
DS rate : 60/120 (DS/sec)
CM-FSK
doc.: IEEE 802.15-16- 0013 -00-007a

## Slide 21
Submission
 | MCS indication | PHY modes | Data rate | Unit
7 | 0000 0110 | I.7 | 0.084 | kbps
8 | 0000 0111 | I.8 | 0.17 | 
9 | 0000 1000 | I.9 | 0.22 | 
10 | 0000 1001 | I.10 | 0.44 | 
11 | 0000 1010 | I.11 | 0.53 | 
Medium-rate PHY I modes
 |  |  |  |  |  |  | Data rate | Compatibility Support | 
 |  | Modulation | Coding | Optical Clock rate | Symbol rate | DS rate | (e.g. 10 sym/s) | Varying frame rates | Shutter speeds/ Sampling rates
7 | Medium PHY I (kbps) | OOK based | Manchester | 2 kHz | 5/ 10/ 15 | 120 | 84 bps | Y | Y
8 |  | OOK based | Manchester | 2 kHz | 5/ 10/ 15 | 60 | 0.17 kbps | Y | Y
9 |  | OOK based | 4B6B | 2 kHz | 5/ 10/ 15 | 60 | 0.22 kbps | Y | Y
10 |  | OOK based | 4B6B | 4 kHz | 5/ 10/ 15 | 60 | 0.44 kbps | Y | Y
11 |  | OOK based | 8B10B | 4 kHz | 5/ 10/ 15 | 60 | 0.53 kbps | Y | Y
Detail parameters in medium-rate PHY I modes (using C-OOK)
doc.: IEEE 802.15-16- 0013 -00-007a