## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Kookmin University PHY sub-proposal for ISC using a Compatible M-FSK Scheme (CM-FSK)
Date Submitted: January 2016
Source: Yeong Min Jang, Trang Nguyen, Hong Chang Hyun [Kookmin University]
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: This is a PHY sub-proposal using M-FSK based Modulation Scheme. Being compatible to rolling shutter image sensors, it is called Compatible M-FSK (CM-FSK).
Purpose: Call for Proposal Response
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-16- 0014 -01-007a
Submission

## Slide 2
Submission
Content
PHY design considerations
  Frame rate variation
  Different sampling rates and shutter speeds
System designs
  System architecture
  Frequency band and frequency separation
  Data packet structure
  Asynchronous Decoding
PHY format and PHY modes
Appendix 1: Indoor hybrid Compatible M-FSK/N-PSK system
Appendix 2: Seaside communications using CM-FSK
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 3
Submission
PHY design considerations
for Compatible M-FSK (CM-FSK)
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 4
Submission
Compatibility to varying-frame-rates
… | symbol i | symbol (i+1) | …
Symbol clock out
Rolling camera sampling
Transform
frequency
symbol i
frequency
symbol i
frequency
symbol i/(i+1)
frequency
symbol (i+1)
frequency
symbol (i+1)
symbol i voting
symbol (i+1) voting
Majority voting
How to transmit the clock information along with the symbol?
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 5
Submission
Different sampling rates/shutter speeds
The frequency band in use is upper limited by shutter speed of camera. Lower shutter speed narrows the available band for communications
Sampling rate (rolling sampling rate) is also a matter to utilize the usage of frequency band efficiently. E.g. the sampling rate defines the minimum value of frequency separation.
In-band
Camera
shutter speed
Eye cut-off
Camera cut-off
~8 kHz
~200 Hz
In-band
lower
shutter speed
Eye cut-off
Camera cut-off
~200 Hz
Bandwidth =?
(shutter speed)
Frequency separation =?
(sampling rate)
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 6
Submission
CM-FSK for ISC
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 7
Submission
System Architecture
Transmitter side
Receiver side
clock information (of a data packet): This scheme is similar to the C-OOK scheme in which asynchronous bits (Ab) represent the form of clock information. However, the data packet with clock information (called a symbol) is encoded using M-FSK technique.
… | data packet i | …
Symbol clock
Clock information
Ab = 1
Clock information
Ab= 0
Merger
Ab=1
data packet i
M-FSK Encoder
a frequency symbol i
a data packet with the clock information
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 8
Submission
CM-FSK Modulation frequency band
Frequency band | Compatibility
[200Hz ; ~2 kHz] | Webcams, Smartphone cameras (Auto-exposure is OFF)
[200Hz ; ~4 kHz] | Smartphone cameras (Auto-exposure is OFF)
In-band
Camera
shutter speed
Eye cut-off
Camera cut-off
~8 kHz
~200 Hz
The frequency band:
B = 2kHz to be compatible to low shutter speed cameras
B = 4kHz (or higher, up to < 8kHz) to be compatible to most of smartphone cameras.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 9
Submission
CM-FSK frequency separation
In our specific experiment
  Center frequency values:
  Frequency separation: ∆(FFT peak) ≥ 1 <=> ∆(frequency) ≥ 32.192 Hz
Selected image resolution: 640x480
Chart: 
| 0 | 100 | 200 | 500 | 1000 | 2000 | 4000
FFT peak | 0 | 3 | 6 | 16 | 32 | 63 | 123
Spectrum peak and the corresponding frequency measurement
The peak value of the FFT spectrum is linear proportional to the modulation frequency of light
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 10
Submission
Frequency separation
FDM spectrum with frequency separation = 96.576 Hz
FDM spectrum with frequency separation = 32.192 Hz
Max (number of channel)= 41 [channels]
Max (number of channel= 124 [channels]
∆(FFT peak) =3
∆(FFT peak) =1
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 11
Submission
Data packet Structure and Encoding
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 12
Submission
Ab
Data packet i
DS i (1)
DS i (2)
DS i (N)
frequency symbol (i-1)
frequency symbol i
frequency symbol (i+1)
DS: Data Sub-Packet; SF: Start Packet-Frame Symbol; Ab: Asynchronous bit(s)
Time Domain
Information of a symbol before encoding
Data packet structure
A symbol is N times repeated in transmission
An asynchronous bit (represents the clock information of the data packet) is along with the packet in transmission.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 13
Submission
fSF
f'SF
best compatible band
. . .
32 frequency
. . .
extended band
Camera
limit
~8 kHz
SHR and PHR design:
On the lowest-band among the CM-FSK PHY modes to ensure compatibility with low sampling-rate cameras.
Relationship between fSF and f’SF is for training
  fSF is chosen as lowest frequency on the available bandwidth, e.g. 200Hz, to be easily detected.
  f’SF = fSF + 33x ∆f to train different cameras which have different sampling rates.
Encoding PHY modes (SHR and PHR)
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 14
Submission
Encoding PHY modes
Data frequency: fi = fSF + i.∆f (i=1; 2;…; 32)
Preamble frequency: f’SF = fSF + 33.∆f
PHY modes | Number of frequency | Data rate | Unit
I.2/ I.3 | 32 | 50 | bps
I.4/ I..5 | 64 | 60 | 
Reserved | 128 | 70 | 
HCS
MCS ID
PSDU length
Reserved
SHR
symbols:
2
2
C32-FSK
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 15
Submission
Baud symbol | Frequency
fSF | fo
00000 | f1
00001 | f2
. . . | 
11110 | f31
11111 | f32
f'SF | f33
C32-FSK encoding table
Encoding table (C32-FSK)
bits: 1 | 4
Ab | Data packet
Symbol structure
∆f = Hz (~ 100Hz)
B = [200Hz; 3400Hz]
Data frequency: fi = fSF + i.∆f (i=1; 2;…; 32)
Preamble frequency: f’SF = fSF + 33.∆f
Symbol rate: 5/10/15 (symbol/sec)
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 16
Submission
Baud symbol | Frequency
fSF | fo
000000 | f1
000001 | f2
. . . | 
101110 | f31
101111 | f32
f'SF | f33
010000 | f34
010001 | f35
. . . | 
111110 | f64
111111 | f65
C64-FSK encoding table
Encoding table (C64-FSK)
bits: 1 | 5
Ab | Data packet
Symbol structure
∆f = Hz (~ 50Hz)
B = [200Hz; 3500Hz]
Data frequency: fi = fSF + i.∆f (i=1; 2;…; 32; 34;35; …; 65)
Preamble frequency: f’SF = fSF + 33.∆f
Symbol rate: 5/10/15 (symbol/sec)
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 17
Submission
Asynchronous Decoding
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 18
Submission
Symbol out
Ab=1
Ab=0
Ab=1
Image frame sequence
1-0100
Decoded symbol
along with Ab(s)
1-0100
0-0011
0-0001
0-0011
1-1110
1-1110
0100
0011
1110
Ab =1
Ab=0
Ab=1
Group to vote
Majority voting result
Asynchronous Decoding example
CM-FSK solves the communications performance, and the asynchronous bits solve the frame rate variation.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 19
Submission
PHY frame format
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 20
Submission
SHR symbol 1
HCS
MCS ID
PSDU length
Reserved
PSDU
SHR symbol 2
fSF
CM-FSK scheme (on the compatible-band)
CM-FSK (extended band)
f’SF
SHR
PHR
Extended band
Camera
Physical
limit
Best Compatible Band
Camera
Physical
limit
SHR and PHR design:
This part should have compatibility to almost of rolling shutter cameras
  CM-FSK is chosen because of its advantages of lower error rate compared to OOK:
    Hence CM-FSK is more reliable in detection and synchronization
    The frequency band for encoding SHR and PHR is the lowest band among proposed frequency bands to ensure the compatibility to any rolling shutter camera.
  The PSDU (can keep CM-FSK scheme or switch to C-OOK scheme) is performed on extended band to achieve higher link rate in specific situations.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 21
Submission
PHY header design:
  All frequencies used for PHY header are on low- band of the available bandwidth (e.g. 200Hz – 3.5kHz). This is to be compatible to low sampling rate cameras.
  SHR and PHR are allocated in a common band (low-band)
  The length for each frequency symbol is constant throughout the frame between preamble, header, and payload
  PSDU can be allocated to the extended band.
MCS indication | PHY modes | Data rate | Unit
0000 0001 | I.2 (C32-FSK) | 50 | bps
0000 0010 | I.3 (C32-FSK/2-PSK) | 60 | 
0000 0011 | I.4 (C64-FSK/2-PSK) | 70 | 
0000 0100 | I.5(C32-FSK/4-PSK) | 80 | 
CM-FSK PHY modes
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 22
Submission
Appendix 1:
Indoor hybrid Compatible M-FSK/M-PSK system
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 23
Submission
Camera sequentially exposes light row by row. To get the maximum length of a LED on the image, LEDs are hang up along the walking way.
1
2
3
Camera FOV
Walking road
Top-floor LEDs
Walking direction
4
Walking road
5
1
2
3
4
5
CM-FSK LEDs lighting
Camera’s RoI
In general way, multiple LEDs are grouped together in communications. This is to provide the brightness for indoor when LEDs seems to be dimmed at 50%.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 24
Submission
FOV
d
L
H
Walking Speed = w (m/s)
LED 1
LED 2
LED 3
- Condition of LEDs separation in user moving environment: L ≤ 2H.tg(FOV/2)
- Longer d is better for communications, but not power consumption.
Example: H = 2m; FOV = 680 (Samsung S5); d = 1.2m (equal size of fluorescent lamp); L = 2.7m.
Walking speed is limited by connection switching algorithm between LEDs.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 25
Submission
Advantages of M-FSK:
  Support for multiple transmitters (LEDs). Frequency allocation is based on M-FSK to share the bandwidth to all LEDs. The M-FSK technique is to avoid interference efficiently.
  Great support for rolling shutter receivers. The detection of frequency is much easier with rolling effect.
Additional advantage of N-PSK:
  The N-PSK is additionally used to achieve higher data rate than just M-FSK. The higher link rate is helpful when a part of link rate must be shared for mitigating frame rate variation (by transmitting the asynchronous bits instead of data).
  Additionally support for global shutter receivers (only 2-PSK, optional).
Hybrid Compatible M-FSK/N-PSK: Benefits
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 26
Submission
Architecture #1 of LEDs-group transmitter employing the hybrid 2-PSK /CM-FSK modulation scheme.
Reference_Phase LED
Data_Phase LED
Hybrid Compatible M-FSK/2-PSK
LED 1 and LED 2 together transmit the clock information of data packets through phase (2-PSK technique). The phase difference between LEDs decide the asynchronous bit (bit 1 if two LEDs are same phase; and bit 0 if phases are inverse). This is to solve the frame rate variation.
The data packets are transmitted through M-FSK, allowing log2M bits data link rate per symbol.
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 27
Submission
2-PSK Modulation
Architecture #2 of LEDs-group transmitter employing the hybrid 2-PSK /M-FSK modulation scheme.
In N-PSK scheme, among three LEDs one is for transmitting a phase reference and the other two are for data phases. It means 2 bits are transmitted through 2-PSK.
The M-FSK still takes whole advantage of bandwidth without any interference to N-PSK transmission.
Hybrid Compatible M-FSK/2-PSK
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 28
Submission
 | Modulation Scheme and Proposed System | Data rate
1 | 2-PSK and M-FSK combination: (groups of 2-LED tubes) | Rbit = (K/2) x logM(#_frequency) x (symbol rate)
2 | 2-PSK and M-FSK combination: (groups of k-LED tubes) | Rbit = (K/k) x logM(#_frequency) x (symbol rate)
3 | 4-PSK and M-FSK combination: (groups of 4-LED tubes) | Rbit = 6 x (K/4) x logM(#_frequency) x (symbol rate)
4 | N-PSK and M-FSK combination: (groups of k-LED tubes) | Rbit = (k-1)log2N x (K/k) x logM(#_frequency) x (symbol rate)
Data rate of hybrid system
where K: is the number of LED tubes
#_frequency: denotes the number of frequencies used for communications in M-FSK
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 29
Submission
Appendix 2:
Seaside communications using CM-FSK
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 30
Submission
The purpose of inter-symbol guard time:
A guard time to mitigate frame rate variation, and
Also is a period for low-rate PD communications. PD communications is allocated in high band that is invisible to camera (>10 kHz).
Prototype
symbol 3
symbol 1
symbol 2
Prototype 1: Continuous symbols transmission along with the clock information (asynchronous bits)
bits: 1 | 4/5
Ab | Data packet
Symbol structure
Prototype 2: Burst mode (with inter-symbol guard time for low-rate PD communications)
The communications for this prototype is exactly same as mentioned.
Purpose of PD communications here:
Additional information broadcasting (more data)
Localization beacon. ISC provides direction of the lighthouse, while PD communication determines the distance from the lighthouse.
symbol 3
symbol 1
symbol 2
Inter-symbol
guard time
Inter-symbol
guard time
x
Data packet
Symbol structure
doc.: IEEE 802.15-16- 0014 -01-007a

## Slide 31
Submission
The beam output from Fresnel lens into camera will cover the entire of image sensor instead of focusing into an focal point.
Non-Imaging based ISC: An additional optical module
In order to collect light energy and distribute uniformly into 2D image sensor, an additional optical lens module is used in front of the camera lens.
A type of Fresnel Lens
(to collect light energy)
Lighthouse LED
Image Sensor
Fresnel Lens
Incoming beam
Rolling shutter camera
doc.: IEEE 802.15-16- 0014 -01-007a