## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Kookmin University PHY sub-proposal for ISC using Dimmable Spatial M-PSK (DSM-PSK)
Date Submitted: January 2016
Source: Yeong Min Jang, Trang Nguyen [Kookmin University]
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: This is a PHY sub-proposal for ISC using Spatial M-PSK. The dimming and compatibility are supported in the scheme.
Purpose: Call for Proposal Response
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-16- 0015 -01-007a
Submission

## Slide 2
Submission
Content
PHY design considerations
Technologies Detail
  Spatial 2-PSK (S2-PSK)
  Spatial M-PSK (S8-PSK)
  Dimmable Spatial M-PSK (DS8-PSK)
PHY modes and PHY frame format
Appendix: System designs
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 3
Submission
spatial phase (denoted by S_Phase): the phase of a discrete waveform which is built from the states of LEDs on a group those captured and decoded from a global shutter image.
global phase shift: the phase value that all LEDs in a data group together are shifted to transmit data.
data group: A group of data LEDs those operate together to transmit a data symbol
reference group: A group of reference LEDs those operate together to transmit a reference signal
S_Phase shift: the abstraction value between the spatial phase values of data group and of the reference group.
long exposure bad-sampling: an image sampling that captures an unclear sate of LED (neither ON nor OFF) due to long exposure time.
SM-PSK (e.g. S2-PSK; S8-PSK; etc.): Spatial Multiple-Phase Shift Keying
DSM-PSK (e.g. DS8-PSK): Dimmable SM-PSK
Definitions
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 4
Submission
PHY design considerations
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 5
Submission
Flicker mitigation
  The flicker-free band is used.
Frame rate variation Mitigation
  The variation is irregular, but the range > 20 fps
Spatial MIMO to target high link rate for a global shutter receiver
  Link rate goal is kbps - Mbps
Dimming support
  Dimming is supported in steps of <20%
Error correction
  Cancel error due to long exposure time
Considerations for PHY design
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 6
Submission
Detail of technologies
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 7
Submission
Spatial 2-PSK
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 8
Submission
Spatial 2-PSK (S2-PSK)
Bit definition (Encoding):
  Same frequency and amplitude
  Inverse phase
  (bit 1 phase = 0; bit 0 phase = 180
Decoding
Decoding principle (applied for a random sampling):
  The state of bit 1 is always equal to the state of the reference signal (x1 = xr)
  The state of bit 0 is always inverse to the state of the reference signal (x0 = )
Captured reference state
xr = ON
Captured bit 1 state
x1 = xr
Captured bit 0 state
x0 =
A random sampling of global receiver
Reference signal
Reference LED:
Phase = 0
Data LED:
Phase = 0  bit 1
Phase = 180 bit 0
2 LEDs transmitter
Compatibility support
  The decoding result is non-affected by the state of the LEDs but by the comparison.
  The principle is compatible to different frame rate variation.
x0
x1
xr
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 9
Submission
Modulation considered
  Modulation frequency is less than the global shutter speed of the camera (e.g. 1 kHz)
  The long exposure causes error (BER)
Bad sampling due to long exposure time
The appearance of bad-sampling
Note
  BER is proportional to the value of exposure time
  (TBD) FEC can be used to correct error caused by the long exposure
Long exposure bad-sampling in S2-PSK
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 10
Submission
Compatible Spatial M-PSK
(SM-PSK)
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 11
Submission
Advantage of spatial M-PSK
Advantages of spatial M-PSK compared to spatial 2-PSK
  At the moment of capturing, among LEDs in a group there is only one or non bad-sampling happens because those LEDs are phase-shifted. => Easy to detect and mitigate error.
. . .
.
.
.
.
.
.
. . .
1
2
3
Spatial 8-PSK
Transmitter
(1) Group of 4-LEDs for reference Phase transmission
(2): Group of 4-LEDs for Data transmission
(3): A LED.
  - Green color represents data LED.
  - Red color represents reference LED.
Principles
  A group of LEDs together define a spatial phase (e.g. 4 LEDs per group as illustrated in the figure)
  LEDs in a group are phases-shifted in encoding procedure to define a spatial phase
Green slots : good-sampling (clear state of LED)
Pink slots : may cause bad-sampling (unclear state of LED)
A random sampling
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 12
Submission
Operation of Compatible Spatial 8-PSK (S8-PSK)
A discrete waveform (4-States) Input | Spatial Phase (S_Phase) Output
1000 | 1
1100 | 2
1110 | 3
1111 | 4
0111 | 5
0011 | 6
0001 | 7
0000 | 8
LED # 1
LED #2
LED #3
LED# 4
Delay T/8
Delay 2T/8
Delay 3T/8
1 2 3 4 5 6 7 8 1 2
Phase Shift
Delay 0
Duty Circle T
Camera sampling
A group of reference LEDs
Spatial-Phase Definition Table
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 13
Submission
LED # 1
LED #2
LED #3
LED# 4
Duty Circle
A group of data LEDs: Global Phase Shift = 0
S_Phase Shift Value (compared to the spatial phase of the reference group): S_Phase_Shift = 0
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 14
Submission
LED # 1
LED #2
LED #3
LED# 4
2π/8
Duty Circle
A group of data LEDs: Global Phase Shift = 2π/8
S_Phase Shift Value (compared to the spatial phase of the reference group): S_Phase_Shift = 1
Global Phase Shift
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 15
Submission
LED # 1
LED #2
LED #3
LED# 4
Duty Circle
2 × 2π/8
A group of data LEDs: Global Phase Shift = 2 × 2π/8
S_Phase Shift Value (compared to the spatial phase of the reference group): S_Phase_Shift = 2
Global Phase Shift
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 16
Submission
LED # 1
LED #2
LED #3
LED# 4
Duty Circle
3 × 2π/8
A group of data LEDs: Global Phase Shift = 3 × 2π/8
S_Phase Shift Value (compared to the spatial phase of the reference group): S_Phase_Shift = 3
Global Phase Shift
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 17
Submission
LED # 1
LED #2
LED #3
LED# 4
Duty Circle
4 × 2π/8
A group of data LEDs: Global Phase Shift = 4 × 2π/8
S_Phase Shift Value (compared to the spatial phase of the reference group): S_Phase_Shift = 4
Global Phase Shift
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 18
Submission
LED # 1
LED #2
LED #3
LED# 4
Duty Circle
7 × 2π/8
A group of data LEDs: Global Phase Shift = 7 × 2π/8
S_Phase Shift Value (compared to the spatial phase of the reference group): S_Phase_Shift = 7
Global Phase Shift
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 19
Submission
3-bits Input | Global Phase Shift Output
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
A discrete waveform (4-States) Input | Spatial Phase (S_Phase) Output
1000 | 1
1100 | 2
1110 | 3
1111 | 4
0111 | 5
0011 | 6
0001 | 7
0000 | 8
(S_Phase_Shift) Input | 3-bits Output
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
Encoding Table
Decoding Tables
Encoding/Decoding
States-to-Phase Table
Phase-to-Bits Table
S_Phase Shift = S_Phase(data) – S_Phase(reference)
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 20
Submission
Decoding Example
1 1 1 0
0 0 1 1
Reference group
Data group
S_Phase = 3
S_Phase = 6
S_Phase_Shift = 3
0 1 0
Camera sampling
Data (3 bits)
Build discrete waveform
Spatial Phase detecting
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 21
Submission
Long exposure Bad-sampling Mitigation
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 22
Submission
Time axis
LED # 1
LED #2
LED #3
LED# 4
0
1
1
Capturing moment
1 2 3 4 5 6 7 8 1 2
Where x state is the unclear state of LED.
Spatial Phase Re-Definition in Bad-sampling Image
doc.: IEEE 802.15-16- 0015 -01-007a
A discrete waveform (4-States) Input | Spatial Phase (S_Phase) Output
1x00 | 1
11x0 | 2
111x | 3
x111 | 4
0x11 | 5
00x1 | 6
000x | 7
x000 | 8
States-to-Phase Table (2)

## Slide 23
Submission
1 1 x 0
0 x 1 1
Reference group
Data group
S_Phase = 2
S_Phase = 5
S_Phase_Shift = 3
0 1 0
bad sampling
Data (3 bits)
Build discrete waveform
Spatial Phase detecting
(Re-defined table)
Decoding Example with bad-sampling image
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 24
Submission
Dimmable Spatial M-PSK (DSM-PSK)
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 25
Submission
1
2
3
Example of 8x8 Transmitter
for DS8-PSK
Dimmable Spatial 8-PSK (DS8-PSK)
Principles
  8 LEDs per group together define a spatial-phase (with dimming supported)
(1) Group of 8-LEDs for reference Phase transmission
(2): Group of 8-LEDs for Data transmission
(3): Single LED.
  - Green color represents data LED.
  - Red color represents reference LED.
 | S8-PSK | DS8-PSK
Data rate | 4 LEDs per group together define a S_Phase Data rate = 3×K/4 (bits/symbol) | 8 LEDs per group together define a S_Phase Data rate = 3×K/8 (bits/symbol)
Dimming | No dimming supported. AB% = 50% constant | Dimming is supported in steps of 1/8 (12.5%)
where K is the number of LEDs in a transmitter
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 26
Submission
Operation of DS8-PSK
To due dimming, there are 7 tables for every single dimming level (1/8; 2/8; 3/8; 4/8; 5/8; 6/8 ; 7/8).
Similar to S8-PSK
  A reference group
  Global Phase Shift = 0
  A data group
  Global Phase Shift = 0/1/…/7
Time axis
Dimmed Signal of LED 1
Dimmed Signal of LED 2
Dimmed Signal of LED 3
Dimmed Signal of LED 8
Delay T/8
Delay 2T/8
Delay 7T/8
Camera sampling
Duty Circle T
Delay 0
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 27
Submission
Encoding/Decoding Tables
3-bits Input | Global Phase Shift Output
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Encoding Table
S_Phase_Shift Input | 3-bits Output
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
Decoding Tables
(Phase-to-Bits Table)
S_Phase_Shift = S_Phase(data) - S_Phase(reference)
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 28
Submission
8-States Input |  | S_Phase Output
1000 | 0000 | 1
0100 | 0000 | 2
0010 | 0000 | 3
0001 | 0000 | 4
0000 | 1000 | 5
0000 | 0100 | 6
0000 | 0010 | 7
0000 | 0001 | 8
8-States Input |  | S_Phase Output
1000 | 0001 | 1
1100 | 0000 | 2
0110 | 0000 | 3
0011 | 0000 | 4
0001 | 1000 | 5
0000 | 1100 | 6
0000 | 0110 | 7
0000 | 0011 | 8
8-States Input |  | S_Phase Output
1000 | 0011 | 1
1100 | 0001 | 2
1110 | 0000 | 3
0111 | 0000 | 4
0011 | 1000 | 5
0001 | 1100 | 6
0000 | 1110 | 7
0000 | 0111 | 8
8-States Input |  | S_Phase Output
1000 | 0111 | 1
1100 | 0011 | 2
1110 | 0001 | 3
1111 | 0000 | 4
0111 | 1000 | 5
0011 | 1100 | 6
0001 | 1110 | 7
0000 | 1111 | 8
8-States Input |  | S_Phase Output
1000 | 1111 | 1
1100 | 0111 | 2
1110 | 0011 | 3
1111 | 0001 | 4
1111 | 1000 | 5
0111 | 1100 | 6
0011 | 1110 | 7
0001 | 1111 | 8
8-States Input |  | S_Phase Output
1001 | 1111 | 1
1100 | 1111 | 2
1110 | 0111 | 3
1111 | 0011 | 4
1111 | 1001 | 5
1111 | 1100 | 6
0111 | 1110 | 7
0011 | 1111 | 8
8-States Input |  | S_Phase Output
1011 | 1111 | 1
1101 | 1111 | 2
1110 | 1111 | 3
1111 | 0111 | 4
1111 | 1011 | 5
1111 | 1101 | 6
1111 | 1110 | 7
0111 | 1111 | 8
1/8 Dimming
2/8 Dimming
3/8 Dimming
4/8 Dimming
5/8 Dimming
6/8 Dimming
7/8 Dimming
S_Phase Decoding Tables in DS8-PSK
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 29
Submission
Decoding Procedure in DS8-PSK
Step 1: Choose the proper S_Phase decoding Table (among 7 tables) according to the dimming level:
  Dimming level
  Select the proper S_Phase decoding table
Step 2: Map with the selected decoding table to find S_Phase(data); S_Phase(reference) and S_Phase_Shift
  Input: The discrete waveforms of a 8-LEDs groups (a reference group and data groups)
  Output: Spatial Phases
  S_Phase(reference)
  S_Phase(data)
  S_Phase_Shift = S_Phase(data) - S_Phase(reference)
Step 3: Data decoding using Phase-to-Bits table
Input: S_Phase_Shift
Output: 3 data bits
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 30
Submission
PHY modes
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 31
Submission
 |  |  |  | Data rate | Compatibility Support |  | 
PHY modes ID | Modulation | Symbol Rate (/sec) |  | (e.g. 10 symbol/s) | Varying frame rates | Long-exposure mitigation | shutter type
16 | S2-PSK | 5/ 10/ 15 |  | 2.5 kbps | Y | Y | Global
17 | S8-PSK | 5/ 10/ 15 |  | 1.92 kbps | Y | Y | Global
18 | DS8-PSK | 5/ 10/ 15 |  | 0.96 kbps | Y | Y | Global
19 | S2-PSK | 5/ 10/ 15 |  | 40 kbps | Y | Y | Global
20 | S8-PSK | 5/ 10/ 15 |  | 30.7 kbps | Y | Y | Global
21 | DS8-PSK | 5/ 10/ 15 |  | 15.3 kbps | Y | Y | Global
PHY modes for SM-PSK and DSM-PSK
 | S2-PSK | S8-PSK | DS8-PSK
Data rate [bps] | Data rate = (bit/symbol) x (symbol rate) = (K) x 10 | Data rate = (bit/symbol) x (symbol rate) = (3×K/4) x 10 | Data rate = (bit/symbol) x (symbol rate) = (3×K/8) x 10
Advantages | - Highest data rate | - Support for decoding even under presence of bad-sampling due to long-exposure time | - Dimming supported in steps of 12.5%
where K is the number of data LEDs
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 32
Submission
PHY frame structure
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 33
Submission
SHR and PHR design
Preamble symbols are inverse forms in order to
  Help a receiver in identifying how many LEDs available on the transmitter.
  Help a receiver in identifying how many LEDs-groups available
Preamble symbols are at lowest spatial-resolution among available spatial PHY modes.
Although the resolution can be increased at PSDU, the symbol rate does not change throughout the frame between preamble, header, and payload. Any symbol rate should be pre-noticed
symbol s
Preamble symbols
HCS
MCS ID
PSDU length
Reserved
PSDU
constant symbol rate
resolution mode 1
resolution mode 2
PHY SHR and PHR design
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 34
Submission
symbol s
Preamble
PHY SHR and PHR design: S2-PSK
Symbol s and
In case of S2-PSK, the white dot represents a single LED is ON while the grey dot represents a single LED is OFF.
Preamble symbols are to extract single LEDs
LED on
LED off
symbol s
Preamble: 4 symbols
s s
Preamble: 4 symbols
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 35
Submission
symbol s1
Preamble 2: LED unit identifier
PHY SHR and PHR design: SM-PSK/DSM-PSK
Symbol s and
In case of SM-PSK, the white dot represents a group of LEDs is ON while the grey dot represents a group of LEDs is OFF.
Preamble symbols s1 and are to extract the LEDs-groups
Preamble symbols s2 and are to extract the single LED(s)
Preamble 1: LEDs-group identifier
symbol s2
Preamble: 4 symbols
s1 s2
Preamble: 4 symbols
LED on
LED off
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 36
Submission
PHY Summary
The proposed PHY modes using SM-PSK schemes are
  In flicker-free
  Compatible to varying frame rate
  Able to cancel the bad-sampling problem due to long exposure time of global shutter camera receiver
Performance:
  The data rate is from kbps to tens of kbps based upon the number of LEDs
  The S2-PSK provides highest data rate
  The DM8-PSK provides dimming feature in steps of 12.5%
In case of single LED, the S2-PSK scheme is compatible to both global shutter and rolling shutter receiver type.
The PHY frame structure is considered.
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 37
Submission
Appendix
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 38
Submission
Scenarios for SM-PSK and DSM-PSK
SM-PSK signal
SM-PSK signal
SM-PSK signal
doc.: IEEE 802.15-16- 0015 -01-007a

## Slide 39
Submission
Transmitter side
Receiver side
DSM-PSK and Color transmission
doc.: IEEE 802.15-16- 0015 -01-007a