## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: High-speed VLC for out-door free-space communication
Date Submitted: January 2016
Source: Prof. Nan Chi, Dr. Junwen Zhang Company: Fudan Univerisity
Address: Fu Dan University, 220 Handan Rd., Yangpu District, Shanghai
Voice: Tel: 0086-21-65642983, E-Mail: nanchi@fudan.edu.cn hustzjw@gmail.com
Abstract: In response to «Call for Proposals for OWC Channel Models» issued by 802.15.7r1, this contribution presents the PHY technologies proposal of outdoor free space VLC long distance transmission for high rate PD communication in wireless backhaul (mobile back haul).
Purpose: Call for Proposal Response
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Application Scenarios: Mobile backhauling
Backhaul is a top priority for small cell deployments
•80% of small cells will have wireless backhaul
•Cost of fiber is ~4x greater than wireless (cumulative CAPEX/OPEX)
•Small Cell mesh inter-connectivity over ~250m
•Large indoor and outdoor public spaces
* According to InterDigital Whitepaper 2013
*A typical mmW backhaul link
VLC outdoor free-space high speed PD communication for mobile backhaul
It shares the same CAPEX/OPEX advantages with mmW
More competitive with lower device cost
Characters:
Large indoor/outdoor public spaces
Distance: ~50 m~1 km
Speed: ~Gbps
Link: mainly Point-to-point

## Slide 3
Targets
High-speed VLC Out-door long-distance communication for mobile backhaul
Data Rates Speed: ~Gbps
Distance: 50m~1km, typical ~250-500 m
Environment: Large outdoor public spaces
Link: mainly Point-to-point
To provide a Out-door VLC free-space link for high-speed user applications.

## Slide 4
Proposal Research Route
Simulation for Outdoor Long Distance VLC Transmission System
System Structure and Simulation Parameters
Simulation Results and Analysis
Key Technique for High Speed Outdoor VLC Transmission System
Modulation formats
Pre Equalization and post-equalization
Diversity reception technology
VLC Free Space Transmission Channel Model
LED/PD Modulation Property
Optics System design
Free-space channel
Outdoor Transmission Experiments
System Structure
Results and Analysis
Multiplexing Technology

## Slide 5
High-speed VLC our-door modeling
High-speed VLC Out-door long-distance communication for mobile backhaul:Theoretical study of system Model
Tx/Rx LED and PD modulation model
LED Tx model:
modulation bandwidth (linear); Nonlinearity
PD/APD receiver sensitivity, noise
Optical System Model
LED beam, LED power, active area, beam width, multi-LED
Tx Focal length and diameter of lens, Tx/Rx Angle of Half
Received power, PD area, Rx Focal length/diameter of lens
Path loss, Distance
Air Turbulence
Background Noise, optical filter
Fog/Rain, impact of visibility
Free-space channel model
Link analysis
SISO
MIMO
Point-to-Point
Point-to-multi-Point

## Slide 6
TX：
  electronics：LED driving circuit，signal processing (coding,modulation, equalization)
  optics：transmitter antenna
RX：
  optics：receiver antenna，PD
  electronics： signal processing (decoding,demodulation, equalization),
Physical Layer of VLC system
Visible light transmission
LED
coding
modulation
Pre-equalization
O to E
Tx Module
LED Modulation
Rx Module
AD
AD
Demodulator
Decoder
Data
Baseband
Q
I
Phase
Signal processing

## Slide 7
Phosphor LED 10dB bandwidth<15MHz
RGB LED 10dB bandwidth<25MHz
1. LED bandwidth limitations
Higher order modulation and pre-equaliztion
PAM、OFDM
Advanced post-equalization techniques
ZF、DFE、RLS、DD-LMS
Single Carrier、CAP and so on
CMMA、M-CMMA
Volterra
Software/ hardware pre-equalization
2. VLC system Nonlinear
Inter-symbol interference
LED nonlinearity
Solutions
10dB Bandwidth
LED Nonlinearity

## Slide 8
Pre-equalization
Visible light transmission
LED
coding
modulation
O to E
Tx Module
LED Modulation
Rx Module
AD
AD
Demodulator
Decoder
Data
Baseband
Q
I
Phase
Signal processing
Pre-equalization schemes:
  Hardware Equalization：hardware circuit design
  Software Equalization：digital signal processing
VLC Channel Pre-equalization

## Slide 9
Software Pre-equalization
—FIR response
—Channel response
Pre-equalization
  Obtain the channel knowledge(H) at the RF domain
  Make pre-equalization Tx*1/H at the baseband
w/o pre-equlization
with pre-equlization
Y. Wang, et al, IEEE Communication Letters, Vol. 18, No. 10

## Slide 10: Hardware bridged-T amplitude equalizer
  Z11 : RLC network1 (R1, C1 and L1)
  Z22 : RLC network2 (R4, C2 and L2)
  R2 =R3 =R0
X. Huang, et al, OFC 2015, Tu2G.1
Notes: Resistor, Inductor and capacitor

## Slide 11
Hardware Pre-EQ for Gbps VLC system
X. Huang, et al, Optics express, 2015

## Slide 12
Bit-loading based OFDM-DMT modulation for Gbps VLC
X. Huang, et al, IEEE Photonics Journal, 2015

## Slide 13
Bit-loading based OFDM-DMT modulation for Gbps VLC
X. Huang, et al, IEEE Photonics Journal, 2015

## Slide 14
Post-equalization
Visible light transmission
LED
coding
modulation
O to E
Tx Module
LED Modulation
Rx Module
AD
AD
Demodulator
Decoder
Data
Baseband
Q
I
Phase
Signal processing
Post-equalization solutions:
  ISI Equalization：Classical DFE Modified Eqs
  Nonlinear Compensations：Volterra series
VLC Channel Post-equalization

## Slide 15
LED nonlinearity
LED nonlinearity seriously degrades the system performance;
The LED forward current exhibits strong nonlinearity with the bias voltage;
Two factors dominate the nonlinear effects: DC bias voltage and the input signal peak-to-peak value (Vpp);
Volterra nonlinear equalizer

## Slide 16
The Volterra series based equalizer is considered as a promising solution to mitigate the LED nonlinearity;
The Volterra series expansion contains a linear term and nonlinear series.
M-CMMA is utilized to update the weights of the nonlinear equalizer without using training symbols
Principle
Volterra nonlinear equalizer

## Slide 17
RGB LED (LED Engine) Multiplexing for high-speed VLC (WDM

## Slide 18: Receiver diversity technology
In receiver diversity, the outputs of multiple receivers are combined which is a weighted sum of the different branches
the output SNR:
The goal of MRC is to find the weight to maximize the output SNR
According to the Schwarz inequality, it is found that:
the maximum SNR of the combiner output is the sum of SNRs in each branch:
January, 2015

## Slide 19
At the distance of 50m, the total data rate of 1.8Gb/s can be achieved with the BER less than the 7 % FEC limit of 3.8x10-3.
Out-door Long distance testing results

## Slide 20
Conclusion
The out-door high-speed VLC modeling including three parts
LED/PD Modulation Property
Optical system design
Free-space channel
The results show the benefit and feasibility of the advanced pre-equalization and post-equalization technology for the high-speed VLC systems.
To achieve high speed VLC out-door communication, we provide analysis and our proposals on the following aspects
Adaptive Modulation formats: DMT with bit loading
Multiplexing Technology using different color LED and MIMO setup
Advanced Pre-/post- equalization methods
Receiver-diversity reception technology
In this contribution, we propose several general technique considerations for high rate PD VLC out-door communications.