## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [One-to-many and many-to-many peering procedures]
Date Submitted: [January 2016]
Source: [Huan-Bang Li, Marco Hernandez, Igor Dotlic, and Ryu Miura] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Contribution to 15.8 PAC draft]
Abstract: [Proposal of One-to-many and many-to-many peering procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: One-To-Many and Many-To-Many Peering Procedures
January, 2016

## Slide 3
Procedure for
One-to-many Peering

## Slide 4
MAC Higher Layer
#j R-PD
Higher Layer MAC
I-PD
#i R-PD
Higher Layer MAC
Peering Request
ACK with random back-off (#i)
#k R-PD
MAC
PEER_REQ.request.
ACK with random back-off (#j)
ACK with random back-off (#k)
PEER_REQ.indication
PEER_REQ.indication
Optional: Authentication & Authorization
PEER_REQ.response
PEER_REQ.response
Peering Response
Peering Response
Peering Response
ACK
ACK
ACK
PEER_REQ.confirm
PEER_REQ.confirm
PEER_REQ.confirm
Establish links

## Slide 5
Procedure for
Many-to-many Peering

## Slide 6
I-PD performs one-to-(N-1) peering
I-PD multicasts peered PDs list to N1 PDs
N1 ≤ (N-1)
Next PD in the list performs one-to-Ni) peering
The PD multicasts updated peered PDs list to N2 PDs
Ni+1 ≤ Ni
Last PD in the
updated peered list?
i = 1
i = i + 1
No
Yes
end
start

## Slide 7
Procedure for
One-to-many Re-Peering

## Slide 8
MAC Higher Layer
#j R-PD
Higher Layer MAC
I-PD
#i R-PD
Higher Layer MAC
Re-Peering Request
ACK with random back-off (#i)
#k R-PD
MAC
RE-PEER_REQ.request.
ACK with random back-off (#j)
ACK with random back-off (#k)
RE-PEER_REQ.indication
RE-PEER_REQ.indication
Optional: Authentication & Authorization
RE-PEER_REQ.response
RE-PEER_REQ.response
Re-Peering Response
Re-Peering Response
ACK
ACK
ACK
RE-PEER_REQ.confirm
RE-PEER_REQ.confirm
RE-PEER_REQ.confirm
Re-establish links
Re-Peering Response

## Slide 9
Procedure for
Many-to-many Re-Peering

## Slide 10
I-PD performs one-to-(N-1) re-peering
I-PD multicasts re-peered PDs list to N1 PDs
N1 ≤ (N-1)
Next PD in the list performs one-to-Ni) re-peering
The PD multicasts updated re-peered PDs list to N2 PDs
Ni+1 ≤ Ni
Last PD in the
updated re-peered list?
i = 1
i = i + 1
No
Yes
end
start

## Slide 11
Procedure for
One-to-many De-Peering

## Slide 12
MAC Higher Layer
#j R-PD
Higher Layer MAC
I-PD
#i R-PD
Higher Layer MAC
De-Peering Request
ACK with random back-off (#i)
#k R-PD
MAC
DE-PEER_REQ.request.
ACK with random back-off (#j)
ACK with random back-off (#k)
DE-PEER_REQ.indication
DE-PEER_REQ.indication
Optional: Authentication & Authorization
DE-PEER_REQ.response
DE-PEER_REQ.response
De-Peering Response
De-Peering Response
ACK
ACK
ACK
DE-PEER_REQ.confirm
DE-PEER_REQ.confirm
DE-PEER_REQ.confirm
Disconnect links
De-Peering Response
Optional

## Slide 13
Procedure for
Many-to-many De-Peering

## Slide 14
Any PD that intends to de-peer performs the one-to-many de-peering procedure.