## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [One-to-many and many-to-many peering procedures]
Date Submitted: [January 2016]
Source: [Huan-Bang Li, Marco Hernandez, Igor Dotlic, and Ryu Miura] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Contribution to 15.8 PAC draft]
Abstract: [Proposal of One-to-many and many-to-many peering procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: One-To-Many and Many-To-Many Peering Procedures
January, 2016

## Slide 3
Procedure for
One-to-many Peering

## Slide 4
MAC Higher Layer
#j R-PD
Higher Layer MAC
I-PD
#i R-PD
Higher Layer MAC
Peering Request
ACK with random back-off (#i)
#k R-PD
MAC
PEER_REQ.request.
ACK with random back-off (#j)
ACK with random back-off (#k)
PEER_REQ.indication
PEER_REQ.indication
Optional: Authentication & Authorization
PEER_REQ.response
PEER_REQ.response
Peering Response
Peering Response
Peering Response
ACK
ACK
ACK
PEER_REQ.confirm
PEER_REQ.confirm
PEER_REQ.confirm
Establish links
Group ACK with peered PD IDs
Re-ACK from lost PD
Repeat upto three times

## Slide 5
Procedure for
Many-to-many Peering

## Slide 6
I-PD performs one-to-(N-1) peering
I-PD multicasts peered PDs list to N1 PDs
N1 ≤ (N-1)
Next PD in the list performs one-to-Ni peering
The PD multicasts updated peered PDs list to Ni+1 PDs
Ni+1 ≤ Ni
Last PD in the
updated peered list?
i = 1
i = i + 1
No
Yes
end
start

## Slide 7
Procedure for
One-to-many De-Peering

## Slide 8
MAC Higher Layer
#j R-PD
Higher Layer MAC
I-PD
#i R-PD
Higher Layer MAC
De-Peering Request
#k R-PD
MAC
DE-PEER_REQ.request.
Disconnect links

## Slide 9
MAC Higher Layer
#j R-PD
Higher Layer MAC
I-PD
#i R-PD
Higher Layer MAC
De-Peering Request
#k R-PD
MAC
DE-PEER_REQ.request.
#i R-PD leaves group
(disconnect link between I-PD and #i R-PD)

## Slide 10
Procedure for
Many-to-many De-Peering

## Slide 11
Any PD that intends to de-peer performs the one-to-many de-peering procedure.