## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IG DEP Scope and Focused Applications with Different QoS Levels]
Date Submitted: [20 January, 2016]
Source: Ryuji Kohno, Yokohama National University/CWC-Nippon Co.
Address 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501
Voice: +81 (0)45-339-4115 Email: kohno@ynu.ac.jp, ryuji.kohno@cwc-nippon.co.jp]
Re: []
Abstract: [This document summarizes necessary technical requirement for focused applications by defining classes of application with various QoS levels corresponding requested levels of Dependability. This is quite important to make IG to SG, TG.]
Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE 802.15 IG DEP Scope and Focused Applications with Different QoS Levels Ryuji Kohno (Yokohama National University/CWC-Nippon Co.) RAtlanta, GA, USA January 20th, 2016

## Slide 3: Summary of Requirements
Number of sensors: few tens to hundreds per network
Support for multiple network co-existence & interoperability: few tens of networks
Types of topologies: star, mesh, inter-connected networks
Data rate requirement: up to 2 Mbps per sensor
Latency in normal operation: 250 ms to 1 s
Latency in critical situation: few ms to 15 ms
Aggregate data rate per network: up to 1 Gbps (in some applications) / few Mbps (in others)
Delivery ratio requirement: >99.9 % (in some applications) / > 99 % (in others)
Disconnection ratio < 0.01 % (of time)
Synchronization recovery time: < 100 ms
Coverage range: up to 1000 m (in some applications) / 20 m (in others)
Feedback loop response time: less than 1 s (10 ms In collision avoidance radar)
January 2016

## Slide 4: Summary of Requirements (cont.)
Handover capability: seamless between BANs and/or PANs, walking speed, 2 seconds
Transceiver power consumption: SotA acceptable
Module size: wearable for hospital use, maximum size 5 cm x 2 cm x 1 cm for automotive
Module weight: < 50 g for hospital, < 10 g for automotive & body
Data packet sizes (typical, maximum):
  Hospital: 100 bytes, 1000 bytes
  Automotive: 10 bytes, 1000 bytes
  Compatibility with CAN and RIM buses for intra-vehicle
Security considerations: Handover peers need to have trust relationship. High confidentiality and privacy requirements in hospital environment. Lifecycle management.
Sensor lifetime: minimum 1 year, up to equipment lifetime
Jitter: < 50 ms in regular case, < 5 ms in critical situations. 5 % outliers acceptable.
January 2016

## Slide 5: Summary of Requirements (cont.)
Interference models:
  Intra network interference (MAC&PHY specification dependent)
  Inter-network interference (take a look at literature, coexistence statements)
Channel models:
  in intra-vehicle (needs to be measured),
  inter-vehicle (exists in literature),
  in factory (partially exists in literature),
  in hospital (exist in literature),
  in emergency rescue field (exists?)
Any other?
January 2016

## Slide 6: Proposed applications
Remote healthcare monitoring
Remote sensing and controlling
Vehicle internal sensing and controlling
Collision avoidance radar
Inter-vehicle communications and ranging
Wearable and implant wireless medical sensing and controlling
Applications for ultra wideband radio
Reliable and robust radio control
Wearable healthcare sensing
Secure remote healthcare and medicine
Wireless sensing system for Factory with feedback control
Dependable multi-hop inter-vehicle communications
Inter-navigation and inter-vehicle information sharing in normal and emergency conditions
Single wireless communication network solution that functions both in normal and in disaster environments
Disaster prevention, emergency rescue and recovery
January 2016

## Slide 7: Focused Potential Applications
1.Automotive
  1.1Car Internal M2M
  1,2 Inter-vehicle M2M
  1.3 Remote Diagnosis in Factory
2. Medical Healthcare
  2.1 Wellness, Wellbeing
  2.2 Healthcare
  2.3 Professional Medicine
3. Social Public Service
  3.1 Life Line (Water/Gas/Electricity Supply)
  3.2 Public Safety
  3.3 Government System
4. Remote Infra Monitoring and Maintenance
  4.1 Remote Diagnosis of Infra(bridge/bldg/train)
  4.2 Remote Sensing and Controlling Mobile Robots
  4.3 Disaster Analysis and Prevention
We have been discussing on focused potential applications according to demands in a world.

## Slide 8
Fitness, Massage
& Sauna
Sports: Walking, Jogging,
Bicycling, Hiking, Skiing etc
Public Safety
Inter-Vehicle M2M
Highly Life Critical Uses(High QoS)
Less Life Critical Uses(Low QoS)
Home &
Consumer
Uses
Industrial &
Governmental
Uses
Internal Car Dependable M2M
Inter-Vehicle M2M
Home Medical Therapy
Government Infrastructure
Visualizing Portfolio of Focused Applications
Remote Diagnosis
for Factory Automation
Hospital Clinical Service
Remote Wellness
& Well-being
QoS 3; Relatively Lower Priority for
Demand of Dependability
  Life Line
  (Water/Gas/Electricity Supply)
Car, Bldg Care
business
Entertainment business
Regulatory Compliance
Test
Big Data Mining
Remote Sensing
& Controlling Mobile Robots
Disaster Analysis
& Prevention
Remote Diagnosi
s of Infra(bridge/bldg/train)
QoS 2; Middle Priority of Demand of Dependability
QoS 1; Highest Priority of Demand
of Dependability

## Slide 9: Three Classes of Focused Potential Applications
QoS 1 Class: Highest Priority Level for Demand of Dependability
  1.1Car Internal M2M
  1.3 Remote Diagnosis in Factory
  2.3 Professional Medicine
  3.2 Public Safety
QoS 2 Class: Meddle Priority Level for Demand of Dependability
  1,2 Inter-vehicle M2M
  2.2 Healthcare
  3.1 Life Line (Water/Gas/Electricity Supply)
  4.1 Remote Diagnosis of Infra(bridge/bldg/train)
QoS 3 Class: Low Priority Level for Demand of Dependability
  2.1 Wellness, Wellbeing
  3.3 Government System
  4.2 Remote Sensing and Controlling Mobile Robots
  4.3 Disaster Analysis and Prevention
We have classified focused potential applications into three classes according to demands of dependability.