## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal of SRM service primitives for Technical Guidance Document]
Date Submitted: [12 March, 2016]
Source: [Hidetoshi Yokota, Ruben Salazar, Chris Calvert, Steve Chasko and Chris Hett] Company [Landis&Gyr]
Address: [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan,
30000 Mill Creek Av., Alpharetta, GA 30022, USA ]
Voice: [+81 3-5532-7455, +1 678 258 3165, +1 678 258 1516, +1 678 258 1538, +1 678 258 1398] E-Mail: [hidetoshi.yokota@landisgyr.com, ruben.salazar@landisgyr.com, chris.calvert@landisgyr.com, stephen.chasko@landisgyr.com, chris.hett@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-11-004s]
Abstract: [This contribution proposes MAC commands that should be considered in the Technical Guidance Document for measuring spectrum resources in WPAN.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal of SRM service primitives for Technical Guidance Document
Authors:

## Slide 3: MLME-SAP for SRM (8.2.1)
Name | Request | Indication | Response | Confirm
MLME-SRM | 8.2.26.1* | 8.2.26.2* | 8.2.26.3* | 8.2.26.4*
MLME-SRM-REPORT | 8.2.27.1* | 8.2.27.2* |  | 8.2.27.3*
MLME-SRM-INFORMATION | 8.2.28.1* | 8.2.28.2* |  | 8.2.28.3*
Table 57—Summary of the primitives accessed through the MLME-SAP

## Slide 4: Primitives for SRM (8.2.26)
MLME-SRM.request primitive (8.2.26.1)
MLME-SRM.request (
          DeviceAddrMode,
          DeviceAddress,
          HeaderIeList,
          StartTime,
          Duration,
          ChannelPage,
          ChannelNumber,
          SecurityLevel,
          KeyIdMode,
          KeySource,
          KeyIndex
      )
Notes: 8.2.5.3 MLME-IE-NOTIFY.indication
8.2.22.1 MLME-PHY-OP-SWITCH.request

## Slide 5: Primitives for SRM (8.2.26)
MLME-SRM.request parameters (8.2.26.1)
Name | Type | Valid range | Description
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device being instructed to execute SRM operation.
DeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device being instructed to execute SRM operation.
HeaderIeList | Set of header IEs as described in 7.4.2 | --- | The SRM-related header IEs, excluding Termination IEs, that were included in the frame. If empty, then no header IEs were included.
StartTime | Unsigned Integer | 0x00000000-0xffffffff | The time at which the requested measurement should be started.
Duration | Integer | 0x0000-0xffff | The duration over which the requested measurement should be measured.
ChannelPage | Integer | Any valid channel page | The channel page on which the measurement to be executed
ChannelNumber | Integer | Any valid Channel number | The channel number on which the measurement to be executed
SecurityLevel | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeyIdMode | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeySource | Set of octets | As defined in Table 8-134 | As defined in Table 8-134
KeyIndex | Integer | As defined in Table 8-134 | As defined in Table 8-134

## Slide 6: Primitives for SRM (8.2.26)
MLME-SRM.indication primitive (8.2.26.2)
MLME-SRM.indication parameters
  Same as MLME-SRM.request parameters
MLME-SRM.indication (
          DeviceAddrMode,
          DeviceAddress,
          HeaderIeList,
          StartTime,
          Duration,
          ChannelPage,
          ChannelNumber,
          SecurityLevel,
          KeyIdMode,
          KeySource,
          KeyIndex
      )

## Slide 7: Primitives for SRM (8.2.26)
MLME-SRM.indication parameters (8.2.26.1)
Name | Type | Valid range | Description
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device requesting to execute SRM operation.
DeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device requesting to execute SRM operation.
HeaderIeList | Set of header IEs as described in 7.4.2 | --- | The header IEs, excluding Termination IEs, that were included in the frame. If empty, then no header IEs were included.
StartTime | Unsigned Integer | 0x00000000-0xffffffff | The time at which the requested measurement should be started.
Duration | Integer | 0x0000-0xffff | The duration over which the requested measurement should be measured.
ChannelPage | Integer | Any valid channel page | The channel page on which the measurement to be executed
ChannelNumber | Integer | Any valid Channel number | The channel number on which the measurement to be executed
SecurityLevel | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeyIdMode | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeySource | Set of octets | As defined in Table 8-134 | As defined in Table 8-134
KeyIndex | Integer | As defined in Table 8-134 | As defined in Table 8-134

## Slide 8: Primitives for SRM (8.2.26)
MLME-SRM.response primitive (8.2.26.3)
MLME-SRM.response (
          DeviceAddrMode,
          DeviceAddress,
          HeaderIeList,
          MeasuredDeviceAddrMode,
          MeasuredDeviceAddress,
          SecurityLevel,
          KeyIdMode,
          KeySource,
          KeyIndex
      )

## Slide 9: Primitives for SRM (8.2.26)
MLME-SRM.response parameters (8.2.26.3)
Name | Type | Valid range | Description
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device requesting to execute SRM operation.
DeviceAddress | Short address or extended Address | As specified by the DeviceAddrMode Parameter | The address of the device requesting to execute SRM operation.
HeaderIeList | Set of header IEs as described in 7.4.2 | --- | The SRM-related header IEs, excluding Termination IEs, that were included in the frame. If empty, then no header IEs were included.
MeasuredDeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device, for which the measurement was executed.
MeasuredDeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device, for which the measurement was executed.
SecurityLevel | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeyIdMode | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeySource | Set of octets | As defined in Table 8-134 | As defined in Table 8-134
KeyIndex | Integer | As defined in Table 8-134 | As defined in Table 8-134

## Slide 10: Primitives for SRM (8.2.26)
MLME-SRM.confirm primitive (8.2.26.4)
MLME-SRM.confirm (
          DeviceAddrMode,
          DeviceAddress,
          MeasuredDeviceAddrMode,
          MeasuredDeviceAddress,
          Status
      )

## Slide 11: Primitives for SRM (8.2.26)
MLME-SRM.confirm parameters (8.2.26.4)
Name | Type | Valid range | Description
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device being instructed to execute SRM operation.
DeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device being instructed to execute SRM operation.
MeasuredDeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device, for which the measurement was executed.
MeasuredDeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device, for which the measurement was executed.
Duration | Integer | 0x0000-0xffff | The duration over which the requested measurement was measured.
Status | Enumeration | SUCCESS, NON_SUPPORTED, REJECTED | The status of the SRM attempt.

## Slide 12: Primitives for SRM-REPORT-NOTIFICATION (8.2.27)
MLME-SRM-REPORT-NOTIFICATION.request primitive (8.2.27.1)
MLME-SRM-REPORT.request (
          DeviceAddrMode,
          DeviceAddress,
          HeaderIeList,
          RequireConfirm,
          SecurityLevel,
          KeyIdMode,
          KeySource,
          KeyIndex
      )
Notes: 8.2.5.3 MLME-IE-NOTIFY.indication
8.2.22.1 MLME-PHY-OP-SWITCH.request

## Slide 13: Primitives for SRM-REPORT-NOTIFICATION (8.2.27)
MLME-SRM-REPORT-NOTIFICATION.request parameters (8.2.27.1)
Name | Type | Valid range | Description
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device, to which SRM report is transferred.
DeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device, to which SRM report is transferred.
HeaderIeList | Set of header IEs as described in 7.4.2 | --- | The SRM-related header IEs, excluding Termination IEs, that were included in the frame.
RequireConfirm | Boolean | TRUE, FALSE | Set to TRUE if MLME-SRM-REPORT-NOTIFICATION.confirm is required
SecurityLevel | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeyIdMode | Integer | As defined in Table 8-134 | As defined in Table 8-134
KeySource | Set of octets | As defined in Table 8-134 | As defined in Table 8-134
KeyIndex | Integer | As defined in Table 8-134 | As defined in Table 8-134

## Slide 14: Primitives for SRM-REPORT-NOTIFICATION (8.2.27)
MLME-SRM-REPORT-NOTIFICATION.indication primitive (8.2.27.2)
MLME-SRM-REPORT.indication parameters
  Same as MLME-SRM-REPORT.request parameters (except for RequreConfirm)
MLME-SRM.indication (
          DeviceAddrMode,
          DeviceAddress,
          HeaderIeList,
          SecurityLevel,
          KeyIdMode,
          KeySource,
          KeyIndex
      )

## Slide 15: Primitives for SRM-REPORT-NOTIFICATION (8.2.27)
MLME-SRM-REPORT-NOTIFICATION.confirm primitive (8.2.27.3)
MLME-SRM-REPORT-NOTIFICATION.confirm (
          Status
      )

## Slide 16: Primitives for SRM-REPORT-NOTIFICATION (8.2.27)
MLME-SRM-REPORT-NOTIFICATION.confirm parameters (8.2.27.3)
Name | Type | Valid range | Description
Status | Enumeration | SUCCESS, FAILURE | The result of the attempt to send MLME-SRM-REPORT-NOTIFICATION.confirm