## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed resolution for CID 2153, 2159, 2161, 2167, 2168, 2276
Date Submitted: Jan., 2016
Source: Jaehwan Kim, Sangsung Choi (ETRI), Jaebeom Kim, Youngbae Ko (Ajou Univ.), Soo-Young Chang (SYCA), and Cheolho Shin (ETRI)
Company: ETRI, Ajou Univ., SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #113
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 2153
Commentor
  Jussi Haapola
Related clause
  5.2.7 P 37 line 22-24
Comment
  Why is the hop count the only applicable routing metric in L2R P2P route establishment?
Proposed Change
  If using only hop count as a metric is intentional, it would be convenient to state a reason for such limitation.

## Slide 3: CID 2153
Proposed Resolution
  Revise
  Relplace "threin" with "retrieved from the hop count field"

## Slide 4: CID 2159
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.7 P 37 line20
Comment
  "it does not propagate the P2P-RQ IE but replies with a P2P-RP IE." is not really accurate In storing mode, an intermediate hop only knows the next hop to the destination but not the entire path. Besides, the Hop Count is not recorded. In non-storing mode, only the destination knows the entire path. Unless there is an option to record the paths in intermediate nodes.
  In each case what kind of information should the Intermediate hop include in the P2P-RP IE?
Proposed Change
  Double check and revise the behavior of the intermediate hops for each mode

## Slide 5: CID 2159
Proposed Resolution
  Revise
  Replace ‘path’ with ‘ the reachable destination information”
  Add a description of the hop count incensement state.
  “If the Request Direct Response field in the P2P-RQ IE is set to 1 and if an intermediate device has the reachable destination information to the requested destination, it does not propagate the P2P-RQ IE but replies with a P2P-RP IE. The original source device may start routing data frames as soon as it receives a P2P-RP IE. Hop count in the P2P-RP is increase by each forwarding node. When a device receives a new P2P-RP IE, it the therein is lower than the hop count provided by the current next hop, the route record is replaced with the information of the new P2P-RP IE. Otherwise the P2P-RP IE is discarded.”

## Slide 6: CID 2161
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.7 P 37 line 22
Comment
  "the hop count therein" here is not "Hop Count field in the P2P-RP IE"
Proposed Change
  Add a Hop Count field or revise this description

## Slide 7: CID 2161
Proposed Resolution
  Revise
  add the “hop count” and “TTL” field.
  remove mesh root address field.
  Hop Count field
  The Hop Count field indicates the number of hops between the device currently transmitting the P2P-RQ IE and the original source and is encoded as an unsigned integer.
  TTL
  The TTL field indicates the remaining number of times the current P2P-RP IE is allowed to be forwarded and is encoded as an unsigned integer. The initial value of this field is set to hop count in the received P2P-RQ IE
Figure 46—Format of the P2P-RP IE

## Slide 8: CID 2167
Commentor
  Jussi Haapola
Related clause
  5.2.7 P 38 Figure 19
Comment
  The figure is grossly inaccurate to depict route establishment behavior described in the text of section 5.2.7. The RQ propagation only shows one of the paths leading to the same hop count and does not really show any of the other possibilities. As a whole it causes more conflict with the text than illustrates the behavior.
Proposed Change
  Remove Figure 19.

## Slide 9: CID 2167
Proposed Resolution
  Revise
  Add a statement for figure 19.
  “Figure 19 shows an example of the P2P route establishment between devices D and H. In this figure, the arrows for P2P-RQ message are represented only source device H to reduce the complexity. If G has a path to H and if intermediate response is enabled, G responds with a P2P-RP IE without reforwarding an in incoming P2P-RQ IE. Otherwise, all devices forward the P2P-RQ IE.

## Slide 10: CID 2168
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.7 P 38 line 11
Comment
  What is the meaning of the non-bold arrow from H to G?
Proposed Change
  Add a legend or make it bold.

## Slide 11: CID 2168
Proposed Resolution
  Revise
  make “the bold arrow from H to G” bold.

## Slide 12: CID 2276
Commentor
  Verotiana Rabarijaona
Related clause
  6.1.5.1 P 66 line 19
Comment
  There is no Mesh Root Address in Fig. 44.
Proposed Change
  Add the field or delete subclause 6.1.5.1.

## Slide 13: CID 2276
Proposed Resolution
  Revise
  Delete “Mesh Root Address” field