## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed resolution for CID R2255, R2256, R2063
Date Submitted: Feb., 2016
Source: Jaehwan Kim, Sangsung Choi (ETRI), Jaebeom Kim, Youngbae Ko (Ajou Univ.), Soo-Young Chang (SYCA), and Cheolho Shin (ETRI)
Company: ETRI, Ajou Univ., SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #113
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID R2055
Commentor
  Charlie Perkins
Related clause
  5.2.2.3 P 30 line33
Comment
  ETT section missing
Proposed Change
  for ETT analogous to ETX

## Slide 3: CID R2055
Proposed Resolution
  Revise
  Delete ETT from table 11

## Slide 4: CID R2056
Commentor
  Charlie Perkins
Related clause
  5.2.2.3 P 30 line54
Comment
  Motivation for airtime metric seems missing
Proposed Change
  Please describe the intended effect of the weighting

## Slide 5: CID R2056
Proposed Resolution
  Revise
  Add a description for airtime link metric
  5.2.2.3 Expected airtime metric
  Expected airtime represents the estimated transmissions time to successfully send a packet (each packet smaller than MTU) over that link, measured in units of ms. Default value of the expected airtime is set to 1. This metric considers the inactive time of a device and the error rate of a link. In non-beacon enabled PANs, the BO and SO are set to ….. The inactive time aware airtime is calculated as follows:

## Slide 6: CID R2063
Commentor
  Charlie Perkins
Related clause
  5.2.4.3 P 34 line53
Comment
  "parent PAN" is undefined
Proposed Change
  Provide (or cite) a definition. Is this only for MCO?

## Slide 7: CID R2063
Proposed Resolution
  Revise
  Add new definition in clause 3.1
    parent PAN: PAN with which a PAN coordinator is associated before starting its own PAN in a TMCTP.