## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [A method for generating realistic wireless traffic through analysis of smartphone operation logs]
Date Submitted: [25 Feb, 2016]
Source: [Yuko Hirabe, Yutaka Arakawa, Keiichi Yasumoto] Company [Nara Institute of Science and Technology (NAIST)]
Address [Takayama-cho 8916-5, Ikoma, Nara 630–0192, Japan ]
Voice:[+81-743-72-5392], FAX: [+81-743-72-5976], E-Mail:[hirabe.yuko.ho2@is.naist.jp, ara@is.naist.jp, yasumoto@is.naist.jp]
Re: []
Abstract: [This document introduces a performance evaluation method for IEEE 802.15-based systems by generating realistic interfering traffic of wireless LAN which smartphones produce. This is informative to discuss significance of performance analysis in IEEE802.15 TG4s.]
Purpose: [For discussion]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: A method for generating realistic wireless traffic through analysis of smartphone operation logs
Authors:
Name | Company | Address | Phone | email
Yuko Hirabe, Yutaka Arakawa, Keiichi Yasumoto | Nara Institute of Science and Technology (NAIST) | Takayama-cho 8916-5, Ikoma, Nara 630–0192, Japan | +81-743-72-5392 | hirabe.yuko.ho2@is.naist.jp ara@is.naist.jp yasumoto@is.naist.jp

## Slide 3: Overview
Power consumption
Location
server
Send
Sensors’ data
Internet
Gateway
Wifi interference
Current: realistic performance evaluation of 802.15 (Zigbee)-based systems is difficult
 realistic Wifi interference is not considered.
Purpose: generating realistic interfering traffic that WiFi devices (e.g., smartphones) actually produce
IoT + Smart Home
Proposal: developing a statistic model generating realistic 802.11 (Wifi) traffic,
and clarify interference patterns to 802.15 (Zigbee)
apply the model to realistic performance evaluation of 802.15 (Zigbee)-based systems
802.11: Wifi 802.15: Zigbee
Wifi interference
Temperature, humidity

## Slide 4: Background
Penetration of the Internet of Things (IoT) in homes
  Increase of networked appliances and sensors (IoT devices) in smart homes
      ex) power meters, ambient sensors
Sensor data are sent by Zigbee
Smartphones/tablets are also used in homes
IoT devices(Zigbee) + smartphone(WiFi)  cause interference
  E.g., Sensor data may not be sent via Zigbee
A method for realistic performance evaluation of 802.15 (Zigbee)-based systems, considering realistic Wifi interference is needed
Power consumption
Temperature, humidity
Location
server
Send
Sensors’ data
Internet
Gateway
Wifi interference
IoT + Smart Home
Current: realistic performance evaluation of 802.15 (Zigbee) base system is difficult due to Wifi interference.
802.11: Wifi 802.15: Zigbee

## Slide 5: How to model the Wifi interference?
General performance evaluation of wireless communication system
  Wireless traffic generation by random/probabilistic traffic model [1]
Wifi coexists with 802.15 in a home environment.
  Wifi traffic may disturb Zigbee data communication.
  Current main WiFi traffic source is a smartphone.
1. H. Zhai et al., Performance analysis of IEEE 802.11 MAC protocols in wireless LANs, Wireless Communications and Mobile Computing 4.8, 2004.
Need to generate realistic Wifi traffic from a smartphone

## Slide 6: Wifi traffic pattern depends on the type of apps.
Various mobile apps generate different traffic
  SNS: Facebook, Twitter, Instagram
    Text, Photo, Movie
  Multimedia: YouTube, Youku, iCloud, Google Photo
    Movie, photo （huge traffic [2]）
  Map: Google Maps, Apple map
    map tile data
  File: Dropbox, Box, Google drive
    Every types
Usage pattern also affects to the generated traffic.
  preload, play a video, input text, share photo
2. Chart by BI Intelligence, used in Business Insider event, IGNITION

## Slide 7: Different traffic for different usage pattern
View posts by others (Download)
Text, picture, movie
Contents
DL happens in only displayed range
Scrolling
preload & increase of traffic
Comments：Like, text
Posts: text, picture, movie, share
larger traffic
Post items
（Upload）

## Slide 8: Traffic generation pattern on Facebook
Facebook
Posts: Upload
View：Download
With scrolling
Without scrolling
Comments
Posts
Traffic
Small (DL)
Big (DL)
Small (UL)
Big (UL)
Operations of 4 types

## Slide 9: Goal and approach
Approach:
Step1: Recognize a user’s operations on each app.
Step2: Measure a generated traffic for each operation
Step3: Construct a statistical traffic generation model by associating each operation with the measured traffic
Step4: Clarify the interference of 802.11 (Wifi) to 802.15 (Zigbee) by using a spectrum analyzer or packet loss evaluation.
Goal: developing the realistic 802.11 (Wifi) traffic generation model
to clarify the interference to 802.15 (Zigbee)

## Slide 10: Step1. Recognize a user’s operations on each app by using smartphone logs
Difficulty of accomplishing the challenge:
With smartphone logs, we can easily know what apps are running, but cannot know what operations are happening on all the apps.
Approach：
Challenge: recognize each operation (4 types)
Try to recognize through analysis of touch panel logs

## Slide 11: Developed system: TouchAnalyzer[3]
The system for acquisition and analysis of touch panel logs
TouchAnalyzer
Acquisition of touch-panel logs
Touch
Swipe
Identify touch operation behaviors
Pinch
Rotate
  Statistical processing
  Identify gesture's name and the number of fingers
  Calculate speed of swipes
  Aggregation for each application
[3] Hirabe, Y, et al. ICMU 2014

## Slide 12: Developed system: TouchAnalyzer[3]
The system for acquisition and analysis of touch panel logs
TouchAnalyzer
Acquisition of touch-panel logs
Touch
Swipe
Identify touch operation behaviors
Pinch
Rotate
  Statistical processing
  Identify gesture's name and the number of fingers
  Calculate speed of swipes
  Aggregation for each application
[3] Hirabe, Y, et al. ICMU 2014
Recognize touch operations (touch, swipe, rotate, pinch) by analyzing touch panel logs

## Slide 13: Step2. Measure communication traffic for each operation
Approach １：
Obtain packets in a smartphone
  ex）tPacketCapture[4]
Approach ２：
Obtain packets on PC (router)
  ex）Wireshark[5]
Associate each app. operation
with the measured traffic
  Construct statistical model
Goal: acquisition of communication traffic for each app. operation
4. Tao Software, tPacketCapture, http://www.taosoftware.co.jp/android/packetcapture/
5. WIRESHARK, https://www.wireshark.org
Screen capture of tPacketCapture
Screen capture of Wireshark

## Slide 14: Step3. Construct statistical traffic generation model for each app. operation
Approach：
Construct a histogram of generated traffic for each operation  probabilistic distribution of traffic
Construct a state transition model among 4 app. operations
Goal: Integration of communication traffic which are generated on apps
View w/o scroll
View w. scroll
Comment
Post
Traffic distribution
Traffic generation model of each mobile user

## Slide 15: Step 4: Measure commun. traffic of 802.11 (Wifi) and 802.15 (Zigbee), using a spectrum analyzer
Observe 802.15 traffic signals in a smart home, producing Wifi traffic by the proposed model
Goal: Measure interference patterns between 802.11 and 802.15
server
Send
Sensors’ data
Internet
Gateway
Wifi interference
IoT + Smart Home
Investigate occurrence degree of interference by using a spectrum analyzer[6]
Screen capture of spectrum analyzer
6. Handheld spectrum analyzer/Signal analyzer, http://www.micronix-jp.com/english/product/product_1.html
Power consumption
Temperature, humidity
Location

## Slide 16: Result of pilot study with Facebook
Confirmed that classification of app. operations is possible
Classification algorithm will be developed
Difference among different app. operations

## Slide 17: Summary and discussion
Proposed a performance evaluation method for IEEE 802.15-based systems by generating realistic WiFi interfering traffic especially smartphones produce.
Constructed a realistic WiFi traffic generation model, reflecting mobile users’ operations in specific applications (SNS applications such as Facebook)
Future work
Develop classification algorithm of users' application
  Operations through analysis of touch panel logs and measurement of WiFi traffic generated by each operation
  target apps: Instagram, Facebook, LINE
Measure interference patterns between 802.15 and 802.11
Implement the model, and incorporate it into network simulators