## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Interference management for high rate PD communications]
Date Submitted: [7 March, 2016]
Source: [Li Qiang, Jiang Tong, Dong Chen] Company [Huawei]
Address [Huawei Building, No.3 Xinxi Road, Haidian, Beijing, China]
Voice:[86-15801539749], FAX: [+86-10-82882144], E-Mail:[john.liqiang@huawei.com]
Re: []
Abstract: [In this contribution, we analyze the interference management mechanisms for high PD communications.]
Purpose: [Contribution to IEEE 802.15.7r1 Optical Wireless Communication]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Interference management for high rate PD communications
Li Qiang, Jiang Tong, Dong Chen
Huawei

## Slide 3: Scenarios
Two scenarios are considered in this contribution
  Centralized: with global controller
  Distributed: without global controller
Global controller : provides coordination between different VPANs. A global controller collects the information of different VPANs and coordinates the resources among these VPANs.
Coordinator : manages the operation of a corresponding VPAN

## Slide 4: Different types of interference
Ambient light (sunlight, incandescent lamp, fluorescent lamp, TV screen, etc)
  Most ambient light interferences are narrow band
Inter-VPAN interference
Ambient light interference
Inter-VPAN interference

## Slide 5: Interference coordination (Centralized)
Inter-VPAN Interference
Step1, interference measurement:
A device may detect and measure interference from neighboring VPANs
A coordinator may detect and measure interference from neighboring VPANs
Step2, interference report from device to coordinator. (command frames may need to be specified)
Step3, interference report from coordinator to global controller. (The procedure may need to be specified.)
Step4, resource coordination:
A global controller allocates resources for coordinators under its control. (The procedure may need to be specified.)

## Slide 6: Interference coordination (Centralized)
Interference coordination for beacon
  WDM: Neighboring coordinators transmit beacons in different wavelength (e.g. Red / Green / Blue)
  TDM: Neighboring coordinators use beacon slots that are orthogonal to each other. (Note the boundaries of super frames need to be aligned)
  TDM and WDM can be jointly used.
  The resources used by beacons are assigned by global controller

## Slide 7: Interference coordination (Centralized)
Interference coordination for data
  TDM and WDM are more straightforward. They can be jointly used.
  The resources used by beacons are assigned by global controller.
Wavelength division
Frequency division
Time division

## Slide 8: Interference coordination (distributed)
Inter-VPAN Interference
Step1, interference measurement:
A device may detect and measure interference from neighboring VPANs
A coordinator may detect and measure interference from neighboring VPANs
Step3, resource reselection:
VPAN1 reallocate resource for the device according to the interference reports.
Step2, interference report from device to coordinator. (command frames may need to be specified)

## Slide 9: Interference coordination (distributed)
For distributed interference management
  If the boundaries of super frames can be aligned between neighboring cells, then TDM is preferred due to its simplicity.
  If super frame alignment is proved to be problematic, then FDM can be used.
  WDM can be jointly used with FDM or TDM
Wavelength division
Frequency division
Time division

## Slide 10: Conclusions
In this contribution, we analyze the interference management schemes for high speed PD communications. It is proposed that,
Proposal 1: define a set of command frames for interference reporting from devices to associated coordinators
Proposal 2: specify a procedure to support interference reporting from coordinators to global controller
Proposal 3: specify a procedure for a global controller to assign resources for the coordinators under its control