## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Performance Evaluation of Millimeter-wave-based Communication System in Subway Tunnels]
Date Submitted: [14 March, 2016]
Source: [Sung-Woo Choi, Junhyeong Kim, Hee-Sang Chung, Seung Nam Choi, Dae-Soon Cho, Bing Hui, and Il Gyu Kim] Company [ETRI]
Address [218 Gajeong-ro, Yuseong-gu, Daejeon, 34129, KOREA]
Voice:[+82-42-860-6113], FAX: [+82-42-861-1966], E-Mail:[csw9908@etri.re.kr]
Abstract: [This document presents performance evaluation results of a prototype of a millimeter-wave-based communication system in tunnel environments]
Purpose: [For discussion]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
People want to access Internet every time and every where
Current Wi-Fi service provided in high-speed trains and subways is hard to satisfy onboard passengers’ demand
  Need performance enhancement
Increasing data rate is possible by using abundant spectrum available in millimeter wave
Current ongoing project in ETRI
  Project Name : Mobile Hotspot Network (MHN)
    Development of MHN mobile wireless backhaul system
Objective of this document
  Provide recent performance evaluation results of a prototype of a mmWave-based communication system in tunnel environments
    Data rate according to distance
    Channel estimation results

## Slide 3: Introduction
Network Architecture
  Backhaul & user access links
Two-tier network
MHN application for railways
DU
GW
RU
RU
TE
Backhaul Link
mmWave
Backhaul Link
mmWave
AP
TE
Public Internet
DU : Digital Unit
TE : Terminal Equipment
RU : Radio Unit
GW : Gateway

## Slide 4: Introduction
Characteristics of Millimeter Wave
  Suffering from increased propagation loss and atmospheric loss
    Ex. 20dB increase in propagation loss (comparison between 3 and 30GHz)
  Decreased coverage of cell
  Strong tendency of straightness
  Less multipath components
    Usually under 100 ns
  Have different feature from cellular frequency bands  Need new OFDM specification
Radio Technology of MHN
  Modulation : OFDM
  Multiple access : OFDMA

## Slide 5: Introduction
Physical Layer Technology of MHN
  Reduced OFDM symbols duration : 6.25us (cf. 71.4us of LTE)
  Reduced slot time : 250 us (cf. 1ms of LTE)
  TDD(mandatory), FDD
Parameters | Value
Size of FFT | 1024
Subcarrier spacing | 180 kHz
Sampling frequency | 184.32 MHz
Cyclic prefix | 0.69 μs
Carrier frequency | 31.5 – 31.75 GHz
Symbol duration | 6.25 μs
Channel coding | Turbo code
Modulation | QPSK, 16QAM, 64QAM
Sub-band bandwidth | 125 MHz
Peak data rate | 250 Mbps per sub-band

## Slide 6: Introduction
Frame Structure of MHN

## Slide 7: Experimental Environment
System Prototype
  RU-DU (Transmitter) : RF module, BB module, 1 antenna
  TE (Receiver) : RF module, BB module, 2 antennas
  Two sub-bands : 125 MHz x 2
  Max. physical layer data rate : 500 Mbps
RF module
  Power amplifier with a maximum power of 1 watt and 10-dB back-off
  TX antenna input power : 100 mW
  8x8 patch array antenna
  3-dB beamwidth (vertical, horizontal) : 8°
  Antenna gain (TX, RX) : 22 dBi
  Size : 60mm x 76mm
RU-DU
TE

## Slide 8: Experimental Environment
Seoul subway line 8
Jamsil
Seokchon
Songpa
curved route
(600 m)
straight route
(1.1 km)
RU/DU
TE
MHN Test beds on Moving Carts

## Slide 9: Experimental Environment
Tunnel structure in Seoul subway line 8
  Box-type tunnels and have two lanes
  Two lanes are separated by pillars in the middle
    Average width : 2 m, Average spacing : 85 cm

## Slide 10: Measuring tools
Functional blocks in TE and DU
Turbo Code
QAM Signal Mapping
Resource Mapping
OFDM Signal Generation
RF
RF
Sell Searcher
OFDM Demodulation
Channel Estimation
Signal Detection
Resource and QAM Demapping
Turbo Decoding
BLER Calculation
SNR
Freq. response
Time response
DU
TE
RU-DU
TE

## Slide 11: Experimental Results – Curved Route
SNR and data-rate according to distance between TX and RX
  MCS 21 : 64 QAM, code rate = 0.58  500 Mbps
  MCS 10 : 16 QAM, code rate = 0.32  183 Mbps
  MCS 5 : QPSK, code rate = 0.35  102 Mbps

## Slide 12: Experimental Results – Curved Route
Frequency domain response (at 320 meters)
Green : ABS of ideal channel
Magenta : ABS of measured channel
# of sub-carriers
FA-0, Ant. 0
FA-0, Ant. 1
FA-1, Ant. 0
FA-1, Ant. 1

## Slide 13: Experimental Results – Curved Route
Time-domain impulse response (at 320 meters)
  Time domain response : IFFT of channel estimation
Ant. 0
Ant. 1
Delay spread ≤ 60 ns
(OFDM CP length = 0.69 μs = 690 ns)
Green : reference
Blue : POW of estimated impulse response
# of samples

## Slide 14: Experimental Results – Curved Route
Frequency response (at 440 meters)
Green : ABS of ideal channel
Magenta : ABS of measured channel

## Slide 15: Experimental Results – Straight Route
SNR and data-rate according to distance between TX and RX
500 Mbps

## Slide 16: Experimental Results – Straight Route
Frequency domain response (at 1.1 km)
Green : ABS of ideal channel
Magenta : ABS of measured channel
FA-0, Ant. 0
FA-0, Ant. 1
FA-1, Ant. 0
FA-1, Ant. 1

## Slide 17: Experimental Results – Straight Route
Time-domain impulse response (at 700 meters)
Green : reference timing
Blue : POW of estimated impulse response
Second peak

## Slide 18: Field Trial of MHN System
MHN Test Bed Installation along Seoul Subway Line 8
mDU : MHN Digital Unit
mTE : MHN Terminal Equipment
mRU : MHN Radio Unit
mGW : MHN Gateway
Coverage Test : Nov. 10, Nov. 12, 2015
End of Construction : Dec. 4, 2015
Jamsil
Seokchon
Songpa
Jamsil Station
Seokchon
Station
Songpa
Station

## Slide 19: Field Trial of MHN System
Revision of MHN Test Bed
mDU Test Bed at Jamsil Station
mGW
5 mDUs
MODEMs
mRU of mDU
mTE
Optical Fiber
(for 2 mRUs)

## Slide 20: Field Trial of MHN System
mRU & mTE Test Bed Installation
mRU
mTE

## Slide 21: Field Trial of MHN System
Performance Evaluation of MHN System for Moving Subway
  Peak data rate of over 400Mbps was achieved

## Slide 22: Conclusions
We developed a prototype of a millimeter wave-based communication system (MWBCS) for a use in the Railway communication networks (RCNs)
In a curved route, the system could achieve a data rate of 500 Mbps in the first 400 m, and a data rate of 100 Mbps was possible over 400 ~ 560 m
In the case of a straight route, the testbed is able to achieve 500 Mbps in the distance up to 1.1 km
The test also gave us an important information about
  characteristics of channel in frequency-domain
  time impulse response
The time impulse response clarified that the delay spreads in those tunnel environments were less than 60 ns
Furthermore, the results that we obtained from the tests have been used to determine appropriate RU spacing in the system deployment
Finally, we successfully gave a demonstration of the system in the moving subway showing a peak data rate of over 400Mbps

## Slide 23: Field Trial of MHN System
Demonstration Video