## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution on comment #42, #44 and #45 for HRCP-SC PHY]
Date Submitted: [14 March 2016]
Source: [Keitarou Kondou]
Company: [Sony Corporation]
Address1: [1-7-1 Konan, Minato-ku, Tokyo 108-0075]
E-Mail1: [Keitarou.Kondou@jp.sony.com]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution on comment #42, #44 and #45 for HRCP-SC PHY in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #42, #44, #45]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment #42 and the resolution
CID | Page | Sub-clause | Line # | Comment | Proposed Change
42 | 96 | 11a.2.3.2.1 | 12 | Should the Frame Length field indicate the MAC frame length not excluding FCS? | Correct as needed
Accept and change the description as same as that used in the OOK part
Current
The Frame Length field shall be an unsigned integer equal to the number of octets in the MAC frame body of a regular frame, excluding the FCS.
Corrected
The Frame Length field shall be an unsigned integer equal to the number of octets in the MAC frame body including frame payload(s), MAC subheader(s) in the aggregated frames, and FCS(s), but not including the frame header and the preamble.

## Slide 3: Comment #44 and the resolution
CID | Page | Sub-clause | Line # | Comment | Proposed Change
44 | 99 | 11a.2.4.1 |  | Considering P2P communication with equal-basis transceivers, allowable EVM for a transmitter seems to be too strict. Referring to page 33 in IEEE802.15-15-0662-01-003e, target EVM balance between transmitter and receiver should be revisited. | Target EVM for a transmitter and a receiver has to be confirmed for deciding allowable EVM for a transmitter.
Accept, target EVM has been confirmed as below and no change is needed.
description
Eb/N0 is used at the graph on page 33 in IEEE802.15-15-0662-01-003e. Current values of EVM are derived from SNR* required for the criteria. In case of MCS3, where 16QAM and rate-14/15 LDPC used, threshold for frame-error rate of 8 % is 10.5 dB in Eb/N0 and 15.6 dB in SNR. SNR (dB) = Eb/N0 (dB) + 10*LOG10(number of coded bits per symbol)
The Number of coded per symbol is 4 * (14/15) * (56/64), which is 5.1 in dB, for MCS3 evaluation(the last factor comes from pilot insertion).
Current EVM value for MCS3 is –22 dB. If same amount of noise is assumed for both transmitter and receiver, noise level of the received signal shall be –19 dB. Then the margin shall be 3.4 dB and seems to be appropriate.
*SNR is defined here as the ratio averaged signal power to error power at the received signal.

## Slide 4: Comment #45 and the resolution
CID | Page | Sub-clause | Line # | Comment | Proposed Change
45 | 99 | 11a.2.4.1 |  | There are many possible situations where EVM will be measured via a build-in antenna at 60 GHz band. Proposals for measurement methods should be considered, either in this spec or in a separate conformance test plan. | Insert text as follows: when measuring EVM by capturing a transmit signal via an antenna, frequency response of the antenna can be compensated.
Revised. The current draft refers the measurement method defined at 15.3, but it’s not clear whether compensation for antenna response or not. A sentence will be added after the line 24 on page 99 as follows (underlined is added)
The EVM of a compliant transmitter shall be measured and calculated as defined in 11.1.7 and shall not 23 exceed the values given in Table 11-38 for the indicated mode. Note that this requirement assumes a conducted measurement.
- Description in 11.1.7 from line 22 on page 310 (15.3RevA-DF2)
The error vector measurement shall be made on baseband I and Q data after recovery through an ideal reference receiver system. An ideal receiver is a receiver that is capable of converting the transmitted signal into a stream of complex samples at sufficient rate or more, with sufficient accuracy in terms of I/Q arm amplitude and phase balance, DC offsets, and phase noise. It shall perform carrier lock, symbol timing recovery and amplitude adjustment while making the measurements.

## Slide 5: END