## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed resolution to technical comments assigned to ETRI-LB116
Date Submitted: Mar., 2016
Source: Sangjae Lee, Jaehwan Kim, Sangsung Choi (ETRI), Soo-Young Chang (SYCA), and Cheolho Shin (ETRI)
Company: ETRI, SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #116
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 3069
Commentor
  Stephen Chasko
Related clause
  5.2.5.1 P38 Line39
Comment
  This paragraph describes only a single channel mechanism. Is this protocol only meant for single channel environments; if so it must be more clearly explained in a dedicated section of the document
Proposed Change
  The document should include support for channel hopping and those sections which require single channel should be clearly identified.
Proposed Resolution
  Revise
  Replace "Multi channel operation" with "Multi PAN operation"
  State that each PAN works on single channel

## Slide 3: CID 3072
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.5.1 P38 Line41
Comment
  "each PAN coordinator uses two channels" is not accurate. The SPC operates on more channels
Proposed Change
  Replace with "each PAN coordinator, with the exception of the SPC, uses two channels
Proposed Resolution
  Revise
  Replace the sentence with "each PAN coordinator operates on its own channel, the channel of its parent PAN and the channel of its child PAN (if any)

## Slide 4: CID 3073
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.5.1 P38 Line43
Comment
  "The TMCTP superframe is bounded by the beacons sent by the super PAN coordinator (SPC)." does not seem accurate. In Figure 18, PAN ID 5 is not within the range of the SPC in PAN ID 1
Proposed Change
  Should "SPC" be "parent PAN coordinator"?
Proposed Resolution
  Revise
  Replace "SPC" with "parent PAN coordiator"

## Slide 5: CID 3076
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.5.1 P39 Line9
Comment
  The meaning of the "*" after a channel number is not described
Proposed Change
  Add a legend "x*: channel x allocated to a child PAN"
Proposed Resolution
  Accept

## Slide 6: CID 3080
Commentor
  Tero Kivinen
Related clause
  5.2.7.1 P41 Line47
Comment
  The PSN is sequence number which is allowed to roll over, and I assume the case where the PSN is smaller than the recorded PSN is trying to detect roll over, and clear the old entry in case of that situation. This creates discontinuation even when the nodes receive all P2P-RQ messages from the node, as immediately when the PSN rolls over the old values are ignored even when they might have been received very lately. Some kind of serial number arithmetic method would be better, as that would work nicely also while rolling over, i.e., similar than what RFC1982 describes.
Proposed Change
  I think it would be better to just say that for PSN we use serial number arithmetic and use comparisons defined there.
Proposed Resolution
  Revise
  PSN operation (purpose) is same as LSN. Keep using PSN is better.

## Slide 7: CID 3082
Commentor
  Tero Kivinen
Related clause
  5.2.7.1 P42 Line1
Comment
  This paragraph unconditionally forward the P2P-RQ IE frame if it is not the desired destination. I think it should not forward the frame if it has already forwarded before, i.e., if it receives it again. Hmm... actually it does not specify anywhere how the P2P-RQ frames are addressed, I had assumed they are broadcasts, but nothing here says so. So how does the node who is fowarding the frame know where to send it? In the figure it is clear that US and DS routing is NOT used, so what kind of routing is used for P2P-RQ messages?
Proposed Change
  Explain why the situation where node A receives P2P-RQ frame, forwards it to B, which then sends it back to A and so on, cannot happen, and how the node A knows where to forward the frame next.

## Slide 8: CID 3082
Proposed Resolution
  Revise
  Flooding range of the P2P-RQ can be controlled by using TTL in the P2P-RQ.
  Replace "by transmitting a P2P-RQ IE addressed accordingly and with the TTL field initialized to l2rDefaultTtl." with "by broadcasting a P2P-RQ IE addressed accordingly and with the TTL field initialized to l2rDefaultTtl." in 5.2.7 line 31
  State that a device should record the PSN and source address of the P2P-RQ IE. If the device receives another P2P-RQ IE with the same PSN and SA, the P2P-RQ IE should not be forwarded.
  The PSN and SA records should be deleted after l2rlsnsarecordtimeout.

## Slide 9: CID 3088
Commentor
  Don Sturek
Related clause
  5.2.7.2 P42 Line53
Comment
  If I am understanding P2P routing correctly, the Figure 21 is extremely misleading. Isn't P2P just a controlled flood where the intermediate devices accept and either forward or drop the forwarding messages to the destination? Certainly in that scenario while the P2P RP IE will look like wha tis shown the P2P RQ IE will not. It will go to nearly all devices until the cost is deemed higher than a better path.
Proposed Change
  Fix the diagram or explain why it is correct as shown
Proposed Resolution
  Revise
  Re-draw the figure with 6 node, indiacate the instruction step by step propagation of the P2P-RQ IE and the response P2P-RP IE.

## Slide 10: CID 3090
Commentor
  Verotiana Rabarijaona
Related clause
  5.2.7.1 P43 Line13
Comment
  "the PSN, the PQM value are set to the value retrieved from the corresponding fields in the IE." is not accurate. The PSN is retrieved from the IE but the PQM is the sum of the PQM is the IE and the last hop LQM.
Proposed Change
  Replace with "the PSN is set to the value retrieved from the corresponding field in the IE, the PQM value is set to the sum of the value of the PQM field and the LQM on the latest hop."
Proposed Resolution
  Accept

## Slide 11: CID 3100
Commentor
  Don Sturek
Related clause
  5.4.1.4 P49 Line52
Comment
  I never saw a procedure in P2P to record an alternate route. There must be some processing to record the best and a second best (and maybe more?). Where was that text?
Proposed Change
  Explain how the alternate P2P route is established.
Proposed Resolution
  Revise
  L2R dose not consider the alternative P2P route concept. Each device maintain only one path (next hop address) for a destination device. If the device receives duplicated P2P-RQ, then better route (by using metric) will be stored to P2P table.
  Replace the sentence "If the frame is being routed P2P, an alternative next hop may be selected if several paths to the desired destination are recorded." with "If the frame is being routed P2P, retransmission is attempted on the same path“
  Move "Neighbors whose address are recorded in the list of used neighbors described in 5.4.1.2 should not be considered in the selection of an alternative next hop for retransmission" before "if the frame is routed P2P".
  State that a single path should be recorded for each destination.

## Slide 12: CID 3112
Commentor
  Tero Kivinen
Related clause
  6.1.2.10 P64 Line48
Comment
  The 802.15.4-2015 expanded for example the coordinator realignment command to support 15-bit channel numbers. This channel number field is only 8-bit. Do we want to support larger channel numbers here too or is the 8-bits enough?
Proposed Change
  Make the channel number field 16-bit? If so then the length in figure 35 also needs to be updated.
Proposed Resolution
  Revise
  Make the channel number field 16 bit.

## Slide 13: CID 3121
Commentor
  Tero Kivinen
Related clause
  6.1.6 P70 Line44
Comment
  How does the receiver know to which mesh this belongs to, or more accurately whether the mesh root is 2 or 8 octet long? There is no mesh root address mode field in this IE, and our neighbor sending this and us might actually belong to two meshes and one of them might use short and other use extended addresses.
Proposed Change
  Add mesh root address mode field.
Proposed Resolution
  Accept