## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution of comment #12]
Date Submitted: [13 March 2016]
Source: [Kiyoshi Toshimitsu and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 shibaura, Minato-ku, Tokyo 108-8001]
E-Mail1: [kiyoshi.toshimitsu@toshiba.co.jp, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution for comment #12 in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #12]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and resolution
Page | Sub-clause | Line # |  | Proposed Change
34 | 6.3.1 | 28 | IE length in beacon may be insufficient to transport higher-layer info. | Expand IE in beacon to add more information
Comment #12
Resolution
In Sec.7.16, change Table 7-7b as following:
Parameter | Values
pNAccessSlot | 1-6
pDAccessSlot | 6.5us(pMaxAssocReqCommandTime + SIFS)
pMaxFrameBodySize | 2099200 octets
pMaxBeaconLengthTime | 84 ms
pMaxAssocReqCommandTime | 84 ms

## Slide 3
Long Preamble
FCS
(4 oct)
Beacon payload (15 oct + IE)
Association Req (13 oct + IE)
Stuff bits
2.33 us
MCS0, w/PW =2.2587Gbps
Max. 0.98 us
When pMaxBeaconLengthTime and pMaxAssocReqCommandTime equals to 4.0us, IE length in Beacon and association Request command is only 257 byte.
Regarding CID16, the length of PHY long preamble may become 3.35us. 4.0us( current value of pMaxBeaconLengthTime and pMaxAssocReqCommandTime ) is insufficient to send Beacon payload because the sum of Long Preamble length(3.35us) and Frame Header length(0.69us) become more than 4.0us.
Header-FEC encoded (PHY Header, MAC Header,HCS)
0.69 us
Short Preamble 1.89 us
Frame Header
Max. 4.0 us
Current Beacon and Association Request command length

## Slide 4
Long Preamble
FCS
(4 oct)
Beacon payload (15 oct + IE)
Association Req (13 oct + IE)
Stuff bits
3.35 us
MCS0, w/PW =2.2587Gbps
Max. 3.96 us
Header-FEC encoded (PHY Header, MAC Header,HCS)
0.69 us
Frame Header
Max. 8.0 us
Proposed Beacon and Association Request command length
Maximum IE length becomes 1099byte in Beacon and 1101byte in Association Request command.

## Slide 5: END