## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution of comment #32]
Date Submitted: [13 March 2016]
Source: [Kiyoshi Toshimitsu1, Keiji Akiyama and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 shibaura, Minato-ku, Tokyo 108-8001]
E-Mail: [kiyoshi.toshimitsu@toshiba.co.jp, Keiji.Akiyama@jp.sony.com, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution of comment #32 in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #32]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and resolution
Page | Sub-clause | Line # |  | Proposed Change
24 | 5.3 |  | There are places where actual parameters are either specified or not specified. There are also SAPs such as those for data transmission/reception which are not specified. If specifications are not necessary and parameters can be added with no restrictions during implementation, then there are no issues, but the SAPs should be re-examined. | Please specify all parameters and SAPs or explain why the definition is not needed.
Comment #32

## Slide 3
Change section 5.3.2.1 as follows:
5.3.2.1 MLME-SCAN.request
Change the first paragraph of 5.3.2.1 as shown:
This primitive is used to initiate the passive scan procedures to search for either a specific PNPP or any PNPP. The semantics of this primitive are:
MLME-SCAN.request (
ScanForBSID,
BSIDLength,
BSID,
ScanForPNPID,
PNPID,
ScanForPNPCAddress,
PNPCAddress,
Timeout
)
The primitive parameters are defined in Table 5-5.
Resolution for MLME

## Slide 4
Replace section 5.3.3 as follows:
5.3.3 Starting a PNPP
These primitives support the process of creating a new PNPP with the DEV acting as PNCC, as described in 7.2.2. The parameters used for these primitives are defined in Table 5-8.

## Slide 5
Name | Type | Valid range | Description
BSIDLength | Integer | As defined in 6.4.2 | The number of octets in the BSID.
BSID | Octet string | As defined in 6.4.2 | The BSID of the new PNPP
SECMode | Enumeration | MODE_0, MODE_1 | The security mode of the PNPP, as described in 6.3.1.
DEVID | Integer | Any valid DEVID as defined in 6.2.3 | The assigned DEVID for the DEV that is acting as the PNC, as described in 7.2.2. This parameter is not valid for HRCP DEVs.
MinDepSuperframePercent | Integer | 1–100 | The minimum percent of the superframe requested as a CTA for the dependent piconet, as described in 7.2.7 and 7.2.8. This parameter is not valid for HRCP DEVs.
Table 5-8—MLME-START primitive parameters
Change the Table 5-8 as follows:

## Slide 6
DesiredDepSuperframePercent | Integer | 1–100 | The desired percent of the superframe requested as a CTA for the dependent piconet, as described in 7.2.7 and 7.2.8. This parameter is not valid for HRCP DEVs.
AllocatedSuperframePercent | Integer | 0–100 | The percent of the superframe allocated to the new dependent piconet. If the channel time request was rejected, the value shall be set to zero. This parameter is ignored if the DEV is starting an independent piconet. This parameter is not valid for HRCP DEVs.

## Slide 7
ResultCode | Enumeration | SUCCESS, FAILURE | Indicates the result of the MLME request.
ReasonCode | Enumeration | NOT_PNC_CAPABLE, NO_CHANNELS_AVAILABLE, ALREADY_PNC, OTHER | Indicates the reason for a ResultCode of FAILURE
PHYMode | Enumeration | 2.4_GHZ, SC_MMWAVE, HSI_MMWAVE, AV_MMWAVE ,HRCP SC PHY, HRCP OOK PHY | The PHY that will be used for the beacons and the CP(s) in the PNPP that will be started.

## Slide 8
Replace section 5.3.3.1 as following
5.3.3.1 MLME-START.request
This primitive is used to start a PNPP. If the DEV is not a member of the PNPP, this primitive causes the DEV to start an independent piconet or P2Plink. If the DEV is a member of the piconet, this primitive causes the DEV to start a child piconet. If the DEV is associated as a neighbor member of a piconet, this primitive causes the DEV to start a neighbor piconet. The semantics of this primitive are:

## Slide 9
Change section 5.3.5.1 as following
5.3.5.1 MLME-ASSOCIATE.request
This primitive initiates the association procedure. The semantics of this primitive are:
MLME-ASSOCIATE.request (
BSIDLength,
BSID,
PNPID,
PNPCAddress,
ChannelIndex,
NeighborPiconetRequest,
PiconetPNPPServicesInquiry,
HRCP DEV Capability,
Timeout
)
The primitive parameters are defined in Table 5-10.

## Slide 10
Change section 5.3.5.2 as follows:
5.3.5.2 MLME-ASSOCIATE.confirm
This primitive reports the result of the association procedure. The semantics of this primitive are:
MLME-ASSOCIATE.confirm (
DEVID,
VendorSpecificIE,
HRCP pair Capability
ResultCode,
ReasonCode
)
The primitive parameters are defined in Table 5-10.

## Slide 11
      Change section 5.3.5.3 as follows:
      5.3.5.3 MLME-ASSOCIATE.indication
Change the first sentence of 5.3.5.3 as follows:
This primitive is used to indicate that a new non-HRCP DEV has associated with the same piconet as this DEV or a new HRCP DEV has associated with this HRCP DEV.
Change the title of 5.3.6 and change the subsequent text as shown:
MLME-ASSOCIATE.indication (
DEVID,
DEVAddress,
HRCP pair Capability
)

## Slide 12
Replace Table 5-30 as follows:
Resolution for MAC-SAP
Table 5-30—Summary of MAC SAP primitives
Name | Request | Confirm | Indication | Response
MAC-ASYNC-DATA | 5.5.1 | 5.5.2 | 5.5.3 | -
MAC-ISOCH-DATA | 5.5.4 | 5.5.5 | 5.5.6 | -
MAC-HRCP-DATA | 5.5.7 | 5.5.8 | 5.5.9 | -

## Slide 13
Add following line at the end of Table 5-31 (refer resolution for CID33)
Name | Type | Valid range | Description
LogicalChannel | Enumeration | CH0,CH1 | LogicalChannel value is available for use by the Higher Layer Protocol User and therefore out of scope from this specification.

## Slide 14
Add section 5.5.7 to 5.5.9 as follows:
5.5.7 MAC-HRCP-DATA.request
This primitive is used to initiate the transfer of an MSDU from one MAC entity to another MAC entity or entities using HRCP PHY. The semantics of this primitive are:
MAC-ASYNC-DATA.request (
RequestID,
LogicalChannel,
ACKRequested,
ConfirmRequested,
Length,
Data
)
The primitive parameters are defined in Table 5-31.

## Slide 15
5.5.8 MAC-HRCP-DATA.confirm
This primitive is used to report the result of a request to transfer an asynchronous MSDU from one MAC entity to another MAC entity or entities. This primitive is only generated if the ConfirmRequested parameter in the MAC-ASYNC-DATA.request with the same RequestID value is ALWAYS or is ON_ERROR and the ResultCode is FAILURE. The semantics of this primitive are:
MAC-ASYNC-DATA.confirm (
RequestID,
TransmitDelay,
ResultCode,
ReasonCode
)
The primitive parameters are defined in Table 5-31.

## Slide 16
5.5.9 MAC-HRCP-DATA.indication
This primitive is used to indicate the reception of an asynchronous MSDU. The semantics of this primitive are:
MAC-ASYNC-DATA.indication(
Length,
Data
)
The primitive parameters are defined in Table 5-31.

## Slide 17: END