## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed resolution to MIMO CES]
Date Submitted: [20 April 2016]
Source: [Ken Hiraga(1), Jae Seung Lee, Itaru Maekawa, Keitarou Kondou, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [NTT1, ETRI, JRC, Sony, Toshiba]
Address1: [Hirarinooka 1-1, Yokosuka Japan]
E-Mail1: [hiraga.ken@lab.ntt.co.jp (all contributors are listed in “Contributors” slide)]
Abstract: This document is a proposal for comment resolution to MIMO channel estimation sequences (CES) specification.
Purpose: To propose comment resolution to CID#1 and #7 in LB114.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee@etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee@etri.re.kr
Itaru Maekawa | Japan Radio Corporation | maekawa.itaru@jrc.co.jp
Lee Doohwan | NTT Corporation | lee.doohwan@lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken@lab.ntt.co.jp
Hideki Toshinaga | NTT Corporation | toshinaga.hideki@lab.ntt.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou@jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura@jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa@jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi@toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu@toshiba.co.jp

## Slide 3
Proposed resolution to CID #7
on MIMO CES
CID | Page | Sub-clause | Line # | Comment | Proposed Change | E/T | Must Be Satisfied? | Resolution Stats
7 | 107 | 11a.2.8.5.3 11a.2.8.5.4 | 1~21 | BPSK-modulated Ga128 signal leads to division by zero when frequency-domain equalization (as mentioned in line 8) is applied at the receiver. | Correct the MIMO CES sequence as needed. Change Figure 11a-13 if necessary. | T | Yes | Accepted

## Slide 4: Introduction
Proposed resolution is to prepare two types of MIMO CES
  Option 1: Golay sequences a256 in the frequency domain
    New 11a.2.8.5.3
  Option 2: Golay sequences in the time domain
    New 11a.2.8.5.4
Resolution to CID#7: Golay a256 in the frequency domain -> IFT -> time domain waveform -> CSD.
As another option for MIMO CES, we here propose one for channel estimation using correlator in time domain.

## Slide 5: Option #1 MIMO CES for frequency domain channel estimation
a128
–a128
a128
a128
CES
SYNC
SFD
Proposed preamble structure
for MIMO stream#i
Frequency domain
Time domain waveform
Cyclic shifts of 16*(i-1) [symbols] for #i th stream (i=1,2,3,...,16)
5 times repetitions
IFT[ a256 ]
IFFT
a256 = [a128 b128]
IFT[ a256 ] with cyclic shift
Pi/2-BPSK modulated signal
1280
Time domain waveform

## Slide 6: Option #2 MIMO CES for time domain channel estimation using correlator
a128
–a128
a128
b128
a128
–b128
a128
b128
–a128
b128
a128
a128
CES
SYNC
a512
b512
b128
SFD
a128
b128
SISO CES in draft 1.0
Cyclic shifts of 16*(i-1) [symbols] for #i th stream (i=1,2,3,...,16)
a128
–a128
a128
a128
CES
SYNC
SFD
Proposed preamble structure
for MIMO stream#i
c1024
c1024_i
d_i_256
c1024: a512b512
c1024_i: cyclic shifted c1024
d_i_256: First 256 digits of c1024_i
e_i_256: Last 256 digits of c1024_i
e_i_256
c1024_i
Append d_i_256, and prepend e_i_256
c1024_i
d_i_256
e_i_256
This CES has 256-symbol ZCC zone
Divide 16 streams with cyclic shift.

## Slide 7: To indicate MIMO CES Type...
Also, in order to indicate MIMO CES type (option #1 or #2), we propose to add 1 bit , the “MIMO CES Type,” for MIMO IE in the beacon frame.

## Slide 8
11a.2.8.5 MIMO PHY Preamble
The Preamble is comprised of the SYNC, SFD and CES as shown in Figure 11a-13.
After SFD transmission each antenna sends CES by turns. In other words, when one antenna transmits the CES, other antennas transmit unmodulated RF signals. As the figure shows, total time for CES transmission is in proportion to M.
MIMO PHY assumed the implementation using frequency domain equalization (FDE). When M = 16, CES of Tx#9 ~Tx#16 are transmitted after the CES of Tx#1~Tx#8.
MIMO CES should be one shown in 11a.2.8.5.3 or one shown in 11a.2.8.5.4. The type of MIMO CES is advertised by the beacon, as shown in 6.4.37.
Proposed change in “11a.2.8.5 MIMO PHY Preamble”
This is editorial fix, resolution to CID#1. The highlighted sentence does not correctly describe the CES formation shown in Figure 11a-13 and in 11a.2.8.5.3 and 11a.3.8.5.4.
Change the text in 11a.2.8.5 as follows.
Payload #i
CES# i
Tx#i(i = 1 ~ 16)
SYNC# i
SFD# i
Header # i
Replace Figure 11a-13 with the following figure
Figure 11a-13 —PHY frame structure in MIMO mode

## Slide 9: Proposed change in 11a.2.8.5.3
11a.2.8.5.3 CES for frequency domain channel estimation
The CES for frequency domain channel estimation is generated using Golay complementary sequences of length 256, a256 ,which is defined in 11a.2.3.1.3.
First the sequence is π/2-shift-BPSK-modulated signal in the frequency domain. Then the signal is converted into time domain waveform. For each spatial stream, cyclic shift delays are applied in time domain.
The value of cyclic shift delay for ith transmitter TCSces_i is
TCSces_i = 128* ( i – 1 ) [chips] when M = 2
TCSces_i = 64* ( i – 1 ) [chips] when M = 4
TCSces_i = 28* ( i – 1 ) [chips] when M = 9
TCSces_i = 16* (i – 1 ) [chips] when M = 16.
Finally 5 times repetition is applied to each stream.
Replace 11a.2.8.5.3 with this.

## Slide 10: Proposed change in 11a.2.8.5.4
11a.2.8.5.4 CES for time domain channel estimation
CES for ith stream, which transmitted from ith transmitter is [e_i_256 c1024_i d_i_256], where
c1024_i: shifted c1024
c1024: [a512b512]
d_i_256: First 256 digits of c1024_i
e_i_256: Last 256 digits of c1024_i
Here a512 and b512 is defined in 11a.2.3.1.3. The sequence c1024_i is cyclic-shifted c1024. The value of the cyclic shift delay for ith transmitter TCSces_i is shown in 11a.2.8.5.3.
Replace 11a.2.8.5.4 with this.

## Slide 11: Proposed change in “6.4.37 MIMO Information IE”
Bits: b0-b3 | b4-b7 | b8-b12 | b13-b1415 | b15
SC Supported MIMO | Number of MIMO Array Training | Number of MIMO Array Training | Array Training Interval | MIMO CES Type
Modify Figure Table 6-21a as follows.
Figure 6-126b— MIMO Parameter field format
Modify Figure 6-126b as follows.
b13-b1415 | Array Training Interval Time
000 | 10 ms
001 | 20 ms
010 | 40 ms
011 | 80 ms
100-111 | Reserved
Table 6-21a—Array Training Interval field values
Insert following sentence after Table 6-21a.
The MIMO CES Type field shall be set to 1 when MIMO CES for frequency domain channel estimation which is described in 11a.2.8.5.3, and shall be set to 0 when MIMO CES for time domain channel estimation which is described 11a.2.8.5.4.