## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution on comment #27]
Date Submitted: [13 March 2016]
Source: [Kiyoshi Toshimitsu and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 shibaura, Minato-ku, Tokyo 108-8001]
E-Mail1: [kiyoshi.toshimitsu@toshiba.co.jp, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution on comment #27 in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #27]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and the resolution
Page | Sub-clause | Line # |  | Proposed Change
56 | 7.3a.1 | 2 | (1) For PPC, what is the behavior when ACK is not received after sending an Association Response? (2) For DEV, what is the behavior when ACK is not received after sending an ACK to PPC in reply to an Association Response? | (1) PPC should change the state to Asynchronous phase and resend Association Response after a RIFS period. (2) DEV should change the state to Asynchronous phase and resend ACK after a RIFS period.
Comment #27

## Slide 3
Resolution
In Sec.7.3a.1, insert the text at the end of last sentence as following:
The HRCP PNC determines that the association procedure has completed when either it receives: a) a Stk-ACK in response to the Association Response command, or b) a data frame from its associated DEV. The DEV that receives an Association Response command from the HRCP PNC determines that the association procedure has completed when it transmits a Stk-ACK in response to the Association Response command.
When a Stk-ACK is not received after sending an Association Response, the HRCP PNC should change the state to Asynchronous phase and retry after a RIFS period, as shown Figure 7-Xa and 7-Xb.
For the case Figure 7-Xc, the DEV sends the last correctly received sequence number to the HRCP PNC, since the DEV could only read the MAC header of the last frame. The HRCP PNC then transmits the same Association Response again.

## Slide 4
PPC
DEV
Association
Resp.(SN=0)
DEV does not receive Association Resp.
(MAC Header Error)
RIFS
Stk-
ACK
Last Received
Sequence Number = 0x3FF
Stk-
ACK
SIFS
SIFS
Last Received
Sequence Number = 0x3FF
Association
Resp.(SN=0)
(Error)
retransmission
Figure 7-X-a --
Figure 7-X-b
PPC
DEV
Association
Resp. (SN=0)
Stk-
ACK
DEV received Association Resp.
But, PPC does not receive Stk-ACK (MAC Header Error).
RIFS
Stk-
ACK
Last Received
Sequence Number = 0x3FF
Last Received
Sequence Number = 0
Stk-
ACK
SIFS
SIFS
Last Received
Sequence Number = 0
Data
SIFS
(Error)

## Slide 5
PPC
DEV
Association
Resp.(SN=0)
DEV does not receive Association Resp.
(MAC Header is correct)
Stk-
ACK
Last Received
Sequence Number = 0x3FF
SIFS
SIFS
Association
Resp.(SN=0)
retransmission
Figure 7-X-c
(Error)

## Slide 6: END