## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution on comment #27]
Date Submitted: [25 May 2016]
Source: [Kiyoshi Toshimitsu and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 Shibaura, Minato-ku, Tokyo 108-8001]
E-Mail1: [kiyoshi.toshimitsu@toshiba.co.jp, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution on comment #27 in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #27]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and the resolution
Page | Sub-clause | Line # |  | Proposed Change
56 | 7.3a.1 | 2 | (1) For PPC, what is the behavior when ACK is not received after sending an Association Response? (2) For DEV, what is the behavior when ACK is not received after sending an ACK to PPC in reply to an Association Response? | (1) PPC should change the state to Asynchronous phase and resend Association Response after a RIFS period. (2) DEV should change the state to Asynchronous phase and resend ACK after a RIFS period.
Comment #27 and 1067

## Slide 3
Resolution
In Sec.7.3a.1, insert the text at the end of last sentence as follows:
The HRCP PNC determines that the association procedure has completed when it either receives: a) a Stk-ACK in response to the Association Response, as shown in Figure 7-20b,
or b) a data frame from an already-approved DEV, as shown in Figure 7-20c. The DEV that receives an Association Response from the HRCP PNC determines that the association procedure has completed and transmits a Stk-ACK in response to the Association Response.
When a Stk-ACK or data frame is not received by the HRCP PNC after sending an Association Response, the HRCP PNC should change the state to Asynchronous phase, and resend the Association Response after a RIFS period, as shown Figure 7-20d and 7-20e.
For the case of Figure 7-20f, the DEV sends the last correctly received sequence number to the HRCP PNC, since the DEV could only read the MAC header of the last frame. The HRCP PNC then transmits the same Association Response again.

## Slide 4
Figure 7-20b - DEV receives Association Response from the HRCP PNC correctly
HRCP
PNC
DEV
Association
Resp. (SN=0)
Stk-
ACK
Last Received
Sequence Number = 0
Data
SIFS
SIFS

## Slide 5
Figure 7-20c - DEV receives Association Response correctly, but HRCP PNC does not receive Stk-ACK.
HRCP
PNC
DEV
Association
Resp. (SN=0)
Stk-
ACK
RIFS
Stk-
ACK
Last Received
Sequence Number = 0
Data
SIFS
Last Received Sequence Number
is incremented = 0
By receiving data, PNC deduces
that DEV has correctly received
Association Response even though
the Stk-ACK did not arrive.
SIFS
(Error)
PNC sends Stk-ACK after waiting one RIFS.
Last Received Sequence stays at  0

## Slide 6
HRCP
PNC
DEV
Association
Resp.(SN=0)
RIFS
Stk-
ACK
PNC sends Stk-ACK. Last Received Sequence Number is not incremented  0
Stk-
ACK
SIFS
SIFS
Last Received Sequence Number
is not incremented  0x3FF
Association
Resp.(SN=0)
(Error)
retransmit
Figure 7-20d - DEV receives Association Response correctly, but HRCP PNC does not receive Stk-ACK (MAC Header Error).
Figure 7-20e - DEV receives Association Response correctly, but
HRCP PNC does not receive Stk-ACK (MAC Header Error).
HRCP
PNC
DEV
Association
Resp. (SN=0)
Stk-
ACK
RIFS
Stk-
ACK
Last Received
Sequence Number = 0
Stk-
ACK
SIFS
SIFS
Last Received Sequence Number
is incremented = 0
Data
SIFS
(Error)
PNC sends Stk-ACK. Last Received Sequence Number is not incremented  0

## Slide 7
HRCP
PNC
DEV
Association
Resp.(SN=0)
Stk-
ACK
Last Received Sequence Number
is not incremented  0x3FF
SIFS
SIFS
Association
Resp.(SN=0)
retransmit
Figure 7-20f - DEV does not receive Association Response, but does receive the MAC Header part correctly.
(Partial Error)

## Slide 8: END