## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution of comment #27]
Date Submitted: [25 May 2016]
Source: [Kiyoshi Toshimitsu and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 Shibaura, Minato-ku, Tokyo 108-8001]
E-Mail1: [kiyoshi.toshimitsu@toshiba.co.jp, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution of comment #27 in 15-16-0162-01-003e-lb114-consolidated-comments and 15-16-0371-02-003e-lb119-consolidated-comments.]
Purpose: [Resolving comments #27 and #1067]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and the resolution
Page | Sub-clause | Line # |  | Proposed Change
56 | 7.3a.1 | 2 | (1) For PPC, what is the behavior when ACK is not received after sending an Association Response? (2) For DEV, what is the behavior when ACK is not received after sending an ACK to PPC in reply to an Association Response? | (1) PPC should change the state to Asynchronous phase and resend Association Response after a RIFS period. (2) DEV should change the state to Asynchronous phase and resend ACK after a RIFS period.
Comment #27 and 1067

## Slide 3
Resolution (1)
In 7.3a.1, insert the text at the end of last sentence:
The HRCP PNC determines that the association procedure has completed when it either receives: a) a Stk-ACK in response to the Association Response, as shown in Figure 7-20b,
or b) a data frame from the DEV, as shown in Figure 7-20c. The DEV that receives an Association Response from the HRCP PNC determines that the association procedure has completed and transmits a Stk-ACK in response to the Association Response.
When a Stk-ACK or data frame is not received by the HRCP PNC after it sends an Association Response, the HRCP PNC should change the state to Asynchronous phase, and resend the Association Response after a RIFS period, as shown Figure 7-20d and 7-20e.
For the case of Figure 7-20f, the DEV sends the last correctly received sequence number to the HRCP PNC, since the DEV could only read the MAC header of the last frame. The HRCP PNC then transmits the same Association Response again. The Last Received Sequence Number shall be initialized to 0x3FF.

## Slide 4
Resolution (2)
Change the title of 4.3.1.1 and insert the following new paragraph at the end of 4.3.1.1:
A DEV that is capable of acting as the HRCP PNC starts the pairnet by initializing the Sequence Number and Last Received Sequence Number and by sending the beacon in the default channel. The default channel is defined in 11a.1.4. The HRCP PNC needs not make sure of the availability of the channel. The DEV shall initialize the Sequence Number and Last Received Sequence Number before sending an Association Request.

## Slide 5
Resolution (3)
In 6.3.4a.1, after the fifth paragraph, insert a new paragraph:
This number is initialized at the time of starting a pairnet. Both command and data sequence numbers shall start with a value of 0x000.
In 6.2.10, at the end of the fourth paragraph, insert a new sentence:
This number is initialized to 0x3FF at the time of starting a pairnet.

## Slide 6
Figure 7-20b
HRCP
PNC
DEV
Association
Resp. (SN=0)
Stk-
ACK
DEV receives Association Response from HRCP PNC correctly
Last Received
Sequence Number = 0
Data
SIFS
SIFS
(Sequence Number Type = data)
At the end of 7.3a.1, insert the following five figures (7-20c, 7-20d, 7-20e, 7-20f):

## Slide 7
Figure 7-20c
HRCP
PNC
DEV
Association
Resp. (SN=0)
Stk-
ACK
RIFS
Stk-
ACK
Last Received
Sequence Number = 0
Data
SIFS
Last Received Sequence Number = 0
(Sequence Number Type = data)
By receiving data, PNC deduces
that DEV has correctly received
Association Response even though
the Stk-ACK did not arrive.
SIFS
(Error)
DEV receives Association Response correctly, but
HRCP PNC does not receive Stk-ACK.
PNC sends Stk-ACK after waiting one RIFS.
Last Received Sequence Number = 0
(from the Association Request)

## Slide 8
HRCP
PNC
DEV
Association
Resp.(SN=0)
DEV does not receive Association Response,
due to MAC Header Error.
RIFS
Stk-
ACK
PNC sends Stk-ACK. Last Received Sequence
Number is not incremented and stays at 0
Stk-
ACK
SIFS
SIFS
Last Received Sequence Number
is set to 0x3FF (no packet has been
received yet by the DEV)
Association
Resp.(SN=0)
(Error)
retransmit
Figure 7-20d

## Slide 9
Figure 7-20e
HRCP
PNC
DEV
Association
Resp. (SN=0)
Stk-
ACK
DEV receives Association Response correctly,
But HRCP PNC does not receive Stk-ACK
(MAC Header Error).
RIFS
Stk-
ACK
Last Received
Sequence Number = 0
Stk-
ACK
SIFS
SIFS
Last Received Sequence Number = 0
Data
SIFS
(Error)
PNC sends Stk-ACK.
Last Received Sequence
Number stays at 0
(Sequence Number
Type = data)

## Slide 10
HRCP
PNC
DEV
Association
Resp. (SN=0)
DEV does not receive the entire Association Response,
but does receive the MAC Header section correctly.
Stk-
ACK
Last Received Sequence Number
is set to 0x3FF (no packet has been
received yet by the DEV)
SIFS
SIFS
Association
Resp. (SN=0)
retransmit
Figure 7-20f
(Partial Error)

## Slide 11: END