## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ULP TASK Performance Evaluation
Date Submitted: May 19, 2015
Source: [Kiran Bynam], [Chandrashekhar Thejaswi PS], [Jinesh Nair]
        [Youngsoo Kim], [Changsoon Park], [Young-Jun Hong]
Abstract: This presentation presents the recently published 15.4q (Ultra Low Power). It describes the benefits of the TASK-PHY and performance evaluation
Purpose: This presentation is to provide an analysis of the TG4q TASK PHY
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contents
Introduction
  Requirements
  TASK PHY features and benefits
  Power consumption Figures
Performance Evaluation
  Comparison between BT LE and 802.15.4q TASK
  Comparison between the 802.15.4 and 802.15.4q TASK
Summary

## Slide 3: Application Requirements
Market Sector | Data Rate (Kbps) | Range (m) | Number of Nodes | Reliability | Form Factor | Duty Cycle | Payload Size | Mobility | Battery Life
Smart Utility (Gas/Water) | 100 | 30 | 1000s | High | -- | Low | Small | No | Years
Building Automation | 1000 | 30 | 100s | High | S, M | Mid | Mid | No | Years
Medical / Health Care | 1000 | 10 | 10s | High | Small | High | Small-Mid | Yes | Days-Mos
Retail Service | 100 | 30 | 100s | High | Small | Mid-High | Mid-Large | Yes | Years
Telecom Service | 1000 | 10 | 10s | High | Small | High | Mid-Large | Yes | Days
Industrial Monitoring | 100 | 100 | 100s | High | -- | Mid-High | Small-Mid | No | Years
Environment Monitoring | 100 | 100 | 100s | High | -- | Low | Small | No | Years
Energy-Harvesting Sensor | 100 | 10 | 10s | Low | -- | Low | Small | -- | Years
Smart Active Label | 100 | 30 | 1000s | High | Small | Low | Small | Yes | Days-Mos
Shelf Label/ Inventory Tracking | 1000 | 30 | 1000s | High | Small | Low | Mid-Large | - | Months-years

## Slide 4: Technical Requirements
In addition to 802.15.4 requirements, following were added to technical guidance document
  Less than 15 mW Power consumption
  Range of 30 m to be demonstrated in AWGN environment

## Slide 5: TASK PHY
TASK PHY block diagram & description
Data rates support
Preamble description
Dual RX mode support: coherent & non-coherent

## Slide 6: TASK PHY Block Diagram and Data Rates
MCS Identifier | Modulation format | Coding format | Chip rate (Mcps) | M (Bits/data symbol) | L (Chips/ data symbol) | Code rate | Data rate (kbps)
0 | 1/1-TASK | BCH | 1 | 1 | 1 | 51/63 | 809.52
1 | 2/4-TASK | BCH with interleaving | 1 | 2 | 4 | 51/63 | 404.76
2 | 3/8-TASK | BCH with interleaving | 1 | 3 | 8 | 51/63 | 303.57
3 | 5/32-TASK | BCH with interleaving | 1 | 5 | 32 | 51/63 | 126.48

## Slide 7
  Best suited for non-coherent mode of operation
  enables low power implementation at the receivers
  decodable simultaneously at the coherent receiver also.
  Spreading to enable robustness, data rate scalability and low-complex designs.
  Spreading sequences with good correlation properties:
  sequences with good correlation properties both in coherent (with ternary alphabet) and non-coherent (unipolar binary) modes.
  performance similar to the best-known sequences in the respective domains. (W-H codes in coherent mode and OOC in non-coherent mode)
  Benefits at the transmitter:
  Low power consumption due to duty-cycling
  Low complexity implementation.
  Benefits at the receiver:
  Non-coherent receiver
  based on Super-regenerative reception (SRR) principle
  eliminates need of mixers, and the demodulation is based on simple envelope detection.
  2. Reduction in power consumption due to duty-cycling.
Benefits of TASK Modulation

## Slide 8: Power Consumption
TX Component | Power (µW) @ -5 dBm
Power Amplifier | 3640
VCO | 1070
Frequency Synthesizer | 1850
Digital Baseband | 380
Total | 6940
RX Component | Power (µW)
LNA+SRO | 638
ED+VGA | 33
ADC (8 bit) | 7.5
Frequency Synthesizer | 1850
Digital Baseband | 1050
Total | 3578.5
Total Power consumption less than 5 mW for Receiver
Total Power consumption of transmitter less than 7 mW @ -5 dBm EIRP

## Slide 9: Comparison between BT LE and IEEE 802.15.4q TASK

## Slide 10: Energy Analysis Overall Approach
Protocol for transmission of a single packet from sensor to node is analyzed for BT LE and 802.15.4q TASK
  A generic Power Consumption Model is derived
Power Consumption Tables for BT LE and 802.15.4q TASK are presented for various states
Energy Utility Models derived for BT LE and 802.15.4q TASK from the generic power consumption model
  Model capturing Energy Utility (bits/Joule) as a function of number transmission bytes
  Includes impact of connection establishment
  Multiple packet transmission
Performance comparison results
  Energy Utility vs number of transmission bytes
  Application Scenario comparisons

## Slide 11: Bluetooth Low Energy: TI CC2541 Current Waveform
Reference: Texas Instruments Application Note, “Measuring Bluetooth Low Energy Power Consumption”, 2012.
Wake-up
Pre-processing
Pre-RX
RX Active
RX-to-TX
TX Active
Post-processing
Pre-sleep
Sleeping
Sleeping
Spike from voltage regulator wake-up

## Slide 12: Bluetooth Low Energy: Acknowledged Transmission
Minimum Data Frame Interval 756 us
TX/RX Turnaround Time
150 us
Inter-Frame Spacing
150 us
Maximum
Payload Size
27 Byte
Packet
Overhead
8+12 Byte
ACK Size
8+2 Byte
ACK Frame
Data Frame
Data Frame
Throughput 285.7 kbps
PHY Overhead: 8 Byte
MAC Overhead: 12 Byte
Data: 27 Byte
ACK: 2 Byte
PHY Overhead: 8 Byte
MAC Overhead: 12 Byte
Data: 27 Byte

## Slide 13: 802.15.4 - MAC: Overview
Active Period
  Divided into 16 equal slots of duration
  =60 symbols = 960
Contention Access Period (CAP)
  The minimum CAP duration is
  CSMA/CA in CAP is implemented using units of time called Back Off Period =
  Beginning of the back-off period of each node is aligned with beginning of the beacon transmission
Contention Free Period (CFP)
  Assigned by the PAN coordinator for latency critical applications
  Using contiguous guaranteed time slots (GTS)
  The number of GTS can vary from 0 to 7

## Slide 14: 802.15.4 - MAC: Overview
Brief working
  NB: number of times CSMA/CA was required to back-off while attempting current transmission
  CW: Number of back-off periods that need to be clear of channel activity before transmission can start
  BE: is the back off exponent related to the maximum number of back-off periods that a node will wait before attempting to access the channel
Parameter | Range | Default
 | 3 to 8 | 5
 | 0 to | 3
 | 0 to 5 | 4
Parameter | Range | Default
 | 3 to 8 | 5
 |  | 3
 | 0 to 5 | 4

## Slide 15: Average Time for Channel Access
Example to get R=2.5,
(found by experimentation)

## Slide 16: 802.15.4 - MAC: Acknowledged Transmission
Minimum Data Frame Interval 5440 us
TX/RX Turnaround Time
192 us
Inter-Frame Spacing
640 us
Maximum
Payload Size
118 Byte
Packet
Overhead
6+9 Byte
ACK Size
6+5 Byte
ACK Frame
Data Frame
Data Frame
Throughput 173.5 kbps
PHY Overhead: 6 Byte
MAC Overhead: 9 Byte
Data: 118 Byte
PHY Overhead: 6 Byte
MAC Overhead: 9 Byte
Data: 118 Byte
ACK: 5 Byte

## Slide 17: Generic Power Consumption Model
Receiver
Transmitter
Data Frame
ACK Frame
Pre-processing
Post-processing
Pre-RX
Wake-up
Pre-sleep
RX-TX
Assumption: C1 = 10960 [cycle] (340 us @ 32 MHz)
C1 [cycle] / clock frequency [Hz]
C2 [cycle] / clock frequency [Hz] + C3 [us/Byte] * MSDU [Byte]
Assumption: C2 = 12800 [cycle], C3 = 32 [us/Byte] (1280 us @ 32 MHz, 27 Byte)
Processor Bounded Task
Processor Bounded Task
Memory Bounded Task
Data Frame
ACK Frame
Pre-processing
Post-processing
Pre-TX
Wake-up
Pre-sleep
TX-RX
C2 [cycle]/ clock frequency [Hz] + C3 [us/Byte] * MSDU [Byte]
Processor Bounded Task
Memory Bounded Task
C1 [cycle] / clock frequency [Hz]
Processor Bounded Task

## Slide 18
 |  | Current [mA]
State 9 | Sleep | 0.001
Modified from Reference: Texas Instruments Application Note, “Measuring Bluetooth Low Energy Power Consumption”, 2012.
BT LE Power Model: Transmitter
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 400 | 21.6 | 
State 2 | Pre-processing | 1280 | 26.64 | Fixed for a fixed payload size
State 3 | Pre-TX | 80 | 39.6 | 
State 4 | TX Active | 376 | 63 | 
State 5 | TX-to-RX | 105 | 26.64 | 
State 6 | RX Active | 80 | 63 | 
State 7 | Post-processing | 340 | 26.64 | Fixed for a fixed payload size
State 8 | Pre-Sleep | 160 | 14.76 | 
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 400 | 21.6 | 
State 2 | Pre-processing | 1280 | 26.64 | Fixed for a fixed payload size
State 3 | Pre-TX | 80 | 39.6 | 
State 4 | TX Active | 376 | 63 | 
State 5 | TX-to-RX | 105 | 26.64 | 
State 6 | RX Active | 80 | 63 | 
State 7 | Post-processing | 340 | 26.64 | Fixed for a fixed payload size
State 8 | Pre-Sleep | 160 | 14.76 | 
Data Frame: 376 us (20+27B)
ACK Frame: 80 us (10B)

## Slide 19: BT LE Power Model: Receiver
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 400 | 21.6 | 
State 2 | Pre-processing | 340 | 26.64 | Fixed for a fixed payload size
State 3 | Pre-RX | 80 | 39.6 | 
State 4 | RX Active | 376 | 63 | 
State 5 | RX-to-TX | 105 | 26.64 | 
State 6 | TX Active | 80 | 63 | 
State 7 | Post-processing | 1280 | 26.64 | Fixed for a fixed payload size
State 8 | Pre-Sleep | 160 | 14.76 | 
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 400 | 21.6 | 
State 2 | Pre-processing | 340 | 26.64 | Fixed for a fixed payload size
State 3 | Pre-RX | 80 | 39.6 | 
State 4 | RX Active | 376 | 63 | 
State 5 | RX-to-TX | 105 | 26.64 | 
State 6 | TX Active | 80 | 63 | 
State 7 | Post-processing | 1280 | 26.64 | Fixed for a fixed payload size
State 8 | Pre-Sleep | 160 | 14.76 | 
 |  | Current [mA]
State 9 | Sleep | 0.001
Data Frame: 376 us (20+27B)
ACK Frame: 80 us (10B)
Modified from Reference: Texas Instruments Application Note, “Measuring Bluetooth Low Energy Power Consumption”, 2012.

## Slide 20: IEEE 802.15.4q TASK Power Model: Transmitter
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 10 | 0.77 | 
State 2 | Pre-processing | 4202.6 | 7.5 | 
State 3 | Pre-TX | 96 | 10.02 | 
State 4 | TX Active | variable | 14.5 | 
State 5 | TX-to-RX | 192 | 7.5 | 
State 6 | RX Active | variable | 9.5 | 
State 7 | Post-processing | 365.3 | 7.5 | 
State 8 | Pre-Sleep | 10 | 0.77 | 
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 10 | 0.77 | 
State 2 | Pre-processing | 4202.6 | 7.5 | 
State 3 | Pre-TX | 96 | 10.02 | 
State 4 | TX Active | variable | 14.5 | 
State 5 | TX-to-RX | 192 | 7.5 | 
State 6 | RX Active | variable | 9.5 | 
State 7 | Post-processing | 365.3 | 7.5 | 
State 8 | Pre-Sleep | 10 | 0.77 | 
 |  | Current [mA]
State 9 | Sleep | 0.001
MCU 30 MHz
MSDU 118 B

## Slide 21: IEEE 802.15.4q TASK Power Model: Receiver
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 10 | 0.77 | 
State 2 | Pre-processing | 365.3 | 7.5 | 
State 3 | Pre-RX | 96 | 8.22 | 
State 4 | RX Active | variable | 9.5 | 
State 5 | RX-to-TX | 192 | 7.5 | 
State 6 | TX Active | variable | 14.5 | 
State 7 | Post-processing | 4202.6 | 7.5 | 
State 8 | Pre-Sleep | 10 | 0.77 | 
 |  | Time [us] | Power [mW] | Remark
State 1 | Wake-up | 10 | 0.77 | 
State 2 | Pre-processing | 365.3 | 7.5 | 
State 3 | Pre-RX | 96 | 8.22 | 
State 4 | RX Active | variable | 9.5 | 
State 5 | RX-to-TX | 192 | 7.5 | 
State 6 | TX Active | variable | 14.5 | 
State 7 | Post-processing | 4202.6 | 7.5 | 
State 8 | Pre-Sleep | 10 | 0.77 | 
 |  | Current [mA]
State 9 | Sleep | 0.001
MCU 30 MHz
MSDU 118 B

## Slide 22: BT LE: MAC Mechanism
Connection Establishment
Scanner
Advertiser
ADV
ADV
CON_REQ
EVENT_1
ACK
EVENT_1
EVENT_2
EVENT_3
ACK
ACK
ACK
Connected Communication
Scanner/Master
Advertiser/Slave

## Slide 23: BT LE: Energy Model for Point to Point Link
Non-Connected communication
Energy consumed by master
      , power consumption while scanning
      , advertisement interval
Energy consumed by Slave
      , Energy consumed by a single advertisement interval
      scanning duty cycle (Probability that the master finds the slave)
Better models available, but this basic model is adopted.

## Slide 24: BT LE: Energy Model for Point to Point Link
The communication of packets from the sensor to the node is considered
wake-up energy, Pre-processing energy, Pre-transmission energy
Post processing energy, Pre-sleep energy
+
is the number of packets transmitted, , , Length of Phy and Mac headers, =27 bytes,
is the energy associated with the change to go from transmit to receive modes,
Connected communication

## Slide 25: 802.15.4 - MAC: MAC Mechanism and Energy Model for Beacon Enabled Mode (Uplink)
Uplink (Direct) Communication
Coordinator
Beacon
Data
(CAP/GTS)
Device
ACK (Optional)
Energy Consumption at the Device
wake-up energy, Pre-processing energy, Pre-transmission energy, Post processing energy, Pre-sleep energy
(case of GTS,
is the number of packets transmitted, is the energy associated with the change to go from transmit to receive mode, , , Length of MAC headers and duration of PHY headers, payload bytes,

## Slide 26: 802.15.4 - MAC: MAC Mechanism and Energy Model for Beacon Enabled Mode (Downlink)
Downlink (Indirect) Communication:
Coordinator
Beacon
DATA_REQ
(CAP)
Device
ACK
Data
CAP/GTS
ACK
Energy Consumption of Device
Energy Consumption of Coordinator
(In case of GTS,
= Wake up energy, = Pre-processing energy, = Post-processing energy
=Energy associated with channel access in CAP, Transmitter Power, Receiver Power
, Transmitter and receiver time in seconds/byte, , is length in bytes for Data, Ack, beacon packets

## Slide 27: Performance Comparisons
Energy utility as a function of packet data size for 802.15.4q TASK and BT LE
Based on active power consumption, the energy utility of 802.15.4q TASK is far superior
Energy utility as a function of packet data size for 802.15.4q TASK PHY: D0, D1, D2, D3
For data beyond 127 bytes, multi-packet transmission and single packet of sizes beyond 127 packets are considered.
Parameter | Value
Number of retransmissions | 1
Multi-rate PHY modes | D0: 1/1-TASK, D1: 2/4-TASK, D2: 3/8-TASK, D3: 5/32-TASK BT LE: 1 Mbps
Size of packets | [1-256] bytes

## Slide 28: Performance comparisons : CAP and GTS
As expected marginal gains are observed with GTS as
Parameter | Value
Number of retransmissions | 1
Multi-rate PHY modes | D0: 1/1-TASK, D1: 2/4-TASK, D2: 3/8-TASK, D3: 5/32-TASK BT LE: 1 Mbps
Size of packets | [1-256] bytes

## Slide 29: Application Scenarios: CAP and GTS
Applications | Packet Size (Bytes) | Packets/Sec/device | Data Rate (kbps) | Mode
ECG | 127 | 4 | 4.064 | CFP
Accelerometer | 127 | 8 | 8.128 | CFP
Humidity | 16 | 2 | 0.256 | CAP
Temperature | 16 | 1 | 0.128 | CAP
Applications | Energy Utility per packet () [kbytes/Joule/packet] |  |  |  | 
 | IEEE 802.15.4q TASK |  |  |  | BT LE
 | D0 | D1 | D2 | D3 | 
ECG | 1800 | 1360 | 1160 | 647.9 | 442
Accelerometer | 1800 | 1360 | 1160 | 647.9 | 442
Humidity | 521.7 | 421.1 | 372.9 | 227.6 | 150
Temperature | 521.7 | 421.1 | 372.9 | 227.6 | 150
Total | 4650 | 3550 | 3070 | 1750 | 1180
Applications |  |  |  |  | 
 | IEEE 802.15.4q TASK |  |  |  | BT LE
 | D0 | D1 | D2 | D3 | 
ECG | 1800 | 1360 | 1160 | 647.9 | 442
Accelerometer | 1800 | 1360 | 1160 | 647.9 | 442
Humidity | 521.7 | 421.1 | 372.9 | 227.6 | 150
Temperature | 521.7 | 421.1 | 372.9 | 227.6 | 150
Total | 4650 | 3550 | 3070 | 1750 | 1180
Chart: 
| D0 | D1 | D2 | D3 | BLE
ECG | 1802.2 | 1355.1 | 1162.8 | 647.959 | 441.6471
Accelerometer | 1802.2 | 1355.1 | 1162.8 | 647.959 | 441.6471
Humidity | 521.768 | 421.1 | 372.91 | 227.678 | 150.0336
Temperature | 521.768 | 421.1 | 372.91 | 227.678 | 150.0336
Total | 4648 | 3553.7 | 3071.4 | 1751.2 | 1183.4
Energy utility per packet
[kByte/J/packet]

## Slide 30: Application Scenarios (with CAP and GTS)
Applications | Energy Utility per second = [kbytes/Joule/s] |  |  |  | 
 | IEEE 802.15.4q TASK |  |  |  | BT LE
 | D0 | D1 | D2 | D3 | 
ECG | 7.21E+03 | 5.42E+03 | 4.65E+03 | 2591.8 | 1.77E+03
Accelerometer | 1.44E+04 | 1.08E+04 | 9.30E+03 | 5184 | 3.53E+03
Humidity | 1043.5 | 842 | 745.8 | 443.2 | 300.1
Temperature | 521.768 | 421 | 372.92 | 227.618 | 150.063
Total | 2.32E+04 | 1.75E+04 | 1.51E+04 | 8.44E+03 | 5.75E+03
Applications |  |  |  |  | 
 | IEEE 802.15.4q TASK |  |  |  | BT LE
 | D0 | D1 | D2 | D3 | 
ECG | 7.21E+03 | 5.42E+03 | 4.65E+03 | 2591.8 | 1.77E+03
Accelerometer | 1.44E+04 | 1.08E+04 | 9.30E+03 | 5184 | 3.53E+03
Humidity | 1043.5 | 842 | 745.8 | 443.2 | 300.1
Temperature | 521.768 | 421 | 372.92 | 227.618 | 150.063
Total | 2.32E+04 | 1.75E+04 | 1.51E+04 | 8.44E+03 | 5.75E+03
Chart: 
| D0 | D1 | D2 | D3 | BLE
ECG | 7208.8 | 5420.4 | 4651.2 | 2591.8 | 1766.6
Accelerometer | 14418 | 10841 | 9302 | 5184 | 3533
Humidity | 1043.5 | 842 | 745.8 | 443.2 | 300.1
Temperature | 521.768 | 421 | 372.92 | 227.6178 | 150.063
Total | 23192 | 17524 | 15072 | 8440.04 | 5749.9
kByte/J/sec

## Slide 31: Summary
BT LE and 802.15.4q TASK power models are derived
  Energy utilization based on the active power consumption
  Power consumption figures are obtained from paper, TI-CC-2541 and ULP prototypes
  802.15.4q applicable for multiple rates
  Sensor to master data transfer considered
Results for BT LE and 802.15.4q TASK are compared
  Energy utilization of IEEE 802.15.4q TASK is more superior than BT LE for higher data rates
  There is a value in extending packet sizes beyond 127 bytes to 255 bytes

## Slide 32: Comparison of IEEE 802.15.4 and 802.15.4q TASK – OPNET simulation

## Slide 33: IEEE 802.15.4q TASK: Protocol Stack
New IEEE 802.15.4q TASK can support the legacy combination of IEEE 802.15.4b MAC and ZigBee stack.
IEEE 802.15.4q TASK PHY
IEEE 802.15.4b MAC
Application
ECG (Ectrocardiography)
PPG (Photoplethysmography)
IMP (Body Impedance)

## Slide 34: Using Variable Data Rate: Rate Adaptation
Simple open loop Rate Adaptation algorithm is used for efficient usage of multi-rate IEEE 802.15.4q TASK
  -SNR is stepped up/down based on the success/failure of the given packet
is used for choosing the rate based on the PER tables of the multiple data rates

## Slide 35: RA algorithm: OPNET Simulation
Simulation Assumptions
  TX Power for 15.4 OQPSK is 10 mW
  RX Power for 15.4 OQPSK is 20 mW
  TX Power for 15.4q TASK is 10 mW
  RX Power for 15.4q TASK is 5 mW
  EIRP for all sensors is -10 dBm
  EIRP of coordinator is 0 dBm
  Single tap, Pedestrian channel at 3 kmph is observed.
  Various packet sizes from 30 to 120 bytes considered
  Number of nodes in network varied between 1 , 4 and 8 for CAP mode
  Simulation done for BO-4 and SO-4

## Slide 36: Results of RA algorithm for GTS
Chart: TX ON Energy comparison
| 30 bytes/1 packet | 30 bytes/4 packet | 60 bytes/2 packet | 120 bytes/1 packet
IEEE 802.15.4 | 0.00031667 | 0.0011111 | 0.0016667 | 0.00094444
TASK PHY | 0.00022222 | 0.00077778 | 0.00083333 | 0.00038889
Chart: RX ON Energy comparison
| 30 bytes/1 packet | 30 bytes/4 packet | 60 bytes/2 packet | 120 bytes/1 packet
IEEE 802.15.4 | 0.00083333 | 0.0012222 | 0.0012222 | 0.00066667
TASK PHY | 0.00055556 | 0.00083333 | 0.00066667 | 0.00044444
Receiver Energy comprises mainly of Beacon and ACK components.
Transmitter Energy comprises of actual transmitted packets.
Gain in TX energy is mainly due to use of Rate adaptation and RX Energy is mainly due to ULP front end (SRR).
Power
[watt]
Power
[watt]

## Slide 37: Results of RA algorithm for CAP
Chart: TX ON energy comparison
| 30 bytes/1 packet/1 node | 30 bytes/1 packet/ 8 node | 30 bytes/4 packet/1 node | 60 bytes/2 packet/8 node
IEEE 802.15.4 | 0.00033333 | 0.01 | 0.00032222 | 0.01
TASK PHY | 0.00021111 | 0.00044444 | 0.00021667 | 0.0005
Chart: CCA Energy comparison
| 30 bytes/1 packet/1 node | 30 bytes/1 packet/ 8 node | 30 bytes/4 packet/1 node | 60 bytes/2 packet/8 node
IEEE 802.15.4 | 0.00033333 | 0.0013889 | 0.00033333 | 0.00055556
TASK PHY | 0.00011111 | 0.00044444 | 0.00011111 | 0.00016667
Chart: RX ON energy comparison
| 30 bytes/1 packet/1 node | 30 bytes/1 packet/ 8 node | 30 bytes/4 packet/1 node
IEEE 802.15.4 | 0.00061111 | 0.00094444 | 0.00088889
TASK PHY | 0.00033333 | 0.00088889 | 0.00072222
Observations
CAP energy consumption is very high when number of nodes is increased in the network
RA algorithm with multiple rate reduces the congestion by taking advantage of higher rate when encountering good SNR
Power
[watt]
Power
[watt]
Power
[watt]

## Slide 38: Mobile Health Care Application
Node description | Number of nodes | Packet Size (Bytes) | Packets/Sec/device | Data Rate (kbps) | Mode | Total packets/3minute
ECG | 3 | 127 | 4 | 4.064 | CFP | ~1900
Accelerometer | 2 | 127 | 8 | 8.128 | CFP | ~2500
Humidity, Temperature, | 2 | 16 | 2 | 0.256 | CAP | ~500
PPG | 1 | 127 | 3 | 3.048 | CFP | ~650
Practical application of mobile health is simulated
Assumptions for simulation are same
Coordinator is placed in Mobile interacting with several health monitoring sensors
All the above applications are run for 3 minutes for benchmarking energy consumption

## Slide 39: Results of Mobile Health Care Application
RX Active Time and Energy comparison
TX Active Time and Energy comparison
RX gain is mainly originated from ULP front-end (4 times)
TX gain is mainly originated from Rate Adaptation (2 times)

## Slide 40: Summary
Demonstrate more than 100% of active energy efficiency improvement by 802.15.4q TASK with Rate Adaptation
CCA being impacted and gaining by 4 times by using multi rate 802.15.4q TASK in efficiency , less retransmissions and non-coherent receivers
TX Energy gains mainly due to decreased retransmissions and RX Energy gains are obtained by using ULP transceiver