## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Reference receiver sensitivity levels modification ]
Date Submitted: [29 August 2016]
Source: [Jun Kobayashi] Company [Japan Radio Co., Ltd.]
Address [Mitaka, Tokyo, Japan]
Voice: [+81.422.45.9228], E-Mail: [ kobayashi.jun@jrc.co.jp]
Abstract: [This document presents reference receiver sensitivity levels modification for TG3e.]
Purpose: [Reference receiver sensitivity levels modification – CID.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Modified reference receiver sensitivity levels for TG3e are presented.
Relaxation of the reference receiver sensitivity has great potential for module size and power consumption.
  Lower gain antennas can provide small size module.
  Power consumption of low noise amplifier and power amplifier can be decreased.
Summary

## Slide 3
The receiver sensitivity and system NF can be expressed as equation (1) and (2) .
MCS identifier | Current Receiver Sensitivity (dBm) | Current Required System NF (dB) | Proposed Receiver Sensitivity (dBm) | Proposed Required System NF (dB)
0 | – 66 | 5.5 | -61 | 10.5
1 | – 63 | 5.5 | -58 | 10.5
2 | – 60 | 5.5 | -55 | 10.5
3 | – 56 | 5.5 | -51 | 10.5
4 | – 54 | 5.5 | -49 | 10.5
5 | – 50 | 5.5 | -45 | 10.5
6 | – 44 | 5.5 | -39 | 10.5
* Antenna Gain=5 dBi, Implementation Loss=4 dB, BW=1.76 GHz, Receiver NF=10 dB
Table.1 Current and Proposed Receiver Sensitivity
Current and Proposed Receiver Sensitivity

## Slide 4
Link Budget for Device to Device on Far Field Communication
Parameters | Value
MCS identifier | 3
Antenna Gain [dBi] | 5
Tx power [dBm] | -5
Required SNR [dB] | 21
BW [GHz] | 1.76
Receiver NF [dB] | 10
Implementation Loss [dB] | 4
Maximum Transmission Distance=9cm
Fig.1 Block Diagram of Link Budget
Table.2 Parameter List
Fig.2 Received Power and Sensitivity

## Slide 5
END