## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Localisation review for TG12 ULI]
Date Submitted: [13 September 2016]
Source: [Billy Verso] Company [Decawave Ltd.]
Address [Peter Street, Dublin 8, Ireland]
Voice:[+353.87.233.7323], E-Mail:[billy.verso @ decawave.com]
Re: [Examination of location awareness functionality for TG12]
Abstract: [Review and discuss the mechanisms for location awareness for TG12 ULI]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: The aim of this presentation:
Begin to look at the question:
  How does localization fit into the 802.15.12 ULI specification?
    two-way ranging, localization, location awareness, RFID, TDOA, AOA, etc
Methodology:
  Examine localisation use cases, types and localization algorithms
  Look at some example location focused (i.e. RTLS) network topologies
  Consider the current 802.15.12 Functional Decomposition
Prompt the group to have a discussion about
  what ULI functionality should be defined to facilitate localization support
  and what sort of SAPs are needed for this

## Slide 3: Localization use cases
Typical methods, architectures and use cases employed in location aware networks and real-time location systems
  Static nodes measure distance between neighbors and “system” figures out the relative location of all participating nodes, typical use case is as an installation aid for commissioning
    Alarm system, smoke detectors, lighting units, etc
  More usual RTLS use case has fixed known position “anchor” nodes defining an infrastructure via which system locates the mobile “tag” nodes
    Two-way ranging to selected anchors, TDOA of a asset tag blink frame, AOA of frame, or, a combination of methods
  Navigation case: mobile node computes its location w.r.t. the anchor nodes
    Two-way ranging, reverse TDOA of anchor messages (like an indoor GPS), AOA, or, a combination of methods
  No fixed infrastructure case where mobile nodes measure distance, (and maybe angle), between to each other to figure out their relative location
    First responders, fire fighters, etc.
    This is essentially the first static case above, but repeated periodically

## Slide 4: Measurement types and localization algorithms
Range / distance between nodes
  Coarse estimate from RSSI (nearly every PHY can support at some level)
  Accurate results from two-way ranging based on PHY (eg HRP UWB PHY) ability to timestamp frame TX and RX and calculate the time of flight (TOF)
  A single range measurement can give proximity measurement, perhaps for safety applications, access control, etc.
  Use multiple range / distance results from fixed nodes to a mobile node can infer its location via multilateration
    network can locate mobile device or unknown location (fixed) node
    navigation mode mobile device figures it position by solving distance to N known fixed nodes

## Slide 5: Measurement types and localization algorithms
Angle-of-arrival (AOA)
  LRP UWB PHY added AOA reporting to MCPS-DATA primitives
  Possible to support with HRP UWB PHY and some others perhaps
  Depends on including an antenna array and receiving at both with double receivers able to determine angle based on different time or signal phases
  Use multiple AOA measurements
    two or more fixed nodes measure AOA of message from mobile node and figure out its locations
    fixed nodes send periodic messages, mobile node measures AOA to each fixed node and figures out its own location

## Slide 6: Measurement types and localization algorithms
Time Difference of Arrival (TDOA)
  Time of arrival measured at three or more fixed known position nodes can be used to locate the sender
  Requires that the RX timestamps TOA have a common time-base so that the TDOA can be used to infer mobile node location via multilateration
    can be achieved via a wired clock distribution
    can be achieved via wireless means, i.e. timestamped messages between fixed nodes used to track their relative clock offset and drift to correct TOA to common time-base for TDOA multilateration
Reverse TDOA “indoor GPS”
  Time of arrival of messages from fixed nodes can be used by mobile node to figure out its own location
  Requires that send time of messages is known with respect to a common (synchronised) time base among the infrastructure nodes

## Slide 7: Measurement types and localization algorithms
Combination methods
  Use two-way ranging with angle to locate a device with respect to fixed known location device
    a range and a bearing define a location, i.e. in polar coordinates
  TDOA with AOA measurement
    Extra information of AOA helps resolving / reducing errors
  Ranging to one (or two nodes), TDOA for others, etc.
  Mixture of AOA, TDOA, TWR etc
    Complex solving algorithms can take all information into account to estimate the most probable location of the mobile device to be located

## Slide 8
Single-sided TWR makes a one round trip measurement
Device B must send its Treply time to device A to allow it to calculate the TOF
Single-sided TWR has error coming from the clock timing errors of the devices measuring Tround and Treply
With shorter messages and higher precision clock sources the ranging errors may be acceptable for some application needs
1 ns ≈ 1 foot or 30 cm.
Single-sided two-way ranging
Typical errors in SS-TWR time-of-flight estimation

## Slide 9
Double-sided two-way ranging
  DS-TWR removes the clock offset error experienced by SS-TWR
  Device A must send its Tround1 and Treply2 times to device B to allow it to calculate the TOF
  The general formula above supports asymmetric response times which can be useful for multi-node ranging schemes
Double-Sided TWR with 3 messages
Double-Sided TWR with 4 messages
General formula for time of flight (TOF) is:

## Slide 10: Facilities to support localization algorithms
MAC/PHY capability to accurately timestamp frame transmissions and receptions and report these to the upper layers along with device addresses to identify the nodes involved
MAC/PHY capability to report an angle-of-arrival (AOA) of a received frame along with senders addresses to identify the node
Facility to combine TX/RX timestamps from local and remote node to compute a time-of-flight (TOF)
  Consider defining IEs to communicate the timestamps
Facility to route relevant data across the network to a “solver” that can use the data to estimate the device’s location
  e.g. device IDs, TOFs, TX & RX timestamps, AOA data, RSSI etc.
For TDOA, facility in anchor or solver application to use TX and RX timestamps to track relative clock drift between anchors
  The alternative is hardware clock distribution/synchronisation of anchor infrastructure

## Slide 11
RTLS network architecture
with IP LAN backhaul to location solver

## Slide 12
RTLS network architecture
with 802.15.4 network backhaul to location solver

## Slide 13
Adding location to a 802.15.4 network

## Slide 14
Adding location to a 802.15.4 network
TX & RX timestamps or TOF results are routed to a Solver, in a network node or external as shown here.

## Slide 15
802.15.12 Functional Decomposition
* Base figure comes from the TG12 closing report of the July 2016 meeting in San Diego, CA.
TX and RX timestamps
AOA information
RSSI
Perform ranging TOF
calculation
Send relevant data to Solver application
Solver
Location solving application
(local or remote)
LOCATING FUNCTIONS
Notes: September 16
Page 15

## Slide 16
DISCUSSION ?