## Slide 1
802.15 Projects: Summary Overview
February 2016
Bob Heile
Chair, IEEE 802.15
Chair, IEEE 2030.5
Co-Chair IEEE P2030 Smartgrid Communications Task Force
Director of Standards, Wi-SUN Alliance

## Slide 2: Disclaimer…
“At lectures, symposia, seminars, or educational courses, an individual presenting information on IEEE standards shall make it clear that his or her views should be considered the personal views of that individual rather than the formal position, explanation, or interpretation of the IEEE.”
IEEE-SA Standards Board Operation Manual (subclause 5.9.3)
Notes: 2
11/10/2016

## Slide 3: IEEE 802 Organization
Standards Activities Board
IEEE Standards Association
802.3
CSMA/CD
Ethernet
802.24
Smart Grid
TAG
802.11
Wireless
WLAN
802.15
Wireless
Specialty
Networks
802.21
Media
Independent
Handoff
802.19
Co-existence
WG
Sponsor
IEEE 802
Local and Metropolitan Area Networks
(LMSC)
Sponsor
Sponsor
Sponsor
802.18
Radio
Regulatory
TAG
802.16
Wireless
Broadband
Access
802.22
Wireless
Regional
Area
Networks
802.1
Higher
Layer
LAN
Protocols
Privacy
Study
Group
Voting Members ~102
www.ieee802.org/15
OmniRan

## Slide 4: 802.15 Scope and Purpose
Initial activities focused on wearable devices hence “personal area networks”
Activities have proven to be much more diverse and varied
  Data rates from 2kbps to 2gbs
  Ranges from millimeters to kilometers
  Frequencies from 100MHz to 800THz
Today’s focus is on “specialty”, typically short range, communications.
If it is wireless and not a LAN, MAN, RAN, or WAN, odds are its 802.15
Only 802 Working Group with multiple MACs

## Slide 5: 802.15 Completed Projects
802.15.1-Original Bluetooth
802.15.2-Coexistence Recommended Practice Bluetooth/802.11
802.15.3-High Rate (55 Mbps) Multimedia WPAN
  15.3 amendments:
  802.15.3c-High Rate (>1Gbps) mmWave 15.3 PHY
802.15.3-2016 recasts standard to use 48bit MAC addresses and rolled up amendment c.
802.15.4-Low Rate (250kbps). Energy Efficient WPAN for WSN type applications
  15.4 amendments:
  802.15.4a-Higher data rate 15.4 UWB PHY

## Slide 6: 802.15 Completed Projects
  802.15.4 Amendments (cont):
  802.15.4c-Sub 1 GHz 15.4 PHY for China
  802.15.4d-Sub 1 GHz 15.4 PHY for Japan
  802.15.4e- 15.4 MAC Enhancements (GTS among others)
  802.15.4f- 15.4 PHY for Active RFID
  802.15.4g- 15.4 PHY for Field Area Smart Utility Networks
  802.15.4-2011: 15.4 Roll-up to include 15.4a,c & d
  802.15.4j- 15.4 PHY using US dedicated medical band
  802.15.4k- 15.4 PHY for Low Energy Critical Infrastructure Monitoring
  802.15.4m- 15.4 PHY for operation in TV White Spaces
  802.15.4n- 15.4 PHY for Chinese Medical Applications
  802.15.4p- 15.4 PHY for Rail Communications and Control
  802.15.4q- Ultra Low Power 15.4 PHY
  802.15.4u- 865-867MHz band in India

## Slide 7: 802.15 Completed Projects
802.15.4-2015 RevisionC (bug fixes and roll-up of amendments e,f,g,j,k,m, and p)
802.15.5-Mesh Networking Recommended Practice
802.15.6- Body Area Networking for medical and entertainment applications
802.15.7- Visible Light Communications using structured lighting
802.15.9 – Key Mgmt Protocol for 15.4
802.15.10 – Layer 2 Routing for 15.4

## Slide 8: 802.15 Active Projects/Status
IEEE802.15.3 Amendments:
  802.15.3d THz band 100Gb/s PHY layer for point to point data center applications
    STATUS: reviewing proposals, writing draft
  802.15.3e High Rate (100Gb/s), Close Proximity Communications using mmWave for 4k HD MPEG file transfers in <250ms total transaction time
    STATUS: in Sponsor Ballot- almost complete

## Slide 9: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects:
  802.15.4r- Common 15.4 ranging protocol for Location Based Services indoors or out
    STATUS: on hold
  802.15.4s- MAC enhancement for improved spectrum resource utilization
    STATUS: In Working Group Letter Ballot
  802.15.4t Higher Rate Phy (HRP): PHY capable of 2 Mb/s data rates, utilizing the 2.4 GHz ISM band, having backwards-compatibility to, and the same occupied bandwidth as, the present 2.4 GHz O-QPSK PHY, and be simple to implement.
    STATUS: Final stages of Sponsor Ballot

## Slide 10: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects (cont):
  802.15.4v Regional Sub 1GHz Band (RSB):
    Define 15.4 PHY clause changes to use 870-876 MHz & 915-921 MHz bands in Europe, 902-928 MHz band in Mexico, 902-907.5 MHz & 915-928 MHz bands in Brazil, 915-928 MHz band in Australia/New Zealand that are not in 15.4-2015
    Update the channel parameters for the 470-510 MHz band in China and the 863-870 MHz band in Europe to align them with current requirements.
      STATUS: Seeking Project approval at March 802 Plenary

## Slide 11: 802.15 Active Projects/Status (cont)
Revision to IEEE802.15.7 -2012, Standard for Visible Light Communications.
  Extend spectral range to include near UV & near IR
  Rename to “Optical Wireless Communications”
  Add capability to specifically to address Optical Camera Communications for use with existing as well as future smart mobile devices
    STATUS: Near to completing a ballotable draft
802.15.8 Peer Aware Communications (PAC)
  Standard for Infrastructure-less Peer Aware Communications among Mobile Devices
    STATUS: In Working Group Letter Ballot

## Slide 12: 802.15 Active Projects/Status (cont)
802.15.12 Upper Layer Interface (ULI) for 15.4:
    STATUS: Developing required content and priotities
  Project Goals:
  Make IEEE 802.15.4 easier to use, like 802.11 and 802.3
  Enable the use of many of the higher layer protocol stacks used by 802.11 and 802.3 without changes
  Allow 15.4 to address new applications, yet maintain backward compatibility with existing devices and applications
  Potentially consolidate L2R, KMP, 6T,& 6lowpan in one ULI
  Will need tight coordination with 802.1 and IETF

## Slide 13: What IEEE 802.15.12 does
  Gives 15.4 devices the ability to add DLL (layer 2) protocols with standard interfaces and primitives, in a modular manner
  Includes EtherType and Dispatch IDs allowing 15.4 to support multiple higher layer stacks or applications simultaneously
  Allows configuration of the 802.15.4 MAC/PHY for proper operation in a standardized manner making applications simpler,
  Includes fragmentation support (6LowPan) allowing 802.15.4 to transport large packets
  Includes L2R (IEEE 802.15.10) and KMP (IEEE 802.15.9) as optional functions to yield mesh and key management, and
  Includes the ability to interface to standardized network monitoring applications, in a fashion similar to IEEE 802.11

## Slide 14: How IEEE 802.15.12 operates
The 15.12 standard complements the 15.4 standard by fulfilling the tasks that 802.15.4 assigns to higher layers:
  The management protocol block can provide configuration settings for starting up networks, and joining networks
  802.15.12 can optimally configure the 802.15.4 MAC and PHY for proper operation in a standardized manner
The 802.15.12 standard supplements the 802.15.4 standard by introducing capabilities that other MAC/PHYs usually have:
  Configuration settings for global regulatory environments
  Ability to differentiate applications and stacks using EtherType and Dispatch IDs
  Ability to fragment and reassemble larger packets

## Slide 15: IEEE 802.15.12 protocol stack model as of the Warsaw meeting

## Slide 16: 802.15 Active Project Status
802.15 Interest Groups:
  Dependability IG (IG DEP): seeking to identify non implementation based strategies, which could be standardized, that inherently improve wireless link reliability.
  High Rate Rail Communications IG (HRRC)
  THz IG: Review and discuss the latest advances for using THz bands for wireless date applications
  LPWA: Low Power Wide Area (see next slide)

## Slide 17: 802.15 LPWA Interest Group
Motivation:
LPWANs are interesting networks for many applications
A variety of proprietary and non-IEEE 802 standards are appearing
The full suitability of existing IEEE802 standards for LPWANs is not clear
Existing standards may offer significant room for improvements
The 3GPP community is very focused on the development of LPWAN standards

## Slide 18: 802.15 LPWA Interest Group
Potential standards candidates include:
  For license-exempt bands:
    IEEE 802.15.4k / g
    SIGFOX
    LoRaWAN
    ETSI LTN, Weightless, IEEE 802.11ah
    ...
  For licensed bands:
    3GPP standards, e.g. NB-IoT (Narrow Band IoT)
    ...

## Slide 19: IEEE802.15 Action Plan
Decision to establish an Interest Group to evaluate existing IEEE802 standards, specifically:
Create usage scenarios for license-exempt bands
Create suitable channel and interference models
Investigate performance of existing standards

## Slide 20: 802.15 Other Activity
Joint efforts with IETF:
802.15 IETF Standing Committee -formed to support collaboration and coordination of 802.15 activities/positions with IETF, specifically 6Tisch, LP-WAN, and 802.15.12
Approaches to support 15.12
Projects for the IEEE/ ISO/IEC PSDO process
802.15.3-2016 High Rate Wireless Multimedia Networks
  STATUS: Responding to comments prior to final ballot
802.15.4-2015 -Status: in review by JTC1 SC6
802.15.6 Body Area Networking
  STATUS: in review by JTC1 SC6

## Slide 21: Questions? Bob Heile, Chair IEEE 802.15 bheile@ieee.org www.ieee802.org/15