## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ULI “Profile” for Protocol Management]
Date Submitted: [17 JAN 2017]
Source: [H Yokota] Company [Landis + Gyr]
Address [Add address Street, City, PC, Province/State, Country]
Voice:[Add telephone number], FAX: [Add FAX number], E-Mail:[Add e-mail address]
Re: [If this is a proposed revision, cite the original document.]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: [Description of document contents.]
Purpose: [Description of what the author wants P802.15 to do with the information in the document.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ULI “Profile” for Protocol Management
Values of ULI
  Simpler interface to the MAC that reduces the number of API calls by combining existing MLME into something easier to use
  Common interface to other IEEE802 families (LLC-like function)
  Yang modeling can be used for this
Challenge
  Mapping between layers or different 802 specs is not so simple…
Proposal
  Define a “ULI Profile”, which is a set of parameters or commands to simply access
Use cases for ULI Profile
  Use case 1: one-shot MAC/PHY configuration
  Use case 2: 802.x <-> 802.y protocol translation
  Use case 3: MAC/PHY configuration by higher layer applications

## Slide 3: ULI Profile identification and operation primitives
Scope of profile ID
  Local ID
  global ID (standardized)
Type of operations
  ULM-CREATE-PROFILE()
  ULM-EXEC-PROFILE()
  ULM-GET-PROFILE()
  ULM-CHANGE-PROFILE()
  ULM-DELETE-PROFILE()

## Slide 4: Use case 1: one-shot MAC/PHY configuration
Simplifies parameter settings
ULI profile ID=0x01
“Configuration profile #1”
Parameter | Value
MAC Parameters | 
Device Type | FFD
PAN | discovery
Operation mode | TSCH-BE
Channel Hopping | 
PHY Parameters | 
Modulation type | FSK
FCS | 4
Data rate | 100
Transmit power | 20mW
ULI profile ID=0x02
“Configuration profile #2”
Parameter | Value
MAC Parameters | 
Device Type | FFD
PAN | Set-up
Operation mode | Generic-BE
PHY Parameters | 
Modulation type | OFDM
FCS | 4
Data rate | 800
Transmit Power | 600mW
Use case 1

## Slide 5: Configuring a set of parameters using a profile
MLME-SET-*
PIB
(performance measurement)
Use case 1

## Slide 6: Configuring a set of parameters using a profile
MPH-EXEC-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next
higher layer
ULM-EXEC-PROFILE.request
MMI-MGMT.request
MAC PIB
Device
MAC
MLME-SRM.request
MMI
sublayer
MPH-EXEC-PROFILE.confirm
ULM-EXEC-PROFILE.confirm
MMI-MGMT.confirm
MLME-SRM.confirm
IEEE802.15.12
Use case 1
MLME-SET.request
MLME-SET.confirm
IEEE802.15.4

## Slide 7: Use case 2: 802.x <-> 802.y protocol translation
Performance measurement between 802.11 and 802.15
ULI profile=0x81
“SRM profile #1”
Parameter | Value
MAC Parameters | 
RCPI | xxx
RSNI | yyy
Category: Radio Measurement
Action: Link Measurement Request
802.11
Radio Resource Measurement
“Action frame”
MLME-SRM-Request
RCPI, RSNI
802.15.4s
Spectrum Resource
Management
SRM profile #1
802.15.12
ULI
MLME-SRM-Response
RCPI=xxx, RSNI=yyy
Category: Radio Measurement
Action: Link Measurement Report
ULI profile ID =0x81
Higher layer
Performance measurement
Use case 2

## Slide 8: Retrieving measurement metrics
MLME-SRM-*
PIB
(performance measurement)
Use case 2

## Slide 9: Retrieving measurement metrics
MPH-GET-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next
higher layer
ULM-GET-PROFILE.request
MMI-MGMT.request
MLME-GET.request
MAC PIB
MLME-GET.confirm
Device
MAC
MLME-SRM.request
MMI
sublayer
MPH-GET-PROFILE.confirm
ULM-GET-PROFILE.confirm
MMI-MGMT.confirm
MLME-SRM.confirm
IEEE802.15.12
Use case 2
IEEE802.15.4

## Slide 10: Use case 3: MAC/PHY configuration by upper-layer application
Provides an API to MAC/PHY layers
Management Protocol is always involved to authorize the service
802.15.4
TSCH
802.15.12
ULI
(6TOP)
6P ADD Request
ULI profile #3
Cell = AAA
celloption=aaa
Cell = BBB
Celloption=bbb
Higher layer
application
(6TOP)
Use case 3
ULI profile #3
slotframe=xxx
Link=yyy
Link=yyy
MLME-SET-LINK
MLME-SET-SLOTFRAME
ULM-EXEC-PROFILE
Configure macLinkTable
PIB

## Slide 11: TSCH slotframe setup by 6TOP
e.g., MLME-SET-SLOTFRAME
PIB
(6TOP)
Use case 3

## Slide 12: TSCH slotframe setup by 6TOP
MPH-EXEC
-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next higher layer (e.g., 6TOP)
ULM-EXEC-PROFILE.request
MMI-MGMT.request
MAC PIB
Device
MAC
MLME-SET
-SLOTFRAME.request
MMI
sublayer
MPH-EXEC -PROFILE. confirm
ULM-EXEC-PROFILE.confirm
6tH-EXEC
-PROFILE. confirm
MLME-SET
-SLOTFRAME. confirm
IEEE802.15.12
IEEE802.15.4
(6P ADD Request)
Use case 3
6TOP
sublayer
MPH-EXEC
-PROFILE.request
PDE
sublayer
6tH-EXEC
-PROFILE.request
MMI-MGMT.confirm
MPH-EXEC
-PROFILE.confirm