## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG12 ULI Report for Mar 2017 Session]
Date Submitted: [14 Mar 2017]
Source: [Patrick Kinney] Company [Kinney Consulting LLC]
Address [Chicago area, IL, USA]
Voice:[+1.847.960.3715], E-Mail:[pat.kinney@ieee.org]
Re: [TG12 Report for Mar 2017 Session.]
Abstract: [Report for the March Session]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Instructions for the WG Chair
The IEEE-SA strongly recommends that at each WG meeting the chair or a designee:
  Show slides #1 through #4 of this presentation
  Advise the WG attendees that:
    The IEEE’s patent policy is described in Clause 6 of the IEEE-SA Standards Board Bylaws;
    Early identification of patent claims which may be essential for the use of standards under development is strongly encouraged;
    There may be Essential Patent Claims of which the IEEE is not aware. Additionally, neither the IEEE, the WG, nor the WG chair can ensure the accuracy or completeness of any assurance or whether any such assurance is, in fact, of a Patent Claim that is essential for the use of the standard under development.
  Instruct the WG Secretary to record in the minutes of the relevant WG meeting:
    That the foregoing information was provided and that slides 1 through 4 (and this slide 0, if applicable) were shown;
    That the chair or designee provided an opportunity for participants to identify patent claim(s)/patent application claim(s) and/or the holder of patent claim(s)/patent application claim(s) of which the participant is personally aware and that may be essential for the use of that standard
    Any responses that were given, specifically the patent claim(s)/patent application claim(s) and/or the holder of the patent claim(s)/patent application claim(s) that were identified (if any) and by whom.
  The WG Chair shall ensure that a request is made to any identified holders of potential essential patent claim(s) to complete and submit a Letter of Assurance.
  It is recommended that the WG chair review the guidance in IEEE-SA Standards Board Operations Manual 6.3.5 and in FAQs 14 and 15 on inclusion of potential Essential Patent Claims by incorporation or by reference.
  Note: WG includes Working Groups, Task Groups, and other standards-developing committees with a PAR approved by the IEEE-SA Standards Board.

## Slide 3: Participants, Patents, and Duty to Inform
All participants in this meeting have certain obligations under the IEEE-SA Patent Policy.
  Participants [Note: Quoted text excerpted from IEEE-SA Standards Board Bylaws subclause 6.2]:
    “Shall inform the IEEE (or cause the IEEE to be informed)” of the identity of each “holder of any potential Essential Patent Claims of which they are personally aware” if the claims are owned or controlled by the participant or the entity the participant is from, employed by, or otherwise represents
    “Should inform the IEEE (or cause the IEEE to be informed)” of the identity of “any other holders of potential Essential Patent Claims” (that is, third parties that are not affiliated with the participant, with the participant’s employer, or with anyone else that the participant is from or otherwise represents)
  The above does not apply if the patent claim is already the subject of an Accepted Letter of Assurance that applies to the proposed standard(s) under consideration by this group
  Early identification of holders of potential Essential Patent Claims is strongly encouraged
  No duty to perform a patent search
Slide #1

## Slide 4: Patent Related Links
  All participants should be familiar with their obligations under the IEEE-SA Policies & Procedures for standards development.
  Patent Policy is stated in these sources:
  IEEE-SA Standards Boards Bylaws
  http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#6
  IEEE-SA Standards Board Operations Manual
  http://standards.ieee.org/develop/policies/opman/sect6.html#6.3
  Material about the patent policy is available at
  http://standards.ieee.org/about/sasb/patcom/materials.html
Slide #2
If you have questions, contact the IEEE-SA Standards Board Patent Committee Administrator at patcom@ieee.org or visit http://standards.ieee.org/about/sasb/patcom/index.html
This slide set is available at https://development.standards.ieee.org/myproject/Public/mytools/mob/slideset.ppt

## Slide 5: Call for Potentially Essential Patents
If anyone in this meeting is personally aware of the holder of any patent claims that are potentially essential to implementation of the proposed standard(s) under consideration by this group and that are not already the subject of an Accepted Letter of Assurance:
  Either speak up now or
  Provide the chair of this group with the identity of the holder(s) of any and all such claims as soon as possible or
  Cause an LOA to be submitted
Slide #3

## Slide 6: TG12 Officers
Slide 6
Chair Pat Kinney
Vice Chair Charlie Perkins
Notes: March 17
Page 6

## Slide 7: TG 12 Status Update
Slide 7
Discussion on mandatory elements of 802.15.12
  Management Protocol Module
    Configuration: adopted the concept of a profile methodology where each identified profile consists of the configuration parameters for a specific, identified implementation for either the 15.4 device or another protocol module
    Management/Monitor: adopts and extends the OMA LWM2M object definitions for 802.15.4
    Discovery: function will determine if an end device is ULI capable or not
  PDE
    Will leverage the MMI concepts
    Fragmentation block is eliminated, it is inherent in the 6LoWPAN protocol module
  MMI
    Will leverage the 802.15.9 multiplex concepts, using MPX IE and ULI IE
    Fragmentation block is eliminated, it is inherent in the MMI header structure
    Use of lower 32 dispatch addresses allow 2-octet Protocol ID to be elided
  PassThru
    Required to allow 6LoWPAN communications to pass through PDE and MMI to 802.15.4 device
    Required to allow application to directly configure 802.15.4 device via MLME SAP and send messaging via MCPS SAP
Notes: March 17
Page 7

## Slide 8: TG 12 Status Update (continued)
Slide 8
Discussion on optional elements of 802.15.12
  6LoWPAN
    Moved fragmentation function back into protocol module
  Ranging and Location Support -- RLS Protocol Module:
    Document 15-17-0082-00-0012 presented, advancing the operating concepts for the RLS module, including active two-way ranging and passive gathering of location enabling information, and beginning the definition of the SAP operations necessary to support this functionality.
Notes: March 17
Page 8

## Slide 9: TG12 Meeting Goals (agenda: 15-17-0158-00)
Slide 9
Tuesday 14 Mar, AM1: Opening report, Agenda, Status and Functional decomposition review
Tuesday 14 Mar, AM2: Session focus: Header Compression, PDE, MMI, Management Protocols Module (MPM), assignment of functional blocks not already assigned
Wednesday 15 Mar, AM1: Detailed discussion on PDE
Thursday 16 Mar, AM1: Detailed discussion on MMI
Thursday 16 Mar, AM2: Detailed discussion on MPM
Thursday 16 Mar, PM2: Detailed discussion on header compression, Generic Module, Assigned module status, recap on week’s efforts, define the next steps, timetable for completion, phone calls
Notes: March 17
Page 9

## Slide 10: TG12 Meeting
Slide 10
Tuesday 14 Mar, AM1: Opening report, Agenda, Status and Functional decomposition review
  Approve Agenda 15-17-0158-00
  Approve Minutes from previous session, 15-17-0083-00
  Status Update
  Functional Decomposition Review
Notes: March 17
Page 10

## Slide 11
Backup Slides

## Slide 12: 802-2014 Reference Model
Slide 12
Notes: March 17
Page 12

## Slide 13: 802-2014 Reference Model
Slide 13
Notes: March 17
Page 13

## Slide 14: 802.15.9 Functional Decomposition

## Slide 15: 802.15.10 Functional Decomposition
The Data SAP and the MCPS-SAP are used for Multicast as indicated in Figure 19 and Figure 66
The MGMT SAP and the MLME-SAP are used as indicated in Figures 3 through 13

## Slide 16: Deliverables
Slide 16
Deliverables
Management SAP
  Configuration Management
    Dynamic PHY management
      B Rolfe to provide
    Network
      Set-Up
    MAC
      Set-Up
    PHY
      Set-Up
    Security
      Set-Up
    TSCH set-up
      P Kinney to provide
    Channel Hopping
  Yang Modeling
  L2 Routing
    C Perkins to provide
Data SAP
  Protocol Differentiation
    EtherType
  Security
    KMP (802.15.9)
      ETSI TS102887-2
      802.1x
      Internet Key Exchange (IKE)
      Dragonfly
      PANA
      Vendor specific
  MAC Resource Management
    Priority
    GTS management
  TSCH Operation
    P Kinney to provide
  Fragmentation
    Adaptive
    PHY (PSDU)
    UpperLayer
      802.15.9
      6LoWPAN
  Location awareness
    Ranging
    B Verso to provide
Notes: March 17
Page 16

## Slide 17: Deliverables
Slide 17
Management SAP
  Configuration Management
    PHY
      Set-Up
        Channel
          Center frequency
          Channel number
          Regional band
        Bandwidth
        Modulation
          Channel page
        Preamble
          Code
          Repetition
        FCS size
        Packet Length
        Data Rate
        Transmit Power level
        Data Whitening
        Common Signalling Mode
        ED Threshold
        Spreading Factor
        DSSS code
        CCA
          Mode
          duration
        FEC?
          Rate
          Coding
          Interleaving
        SFD
          Size
          value
Notes: March 17
Page 17

## Slide 18: Deliverables
Slide 18
Management SAP
  Configuration Management
    MAC
      Set-Up
        FFD?
        Beacon-enabled?
          DSME?
            Seong-Soon Joo to provide
          Superframe parameters
        Low Energy?
          Parameters
        Channel Hopping?
          parameters
        Association?
          Fast?
        Synchronization
          Superframe
          TSCH
        ACK required?
        Promiscuous mode?
          Ask Packet Sniffer vendors or chipset vendors
        Device Announcement
        UL IEs?
          parameters
Notes: March 17
Page 18

## Slide 19: Deliverables
Slide 19
Management SAP
  Configuration Management
    Network
      Set-Up
        PAN Coordinator?
          Beacon-enabled?
          Low Energy?
          Association?
            Fast?
            Permit to Join?
              Criteria to accept
          Short Address?
            Assignment
        Channel Scan
Notes: March 17
Page 19

## Slide 20
Slide 20
Management Protocol Configuration Parameters via MGMT SAP - MAC |  |  |  | 
Operational | Op enumerations |  |  | 
Device Type | FFD, RFD, RFD-TX, RFD-RX |  |  | 
PAN | Set-up, discovery |  |  | 
Notes: March 17
Page 20

## Slide 21
Slide 21
Management Protocol Configuration Parameters via MGMT SAP - MAC |  |  | 
Optional Modes | Configuration set-up |  | 
Generic (GTS) [beacon-enabled] | Superframe |  | 
DSME | Superframe |  | 
TSCH | Slotframe |  | 
SUN [Nonbeacon-enabled] |  | phyCurrentChannel, ChanCenterFreq0 NumChan, ChanSpacing phyCurrentPage, phyCurrentSUNPageEntry, phyNumSUNPageEntriesSupported phySUNPageEntriesSupported macPanId, macCoordShortAddress phySUNChannelsSupported | 
TVWS |  |  | 
LECIM (lp-wan) |  |  | 
RFID |  |  | 
RCC |  |  | 
Generic [non-beacon-enabled] |  |  | 
Notes: March 17
Page 21

## Slide 22
Slide 22
Management Protocol Configuration Parameters via MGMT SAP - MAC |  | 
Option behaviors | Option details | 
Association |  | 
Security | Integrity, Encryption | 
Promiscuous |  | 
Ranging |  | 
Low Energy | CSL, RIT, IRIT | 
Priority |  | 
Metrics | MAC Metrics IE/All MAC Metrics IE | 
Channel Hopping | Channel hopping IE, macHoppingSequenceLength, macHoppingSequenceList, macHoppingSequenceId, macNumberofChannels, macPhyConfiguration, macExtendedBitmap | 
IEs | Header, Payload | 
TRLE |  | 
Spectrum Tracking |  | 
Notes: March 17
Page 22

## Slide 23
Slide 23
Management Protocol Configuration Parameters via MGMT SAP | 
PHY Parameters | PHY Parameters - detail
Channel | phyCurrentChannel = Number: phyCurrentPage
Modulation type | O-QPSK, BPSK, FSK, MSK, OFDM, CSS, UWB-HR, UWB-LR, ASK
Preamble | Code/repetition: phyFskPreambleLength, SecondaryFskPreambleLength
FCS size | 2, or 4
Packet Length | aMaxPhyPacketSize = 127, or 2047, or phyLecimDsssPsduSize
Operating Mode | 
Data Rate (kb/s) | 2.4, 4.8, 6.25, 9.6, 10, 12.5, 16, 19.2, 20, 25, 31.25, 32, 36, 38.4, 40, 50, 100, 110, 150, 156, 200, 234, 250, 300, 312, 468, 600, 624, 800, 850, 936, 1000, 1404, 1562.5, 1638, 2000, 3125, 6250, 6810, 27240
Transmit power level | phyTxPower
CCA | 1, 2, 3, 4, 5, 6, : aCcatime/phyCCADuration
FEC | Off/On, rate, code, interleaving: phyFskFecEnabled, phyFskFecInterleavingRsc, phyFskFecScheme/phyTvwsFskFecScheme, phyLecimFecTailBitingEnabled
SFD | Size/value: phySunFskSfd, phyTvwsSfdLength, phyLecimDsssSfdPresent, SecondaryFskSfd
Notes: March 17
Page 23

## Slide 24
Slide 24
Management Protocol Configuration Parameters via MGMT SAP | 
PHY Parameters (cont’d) | PHY Parameters - detail
TX<->RX | aTurnaroundTime
ED threshold | 
Spreading factor | 
DSSS code | 
Data whitening | 
Common signaling mode | 
Notes: March 17
Page 24

## Slide 25: Example of Options Used for Secured SUN FSK Device
Slide 25
Notes: March 17
Page 25

## Slide 26: Example of Options Used for LECIM O-QPSK Device
Slide 26
Notes: March 17
Page 26

## Slide 27: Example of Options Used for 6tisch O-QPSK Device
Slide 27
Notes: March 17
Page 27

## Slide 28: Future Efforts
Slide 28
Functional Module Technical Details
PDE P Kinney
MMI P Kinney
Management Protocol H Yokota
6LoWPAN
KMP
802.1X
L2R C Perkins
6tisch
Ranging B Verso
Generic
Functional Block Overview
How do they work?
What functions do they include?
How do the SAPs work?
What primitives are required?
What parameters are required?
Notes: March 17
Page 28

## Slide 29: Meeting Accomplishments
Slide 29
Discussion on mandatory elements of 802.15.12
  Management Protocol Module
    Configuration: adopted the concept of a profile methodology where each identified profile consists of the configuration parameters for a specific, identified implementation for either the 15.4 device or another protocol module
    Management/Monitor: adopts and extends the OMA LWM2M object definitions for 802.15.4
    Discovery: function will determine if an end device is ULI capable or not
  PDE
    Will leverage the MMI concepts
    Fragmentation block is eliminated, it is inherent in the 6LoWPAN protocol module
  MMI
    Will leverage the 802.15.9 multiplex concepts, using MPX IE or ULI IE
    Fragmentation block is eliminated, it is inherent in the MMI header structure
    Use of lower 32 dispatch addresses allow 2-octet Protocol ID to be elided
  PassThru
    Required to allow 6LoWPAN communications to pass through PDE and MMI to 802.15.4 device
    Required to allow application to directly configure 802.15.4 device
Notes: March 17
Page 29

## Slide 30: Meeting Accomplishments
Slide 30
Discussion on optional elements of 802.15.12
  6LoWPAN
    Moved fragmentation function back into protocol module
  Ranging and Location Support -- RLS Protocol Module:
    Document 15-17-0082-00-0012 presented, advancing the operating concepts for the RLS module, including active two-way ranging and passive gathering of location enabling information, and beginning the definition of the SAP operations necessary to support this functionality.
  L2R
    No progress this session
  KMP
    No progress this session
  6top
    No progress this session
Notes: March 17
Page 30

## Slide 31: Schedule
Slide 31
TASK | Start | Completed
TG12 | May, 2016 | Mar, 2019
Concept and Architecture | May, 2016 | Nov, 2016
Baseline definition | Nov, 2016 | July, 2017
Draft | May, 2017 | Nov, 2017
TG Comment Collection | Sept, 2017 | Jan, 2018
WG Letter Ballot | Dec, 2017 | Mar, 2018
Sponsor Ballot | Aug, 2018 | Jan, 2019
NesCom | Jan, 2019 | Mar, 2019
IEEE-SA Publication | Mar, 2019 | June, 2019
Notes: March 17
Page 31