## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.12 – Conceptual Overview]
Date Submitted: [7 November 2017]
Source: [Pat Kinney], Company: [Kinney Consulting]
Address [Chicago area, IL, USA]
Voice: [+1.847.960.3715], E-Mail: [pat.kinney@kinneyconsultingllc.com]
Re: [Information on IEEE 802.15.12 for IETF coordination effort]
Abstract: [High Level Overview of current state of IEEE 802.15.12]
Purpose: [For informational purposes only]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.12
Conceptual Overview

## Slide 3: IEEE 802.15.12 Introduction
Slide 3
Introduction
IEEE 802.15.12 performs many of the functions that an LLC would perform but adds additional functionality needed for IEEE 802.15.4 in areas such as configuration, higher layer protocol identity, fragmentation, harmonization of existing of other upper sublayer layer 2 protocols, and management of 802.15.4 devices.
Purpose, to provide the following:
Reduction of the complexity in configuring and using the 802.15.4 device
  Complexity in configuring 802.15.4 results from having to select one correct configuration given all possible combinations of the following: 8 MAC modes with 13 distinct MAC behaviors, 9 PHY modulation types with 4 distinct PHY behaviors and 40 PHY data rates, and 20 PHY bands with greater than 35,390 channels.
    802.15.12 defines a management protocol module that provides configuration parameters to the 802.15.4 device.
  Complexity in the use of 802.15.4 to send messages is shown by a comparison with 802.3 and 802.11. Ethernet (802.3) has 4 parameters in its data transmission primitive while 802.11 has 6. However, the 802.15.4 data transmission primitive contains 28 parameters. See Figure 1 for more details. Additionally, 802.15.4 uses a MAC address order that is contrary to 802-2014.
    802.15.12 will define a ULI data transmission primitive with ~ 4 mandatory parameters that will generate an 802.15.4 MCPS primitive.
    802.15.12 will provide an explicit description of the order of the 64-bit MAC address in the primitive
Notes: January 18
Page 3

## Slide 4: IEEE 802.15.12 Introduction
Slide 4
Purpose (continued) – provide the following:
  Addition of higher layer protocol identification
    An implicit assumption with 802.15.4 is that there is a single application/protocol stack above it, while other standards such as 802.3 and 802.11 use EtherType protocol identities to direct messages to one of many applications.
      802.15.12 adds a header supplying higher layer protocol identification using EtherTypes or Dispatch codes to allow multiple applications to use a single 802.15.4 device.
  Fragmentation
    802.15.4 needs fragmentation of datagrams due to small frame sizes and low to very low data rates even though 802.15.4 does not include frame fragmentation.
      802.15.12 provides two fragmentation methods, one for 6LoWPAN operation and the other for all else.
  Harmonization
    Numerous layer 2 protocols have been designed for 802.15.4, however these protocols have not been harmonized to allow combinations of these protocols.
      802.15.12 will harmonize the logical combinations of layer 2 protocols.
  Management
    Originally, 802.15.4 was not intended to be managed, hence the standard did not include managed objects.
      802.15.12 introduces managed objects to allow 802.15.4 devices to be managed in a manner similar to other devices such as 802.11.
Notes: January 18
Page 4

## Slide 5: Data Request Comparison - Figure 1
Slide 5
802.3
MA_DATA.request (
destination_address,
source_address,
mac_service_data_unit,
frame_check_sequence
)
802.11
MA-UNITDATA.request (
source address,
destination address,
routing information,
data,
priority,
service class
)
802.15.4
MCPS-DATA.request (
SrcAddrMode,
DstAddrMode,
DstPanId,
DstAddr,
Msdu,
MsduHandle,
HeaderIeList,
PayloadIeList,
HeaderIeIdList,
NestedIeSubIdList,
AckTx,
GtsTx,
IndirectTx,
SecurityLevel,
KeyIdMode,
KeySource,
KeyIndex,
UwbPrf,
Ranging,
UwbPreambleSymbolRepetitions,
DataRate,
LocationEnhancingInformationPostamble,
LocationEnhancingInformationPostambleLength,
PanIdSuppressed,
SeqNumSuppressed,
SendMultipurpose
FrakPolicy,
CriticalEventMessage
)
As an example of the complexity of sending or receiving data with 802.15.4 compared to Ethernet or 802.11, the respective data request primitives are shown. Two common parameters are highlighted.
Notes: January 18
Page 5
Common items are 1. destination address, 2. data to be sent
15.12 proposal -> MD_DATA_REQ (SrcAddr, DstAddr, msduLength, msdu)
Where:
SrcAddr - The unique (64-bit IEEE) address of the originator of the transmission.
DstAddr - The unique (64-bit IEEE) address of the intended recipient of the transmission.
msduLength - Length (number of octets) of the DPDU to transmit.
Msdu - A sequence of msduLength octets containing the DPDU to transmit.

## Slide 6: 802.15.12 Functional Decomposition
  Overview:
  The 802.15.12 functional decomposition is based upon the 802-2014 Reference Model and the 802.15.9 KMP reference model.
  The functional decomposition as shown in Figure 2 enables:
    multiple higher layer applications and protocol stacks by use of the Protocol Discrimination Element (PDE). The PDE multiplexes the layer 3 interface to the appropriate protocol module
    all known Layer 2 protocols for 802.15.4, while still allowing extensibility to add protocols. These protocols are contained within the respective protocol modules. The protocol modules format the layer 3 datagrams into 802.15.4 primitives before transmission and extracts the incoming message from the 802.15.4 primitive for the appropriate layer 3 SAP
    all protocol modules access to the appropriate 802.15.4 SAP via the Multiplexed MAC Interface (MMI)
    fragmentation for datagrams, where fragmentation for 6LoWPAN is included in its protocol module and fragmentation for all other messages in included in the Multiplexed MAC Interface (MMI)

## Slide 7: PHY and DLL Functional Decomposition - Figure 2
Slide 7
Notes: January 18
Page 7
The decomposition was derived from the following:
The top part (layer 3 interface to protocol modules) was defined in the 802 (architecture) standard
The bottom part (protocol modules to the MAC interface) was defined in the 802.15.9 (KMP) recommended practice
The MAC and PHY descriptions are defined in the 802.15.4 standard

## Slide 8: 802.15.12 Protocol Discrimination Entity (PDE)
  Purpose:
  Directs and optionally modifies information from the higher layer SAP to the appropriate protocol module directly
  Directs and optionally modifies information from protocol module SAP to the appropriate higher layer SAP directly
  Overview
  For frames going to the higher layer, the PDE determines the appropriate SAP for delivery, as determined by the ULI header, removes the ULI header, reconstitutes the appropriate header, and then directs the datagram to the SAP.
  For datagrams coming from a higher layer, the PDE determines the SAP to which the datagram is to be sent based upon the configuration of the device as set by the Management Protocols entity, and forwards it to the appropriate SAP.
  Further details may be found in 15-16-0656, latest revision

## Slide 9: 802.15.12 Multiplexed MAC interface (MMI)
Purpose
  Directs and may modify information from a protocol module SAP to the appropriate MAC SAP or another protocol module SAP
Overview
Provides multiplex and fragmentation service to the packets sent by the ULI functions and send them to either the MCPS-SAP, the MLME-SAP, or to another function module SAP within the ULI. The process of sending the packets includes formatting the ULI IE or prepending the appropriate headers into the payload of the frame for transmission.
The interface between the MMI and the ULI function modules includes the Multiplex ID and the payload to be sent or the payload received.
The mechanism for the MMI, i.e. the ability to send the data to the proper SAP, will be similar to the mechanism defined in IEEE 802.15.9 for the multiplexed data service.
  Further details may be found in 15-16-0656, latest revision.

## Slide 10: 802.15.12 Protocol Modules
  Purpose:
  Formats messages from the higher layer SAP into the appropriate 802.15.4 primitive requests, e.g. MCPS-DATA.request, for the intended 802.15.4 SAP, or to the appropriate format for the intended protocol module.
  Responds to primitives from an 802.15.4 SAP in an appropriate manner such as sending the MPDU from a MCPS-DATA.indication to the appropriate higher layer SAP, or reacting to a confirm.
  Configures the necessary parameters of the 802.15.4 device for the intended operation such as network operation.
  Overview
  The Protocol Module acts as an intelligent interface from the higher layer SAP to the 802.15.4 SAP.
  The Protocol Module works with the PDE and MMI to allow an 802.15.4 device to handle multiple higher level applications.
  There are two mandatory protocol modules: Management Protocol and PassThru.

## Slide 11: 802.15.12 Mandatory Protocol Modules
Management protocol module provides:
Configuration parameters to the MAC and PHY using configuration data received from a higher layer
Configuration parameters to other protocol modules received from a higher layer or stored in the management protocol module
  Note: ULI Profile IDs, used to identify the device/module configuration, may need to be assigned by the 802.15 ANA for common profiles such as ULI device discovery, etc. However, proprietary configurations will be vendor specific. See 15-17-0050 for more information on ULI Profiles.
Network device monitoring or management. The monitoring function defines managed objects to provide device monitoring metrics to a higher layer application. The management function uses data collected from the device to optimize the device’s configuration for better spectral use.
Discovery services to detect other ULI-capable devices.

## Slide 12: 802.15.12 Mandatory Protocol Modules
PassThru Module has the following functions:
Allows applications/functions above the ULI to access the 802.15.4 device
Generates an 802.15.4 primitive for messages from the upper layers as well as the 6LoWPAN protocol module to be passed via the 802.15.4 data SAP (MCPS-SAP)
Responds to primitives (i.e. MCPS.DATA.confirm and MCPS.DATA.indication) delivered via the data SAP, such as passing the MPDU to a higher layer function

## Slide 13: 802.15.12 Optional Protocol Modules
802.1X provides authentication, authorization, and cryptographic key agreement mechanisms to support secure communication between end stations connected to 802 networks.
802.15.9 (KMP) provides a methodology to enable key management by providing a transport for key management protocols outside the application layers. Additionally, provides a fragmentation and multiplexing layer for those packets so they can be delivered over smaller MAC layer frames and multiplexed on the recipient end to the right processing service.
802.15.10 (L2R) provides the following functions: topology construction, L2R mesh discovery/join/update/recovery, hop-by-hop retransmission, unicast/multicast/broadcast routing, data concatenation, short address assignment, and security

## Slide 14: 802.15.12 Optional Protocol Modules
6LoWPAN provides the function of MAC frame modification into a frame format for transmission of IPv6 packets and the method of forming IPv6 link-local addresses and statelessly autoconfigured addresses on IEEE 802.15.4 networks. Additional functions include a header compression scheme using shared context and provisions for packet delivery in IEEE 802.15.4 mesh networks.
6tisch functions as an abstraction of an IP link over the TSCH mode of the MAC sublayer by providing network formation and maintenance, multi-hop topology, assign time source neighbor, resource management, dataflow control, scheduling mechanisms, and security.
Ranging and Location Support (RLS): includes mechanisms for both passive gathering of location enabling information (from the MAC/PHY) and active messaging supporting two-way ranging (and other localization methods), and provides a higher layer application such as a location solver with the location enabling information or with a TOF estimate derived from this.

## Slide 15: 802.15.12 ULI-Device Discovery Techniques
Slide 15
To be able to determine how a message is to be transmitted from the 802.15.4 device, the 802.15.12 ULI will create and populate a table indicating devices that are ULI capable and IE capable.
ULI capable: IE capable
Reserved for use with devices using 15.4e-2012, or 15.4-2015
  Payload IE, sent out with defined discovery payload
  Devices not understanding this IE will reject the IE with no ill effects
  Devices with 802.15.12 ULI will receive the IE and respond appropriately
ULI capable: IE non-capable
  Reserved for use with devices using older firmware (< 2011), i.e. no IEs
  Defined discovery payload is sent using security with a well known ULI key
  Devices not knowing this key will reject packet with no ill effects
  Devices with 802.15.12 ULI will decrypt payload and respond appropriately
Notes: January 18
Page 15
The discovery technique for IE non-capable described in this slide was intended to keep the query from interfering with any other higher layer protocol being used. The discovery need not require the use of the security mechanism if the higher layer protocol filters on different 1st and 2nd payload octets.

## Slide 16: 802.15.12 ULI-Device Discovery
Slide 16
The following information shall be included in the IE’s payload:
  ULI IE, sent out for discovery of behavior and services, includes
Discovery ID
Extended address
PAN ID
Maximum frame size
Optional Protocol Modules present
Applications and stacks above ULI
Profile repository? (Y/N)
Neighbor Table (Y/N)
  ULI IE, reply with defined discovery payload
Reply to Discovery ID
Extended address
PAN ID
Maximum frame size
Optional Protocol Modules present
Applications and stacks above ULI
Profile repository? (Y/N)
Neighbor Table (Y/N)
Notes: January 18
Page 16
The discovery technique for IE non-capable described in this slide was intended to keep the query from interfering with any other higher layer protocol being used. The discovery need not require the use of the security mechanism if the higher layer protocol filters on different 1st and 2nd payload octets.

## Slide 17: 802.15.12 Header construction: IE Devices
ULI-6lo IE ID (dedicated to 6LoWPAN traffic)
  ULI-6lo IE ID = total IE length (11 bits) =0bxxxxxxxxxxx, 0b01??, 0b1
  No Protocol Identifier is required, resulting in a total overhead of 2 octets
MPX IE (used for all non-6LoWPAN traffic):
  Defined in 802.15.9, MPX IE ID = total IE length (11 bits)=0bxxxxxxxxxxx, 0b0011, 0b1
  MPX IE has a length of 2 octets, followed by a transaction control of 1 octet, followed by a Protocol Identifier of 2 octets for a total overhead of 5 octets
  For the special case where the dispatch code is < 0x001f, the 2-octet Dispatch code is elided, resulting in a total overhead of 3 octets
  Note: Protocol Identifiers:
    EtherType values are > 0x0600
    Dispatch values assigned by 802.15 ANA are < 0x4FF
    Vendor specific values will be set to 0x565 followed by a 3-octet OUI for that vendor
Notes: Since the ULI-6lo IE carries only 6LoWPAN datagrams, the 6LoWPAN protocol identifier (0xA0ED) is elided.

## Slide 18: 802.15.12 Header construction: Non-IE devices
  Non-IE devices
  1st payload octet is set to 0xff in accordance with 6LoWPAN Paging Dispatch
  2nd payload octet denotes page 15 and will be defined in the future
  3rd and 4th payload octets denote the Protocol Identifier
  Non-IE device discovery can use the security mechanism with a “well known” key to effect a discovery ULI packet that will not disturb non-ULI devices. Those 802.15.4 devices not responding to this discovery packet could be assumed to be non-ULI (multiple discovery packets should be sent since a packet may not be received)
  Note: Protocol Identifiers:
    EtherType values are > 0x0600
    Dispatch values assigned by 802.15 ANA are < 0x4FF
    Vendor specific values will be set to 0x565 followed by a 3-octet OUI for that vendor
Notes: As stated earlier, the discovery technique for IE non-capable described in this slide was intended to keep the query from interfering with any other higher layer protocol being used. The discovery need not require the use of the security mechanism if the higher layer protocol filters on different 1st and 2nd payload octets.

## Slide 19: Examples of Frame Construction with 802.15.12
  The basic assumptions for the following examples of data frames are:
    2-octet frame control,
    1-octet sequence number,
    2-octet origination and 2-octet destination short addresses,
    2-octet PAN ID, origination and destination devices in same PAN, source PAN ID elided,
    6-octet auxiliary security header,
    No header IEs,
    4-octet security MIC,
    2-octet Frame Check Sequence.
  Three examples of 802.15.4 data frames using 802.15.12 are shown in the following figures 3 and 4. The examples are:
    Figure 3 - 802.15.4 devices are not IE capable, hence the ULI message is in the payload
    Figure 4 – 802.15.4 devices are IE capable, hence ULI message is in an IE
      Figure 4a– MPX IE used for all non-6LoWPAN messages
      Figure 4b– ULI IE used only for 6LoWPAN messages

## Slide 20: Frame Composition
Slide 20
Figure 4a
Figure 3
Figure 4b
Notes: January 18
Page 20

## Slide 21: Examples of IP Packet Construction using 802.15.12
  Figure 5 shows six examples of IP packets using 802.15.12:
    IE messaging of non-compressed UDP/IPv6
    IE messaging of non-compressed UDP/IPv4
    IE messaging of compressed UDP/IPv6 using 6LoWPAN
    Non-IE messaging of non-compressed UDP/IPv6
    Non-IE messaging of non-compressed UDP/IPv4
    Non-IE messaging of compressed UDP/IPv6 using 6LoWPAN
  All examples use the basic assumptions for frame construction from the previous Frame Construction examples resulting in a 21-octet MAC overhead
  The 6LoWPAN examples are for non-fragmented, no mesh; yielding a 3-octet overhead
  As indicated, the total (MAC + ULI + IP + UDP) header lengths for the six examples range from 26 octets to 74 octets

## Slide 22: Packet Construction - Figure 5

## Slide 23: Conclusion
  Mandatory elements still to be done:
  PDE
  Primitives
  PDE-DATA
  PDE-CONFIG
  PDE-PURGE
    Parameters
    Behavior
  MMI
    Primitives
      MMI-Data
      MMI-MGMT
      MMI-CONFIG
      MMI-Purge
    Parameters
    Behavior
  Management protocol module
    Primitives
    Parameters
    Behavior
  Pass-thru protocol module
    Primitives
    Parameters
    Behavior

## Slide 24: NetConf Flow

## Slide 25: Data Examples and CoMI Flow
Questions:
If no designated app: reject with response or just drop?
For 6LoWPAN: any concerns with end app?

## Slide 26: L2R: 2 places where a dispatch happens

## Slide 27: Dispatching a frame for L2R
MAC
S
A
B
D
MMI
L2R
PDE
Protocol A
MAC
MMI
L2R
PDE
MAC
MMI
L2R
PDE
MAC
MMI
L2R
PDE
Protocol A
MAC
21
octets
L2R routing IE
variable octets
Dispatching by looking at L2R routing IE
Dispatching by looking at Protocol ID in MPX IE.
S
A
B
D
MPX IE
Protocol A
Payload
Various octets
2
octets
Transaction
Control
1
octet
Protocol
Identifier
=
0
x
XXXX
2
octets
The Number 0xXXXX is for the Protocol A. (e.g. IPv4 etc.)

## Slide 28: Dispatching a frame for L2R – 6LoWPAN mesh under
MAC
S
A
B
D
MMI
L2R
PDE
6LoWPAN
MAC
MMI
L2R
PDE
6LoWPAN
MAC
MMI
L2R
PDE
6LoWPAN
MAC
MMI
L2R
PDE
6LoWPAN
ULI
-
6
lo IE
2
octets
IPHC
2
octets
6
LoWPAN
NHC
1
octet
6
LoWPAN
MAC
21
octets
L2R routing IE
variable octets
Dispatching by looking at L2R routing IE
Dispatching by looking at ULI-6lo IE
S
A
B
D

## Slide 29: 802.1x communication flow

## Slide 30: Conclusion (continued)
  Optional Protocol Modules intended to be done:
  6LoWPAN
    Primitives
    Parameters
    Behavior
  Key Management Protocol (KMP)
    Primitives
    Parameters
    Behavior
  Layer 2 Routing (L2R)
    Primitives
    Parameters
    Behavior
  6top (layer 2 portion of 6tisch)
    Primitives
    Parameters
    Behavior
  Ranging & Location Support (RLS)
    Primitives
    Parameters
    Behavior