## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Channel Modeling for MHN-E System]
Date Submitted: [13 March, 2017]
Source: [Junhyeong Kim1, Ke Guan2, Danping He2, Gosan Noh1, Bing Hui1, Hee-Sang Chung1 and Il Gyu Kim1] Company [1ETRI, 2Beijing Jiaotong University]
Address [218 Gajeong-ro, Yuseong-gu, Daejeon, 34129, KOREA]
Voice:[+82-42-860-6239], FAX: [+82-42-861-1966], E-Mail:[jhkim41jf@etri.re.kr]
Abstract: [This document presents channel modeling for MHN-E system]
Purpose: [For discussion]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contents
Objective
Ray-tracing Channel Modeling
  Simulation Configurations and Scenario Models
  Simulation Results
3GPP Channel Modeling
Future Plans

## Slide 3: Contents
Objective
Ray-tracing Channel Modeling
  Simulation Configurations and Scenario Models
  Simulation Results
3GPP Channel Modeling
Future Plans

## Slide 4: Objective
Coverage test of MHN system at Seoul subway line 8[1][2]
  Very small delay spread, which was less than 60 ns
mRU/mDU
mTE
Antenna 0
Antenna 1

## Slide 5: Objective
Field Trial of MHN system[1][3]
  MHN test bed installation along Seoul subway line 8

## Slide 6: Objective
Field Trial of MHN system[1][3]
  mRU & mTE test bed installation and performance evaluation of MHN system in the moving subway train
    Peak data rate of over 400Mbps was achieved
mRU
mTE

## Slide 7: Contents
Objective
Ray-tracing Channel Modeling
  Simulation Configurations and Scenario Models
  Simulation Results
3GPP Channel Modeling
Future Plans

## Slide 8: Simulation Configurations and Scenario Models
Antenna Parameters of MHN-E system
Name or ID | Pattern | Gain (dBi) | Polarization | Array size
Rx | HPBW_E=8 HPBW_H=8 | 22 | Dual polarized | 8x8
Tx | HPBW_E=16 HPBW_H= 16 | 16 | Dual polarized | 8x8

## Slide 9: Simulation Configurations and Scenario Models
Frequencies and bandwidths
Mobility, distance and antenna selection for each scenario
Selection of applications and scenario types
Carrier Frequencies (GHz) | Simulated Bandwidth (MHz) | Bandwidth for analysis (MHz)
24 – 26.5 GHz | 2500 | 500
Application | Route shape | Speed (Km/h) |  |  | Distance (m) |  | Sample Interval(ms) | 
 |  |  |  |  |  |  | 0.25 | 10
Railway | Straight | 120 | 250 | 500 | 1000 | 1500 |  | 
 |  |  |  |  |  |  |  | 
 | Curve | 100 | 200 | 300 | 500 | 1000 |  | 
 |  |  |  |  |  |  |  | 
Application | Route shape | Scenarios |  |  |  | 
 |  | Outdoor |  |  |  | 
 |  | Urban | Rural | Station | Tunnel | Mountain
Railway | Straight |  |  |  |  | 
 | Curve |  |  |  |  | 

## Slide 10: Simulation Configurations and Scenario Models
Reconstructed Environment Models for Straight Route

## Slide 11: Simulation Configurations and Scenario Models
Reconstructed Environment Models for Straight Route
  Tunnel structure of Seoul subway line 8
  Reconstructed straight Tunnel
Tx (mRU)
1000 m

## Slide 12: Simulation Configurations and Scenario Models
Reconstructed Environment Models for Curved Route
  Tunnel-curved
  Urban-curved

## Slide 13: Simulation Results
Calibration of Raytracer – Measurement

## Slide 14: Simulation Results
Simulation scenarios
Simulation metrics
  Rician K-factor
  RMS delay
  Coherence bandwidth
  Doppler effect (Doppler shift, Doppler spread)
  Coherence time
  Angular domain (AoA, AoD, EoA, EoD, ASA, ASD, ESA, ESD)
  XPD
  CPR
Application | Route shape | Scenarios |  |  |  | 
 |  | Outdoor |  |  |  | 
 |  | Urban | Rural | Station | Tunnel | Mountain
Railway | Straight |  |  |  |  | 
 | Curve |  |  |  |  | 

## Slide 15: Simulation Results
RMS Delay Spread and Rician K Factor – Straight Route

## Slide 16: Simulation Results
Doppler Effect – Straight Route

## Slide 17: Simulation Results
Simulation Results
  50% of the Doppler spreads are less than 452.3 Hz at 500 km/h
  50% of the Doppler spreads are less than 108.5 Hz at 120 km/h
  The mean of Doppler spread of all the scenarios are quite similar
  Tunnel has the maximum Doppler spread which reaches 22.5 KHz at 500 km/h, and 5.5 KHz at 120 km/h.

## Slide 18: Simulation Results
XPD – Straight Route

## Slide 19: Contents
Objective
Ray-tracing Channel Modeling
  Simulation Configurations and Scenario Models
  Simulation Results
3GPP Channel Modeling
Future Plans

## Slide 20: 3GPP channel model overview
3GPP channel model for above 6 GHz[4]
  Supported carrier frequency = 6~100 GHz
  Supported channel bandwidth: Up to 10% of carrier frequency
  Supports 3D channel model
  mmWave propagation characteristics, e.g., blocking and atmosphere attenuation
  Scenarios for system level evaluation
    UMi (Urban micro): Street canyon, open area
    UMa (Urban macro): O2O and O2I
    Indoor: Office and shopping malls
    Backhaul
    D2D/V2V
  Models for link level evaluation
    Clustered Delay Line (CDL) models (for MIMO evaluation)
      NLOS: CDL-A/B/C, LOS: CDL-D/E
    Tapped Delay Line (TDL) models (for non-MIMO evaluation)
      NLOS: TDL-A/B/C, LOS: TDL-D/E

## Slide 21: 3GPP channel model overview
Antenna modeling
  Rectangular panel array antenna
  Dual-polarization
  Antenna element radiation pattern
    3-dB beam width = 65º
    Maximum directional gain = 8 dBi

## Slide 22: 3GPP channel model overview
3D modeling concept
  Channel coefficients
  Each cluster is characterized by
    Delay
    Spatial angle of departure (AoD)
    Spatial angle of arrival (AoA)

## Slide 23: 3GPP channel model overview
Channel examples for link level evaluation

## Slide 24: Contents
Objective
Ray-tracing Channel Modeling
  Simulation Configurations and Scenario Models
  Simulation Results
3GPP Channel Modeling
Future Plans

## Slide 25: Future plans
Further performance validation of ray-tracing simulation through measurement campaign
  Collaboration with Fraunhofer HHI
Joint simulation is currently underway
  Link-level simulator and ray-tracing simulator of MHN and MHN-E systems
Link-level performance evaluation based on the 3GPP channel modeling for the purpose of numerology study

## Slide 26: References
[1] | S. W. Choi et al., “Performance Evaluation of Millimeter-wave-based Communication System in Subway Tunnels”, IEEE 802.15-16-0185-01-hrrc, Mar. 2016
[2] | S. W. Choi et al., "Performance Evaluation of Millimeter-Wave-Based Communication System in Tunnels," 2015 IEEE Globecom Workshops, San Diego, CA, USA, 2015, pp. 1-5.
[3] | S. W. Choi, H. Chung, J. Kim, J. Ahn, and I. Kim, "Mobile Hotspot Network System for High-Speed Railway Communications Using Millimeter Waves," ETRI Journal, vol. 38, no. 6, pp. 1042-1051, December 2016.
[4] | 3GPP TR 38.900, “Channel model for frequency spectrum above 6 GHz,” V.1.0.1, Jun. 2016.

## Slide 27
Thank you