## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal of ULI primitives for handling profiles]
Date Submitted: [16 MAR 2017]
Source: [Hidetoshi Yokota] Company [Landis + Gyr]
Address [8-13-1 Ginza, Chuo-ku, Tokyo 104-0061, Japan]
Voice:[+81 3-4572-1407], FAX: [+81 4572-1401], E-Mail:[hidetoshi.yokota@landisgyr.com]
Re: [“ULI Profile for Protocol Management”, IEEE802.15-17-0050-01-0012]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: [Dedicated primitives are proposed for handling ULI profiles.]
Purpose: [Discussion and approval.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ULI “Profile” for Protocol Management (revisit)
Proposal
  Define a “ULI Profile”, which is a set of parameters or commands to simply access
Values of ULI Profile
  Simpler interface to the MAC that reduces the number of API calls by combining existing MLME into something easier to use
  Common interface to other IEEE802 families (LLC-like function)
  Friendly to higher layer applications (e.g., 6Tisch) by using Yang data model
Dedicated primitives are needed to handle profiles
  5 primitives are proposed

## Slide 3: Example: one-shot MAC/PHY configuration
ULI profile ID=0x01
“Configuration profile #1”
Parameter | Value
MAC Parameters | 
Device Type | FFD
PAN | discovery
Operation mode | TSCH-BE
Channel Hopping | 
PHY Parameters | 
Modulation type | FSK
FCS | 4
Data rate | 100
Transmit power | 20mW
list Configuration {
key “profile-id";
leaf profile-id {
type unit8;
}
leaf DeviceType {
type enumeration {
enum FFD;
enum RFD;
enum RFD-TX;
enum RFD-RX;
}
}
leaf PAN {
type enumeration {
enum discovery;
enum set-up;
}
...
...
}
CONFIGURATION TEMPLATE
(Yang data model)

## Slide 4: Flows of operations
MLME-SET-*
PIB
6TOP
Profile
Profile
Profile
XML/JSON
Template
Template
Template
NETCONF
RESTCONF

## Slide 5: ULI Profile Operation Primitives
Type of operations
  ULM-CREATE-PROFILE()
  ULM-EXEC-PROFILE()
  ULM-GET-PROFILE()
  ULM-CHANGE-PROFILE()
  ULM-DELETE-PROFILE()
Name | Request | Indication | Response | Confirm
ULM-CREATE-PROFILE | X |  |  | X
ULM-EXEC-PROFILE | X |  |  | X
ULM-GET-PROFILE | X |  |  | X
ULM-CHANGE-PROFILE | X |  |  | X
ULM-DELETE-PROFILE | X |  |  | X

## Slide 6: ULM-CREATE-PROFILE.request/confirm
ULM-CREATE-PROFILE.request (
Profile Id,
Profile
)
Name | Type | Valid range | Description
Profile ID | Integer | 0x00-0xff | The Profiled ID
Profile | Set of octets | — | The Profile information represented in the form of XML/JSON.
Status | Enumeration | SUCCESS, NON_SUPPORTED, REJECTED | The status of the ULM-CREATE-PROFILE attempt.
ULM-CREATE-PROFILE.confirm (
Profile Id,
Status
)

## Slide 7: ULM-EXEC-PROFILE.request/confirm
ULM-EXEC-PROFILE.request (
Profile Id,
)
Name | Type | Valid range | Description
Profile ID | Integer | 0x00-0xff | The Profiled ID
Profile | Set of octets | — | The Profile information represented in the form of XML/JSON.
Status | Enumeration | SUCCESS, INCOMPLETE NON_SUPPORTED, REJECTED | The status of the ULM-EXEC-PROFILE attempt. In case of incomplete, unsuccessful part should be shown n the profile
ULM-EXEC-PROFILE.confirm (
Profile Id,
Profile //result
Status
)

## Slide 8: ULM-GET-PROFILE.request/confirm
ULM-GET-PROFILE.request (
Profile Id,
)
Name | Type | Valid range | Description
Profile ID | Integer | 0x00-0xff | The Profiled ID
Profile | Set of octets | — | The Profile information represented in the form of XML/JSON.
Status | Enumeration | SUCCESS, INCOMPLETE NON_SUPPORTED, REJECTED | The status of the ULM-GET-PROFILE attempt.
ULM-GET-PROFILE.confirm (
Profile Id,
Profile,
Status
)

## Slide 9: ULM-CHANGE-PROFILE.request/confirm
ULM-CHANGE-PROFILE.request (
Profile Id,
Profile, // to be changed
)
Name | Type | Valid range | Description
Profile ID | Integer | 0x00-0xff | The Profiled ID
Profile | Set of octets | — | The Profile information represented in the form of XML/JSON. For request, all of only changed part
Status | Enumeration | SUCCESS, NON_SUPPORTED, REJECTED | The status of the ULM-CHANGE-PROFILE attempt.
ULM-CHANGE-PROFILE.confirm (
Profile Id,
Profile, //result
Status
)

## Slide 10: ULM-DELETE-PROFILE.request/confirm
ULM-DELETE-PROFILE.request (
Profile Id,
)
Name | Type | Valid range | Description
Profile ID | Integer | 0x00-0xff | The Profiled ID
Status | Enumeration | SUCCESS, NON_SUPPORTED, REJECTED | The status of the ULM-DELETE-PROFILE attempt.
ULM-DELETE-PROFILE.confirm (
Profile Id,
Status
)

## Slide 11: Example: configuring a set of parameters using a profile
MPH-EXEC-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next
higher layer
ULM-EXEC-PROFILE.request
MMI-MGMT.request
MAC PIB
Device
MAC
MLME-SRM.request
MMI
sublayer
MPH-EXEC-PROFILE.confirm
ULM-EXEC-PROFILE.confirm
MMI-MGMT.confirm
MLME-SRM.confirm
IEEE802.15.12
MLME-SET.request
MLME-SET.confirm
IEEE802.15.4

## Slide 12: Backup <15-17-0050-01-0012>

## Slide 13: ULI “Profile” for Protocol Management
Values of ULI
  Simpler interface to the MAC that reduces the number of API calls by combining existing MLME into something easier to use
  Common interface to other IEEE802 families (LLC-like function)
Challenge
  Mapping between layers or different 802 specs is not so simple…
Proposal
  Define a “ULI Profile”, which is a set of parameters or commands to simply access
  Yang modeling can be used for this
Use cases for ULI Profile
  Use case 1: one-shot MAC/PHY configuration
  Use case 2: 802.x <-> 802.y protocol translation
  Use case 3: MAC/PHY configuration by higher layer applications

## Slide 14: ULI Profile identification and operation primitives
Scope of profile ID
  Local ID
  global ID (standardized)
Type of operations
  ULM-CREATE-PROFILE()
  ULM-EXEC-PROFILE()
  ULM-GET-PROFILE()
  ULM-CHANGE-PROFILE()
  ULM-DELETE-PROFILE()

## Slide 15: Use case 1: one-shot MAC/PHY configuration
Simplifies parameter settings
Use case 1
ULI profile ID=0x01
“Configuration profile #1”
Parameter | Value
MAC Parameters | 
Device Type | FFD
PAN | discovery
Operation mode | TSCH-BE
Channel Hopping | 
PHY Parameters | 
Modulation type | FSK
FCS | 4
Data rate | 100
Transmit power | 20mW
ULI profile ID=0x02
“Configuration profile #2”
Parameter | Value
MAC Parameters | 
Device Type | FFD
PAN | Set-up
Operation mode | Generic-BE
PHY Parameters | 
Modulation type | OFDM
FCS | 4
Data rate | 800
Transmit Power | 600mW

## Slide 16: Configuring a set of parameters using a profile
MLME-SET-*
PIB
(performance measurement)
Use case 1

## Slide 17: Configuring a set of parameters using a profile
MPH-EXEC-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next
higher layer
ULM-EXEC-PROFILE.request
MMI-MGMT.request
MAC PIB
Device
MAC
MLME-SRM.request
MMI
sublayer
MPH-EXEC-PROFILE.confirm
ULM-EXEC-PROFILE.confirm
MMI-MGMT.confirm
MLME-SRM.confirm
IEEE802.15.12
MLME-SET.request
MLME-SET.confirm
IEEE802.15.4

## Slide 18: Use case 2: 802.x <-> 802.y protocol translation
Performance measurement between 802.11 and 802.15
ULI profile ID=0x81
“SRM profile #1”
Parameter | Value
MAC Parameters | 
RCPI | xxx
RSNI | yyy
Category: Radio Measurement
Action: Link Measurement Request
802.11
Radio Resource Measurement
“Action frame”
MLME-SRM-Request
RCPI, RSNI
802.15.4s
Spectrum Resource
Management
SRM profile #1
802.15.12
ULI
MLME-SRM-Response
RCPI=xxx, RSNI=yyy
Category: Radio Measurement
Action: Link Measurement Report
ULI profile ID =0x81
Higher layer
Performance measurement
Use case 2

## Slide 19: Retrieving measurement metrics
MLME-SRM-*
PIB
(performance measurement)
Use case 2

## Slide 20: Retrieving measurement metrics
MPH-GET-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next
higher layer
ULM-GET-PROFILE.request
MMI-MGMT.request
MLME-GET.request
MAC PIB
MLME-GET.confirm
Device
MAC
MLME-SRM.request
MMI
sublayer
MPH-GET-PROFILE.confirm
ULM-GET-PROFILE.confirm
MMI-MGMT.confirm
MLME-SRM.confirm
IEEE802.15.12
IEEE802.15.4
Use case 2

## Slide 21: Use case 3: MAC/PHY configuration by upper-layer application
Provides an API to MAC/PHY layers
Management Protocol is always involved to authorize the service
802.15.4
TSCH
802.15.12
ULI
(6TOP)
6P ADD Request
ULI profile #3
Cell = AAA
celloption=aaa
Cell = BBB
Celloption=bbb
Higher layer
application
(6TOP)
ULI profile #3
slotframe=xxx
Link=yyy
Link=yyy
MLME-SET-LINK
MLME-SET-SLOTFRAME
ULM-EXEC-PROFILE
Configure macLinkTable
PIB
Use case 3

## Slide 22: TSCH slotframe setup by 6TOP
e.g., MLME-SET-SLOTFRAME
PIB
(6TOP)
Use case 3

## Slide 23: TSCH slotframe setup by 6TOP
MPH-EXEC
-PROFILE.request
Management
Protocols sublayer
PDE
sublayer
Next higher layer (e.g., 6TOP)
ULM-EXEC-PROFILE.request
MMI-MGMT.request
MAC PIB
Device
MAC
MLME-SET
-SLOTFRAME.request
MMI
sublayer
MPH-EXEC -PROFILE. confirm
ULM-EXEC-PROFILE.confirm
6tH-EXEC
-PROFILE. confirm
MLME-SET
-SLOTFRAME. confirm
IEEE802.15.12
IEEE802.15.4
(6P ADD Request)
6TOP
sublayer
MPH-EXEC
-PROFILE.request
PDE
sublayer
6tH-EXEC
-PROFILE.request
MMI-MGMT.confirm
MPH-EXEC
-PROFILE.confirm
Use case 3