## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Advancing the definition of the RLS function]
Date Submitted: [16 March 2017]
Source: [Billy Verso] Company [Decawave Ltd.]
Address [Peter Street, Dublin 8, Ireland]
Voice:[+353.87.233.7323], E-Mail:[billy.verso (at) decawave.com]
Re: [SAP usage discussion and definition for RLS]
Abstract: [Continue definition of the RLS functionality for TG12 ULI]
Purpose: [Advance the work of defining the ranging and localisation support (RLS) functionality for the TG12 ULI specification]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: The aim of this presentation:
Progress the definition of the RLS functionality of the ULI:
Build upon the ideas presented in submissions:
  15-16-0657-00-0012
  15-17-0082-00-0012
Begin a definition the RLS information flow through the various SAP identified for the ULI architecture by the functional decomposition in conceptual overview doc 15-17-0113-01-0012

## Slide 3
Functional Decomposition
MAC provides:
TX and RX timestamps
AOA information
RSSI
RLS: Send relevant data to application
RLS: Perform ranging TOF calculation in ranging mode
Application
Location solving
(local or remote)
Localisation / RLS Features

## Slide 4: Considering the control/data flow for RLS modes:
Active modes to examine:
Ranging
  Single-sided two-way ranging
  Double-sided two-way ranging
Simple blink TX (and RX)
  for Time-Difference-of-Arrival (TDOA) real-time location systems (RTLS)
Passive mode:
RX timestamp (and RSSI, AOA) reporting
TX timestamp reporting
For this presentation just looking at a couple of these

## Slide 5: Considering the control/data flow for RLS modes:
Active modes to examine:
Ranging
  Single-sided two-way ranging
  Double-sided two-way ranging
Simple blink TX (and RX)
  for Time-Difference-of-Arrival (TDOA) real-time location systems (RTLS)
Passive mode:
RX timestamp (and RSSI, AOA) reporting
TX timestamp reporting
First consider the blink TX and RX mode

## Slide 6: Active RLS mode – simple blink operation
Simple blink for TDOA RTLS
  Sending periodic blink – from a mobile RTLS “tag” device
  Receiving blink from mobile device at fixed RTLS “anchor” devices and reporting the RX times to a “location engine” for solving the tag location
Simple blink for anchor clock tracking/synchronisation
  TDOA RTLS needs to use the anchors to have synchronised time. This can be achieved using TX and RX timestamps from periodic (blink) frames sent between selected anchor nodes.
    Where anchor clocks are not synchronised by a wired means, these TX and RX times can be used (knowing the TOFs between the anchors) to track the anchors’ clock offsets and correct the blink RX times to a common timebase for the TDOA location solving.
TDOA RTLS anchor needs to pick up blink frame receptions and send them to the location engine to do clock tracking and solve tag location
  anchors will typically operate with RX always on, macRxOnWhenIdle TRUE, so they are always listening for blinks (except when they are actively sending a blink to support the clock tracking time synchronisation function).

## Slide 7: Active RLS mode – tag blink control/data flow
Tag application selects appropriate (UWB) profile to support RLS.
  Via APP-SAP it invokes the appropriate MPH-SAP primitive
Tag application requests RLS to send a blink at a selected time
  Via APP-SAP it invokes the RLSH-SAP primitive
  RLSH-BLINK.request with a parameter to say this is a single TX request
RLS issues the instruction to send the blink frame
  RLSM-SAP multiplexed into MCPS-SAP invokes MCPS-DATA.request to initiate the sending of the multipurpose blink frame (broadcast) with “Ranging” set.
  Multiplexed MAC Interface (MMI) picks up the MCPS-DATA.confirm and delivers this to the RLS through the RLSM-SAP
    Because it is a direct TX the confirm is easily identified. [Otherwise MMI could use the handle parameter of the MCPS-DATA.request to associate this transmission with the RLS to identify the confirm].
RLS reports the completion of the Blink TX to the application.
  RLSH-TX-EVENT.indication or some other primitive??
  The application in the mobile (tag) node can enter a low power sleep state until it next wants to send a blink. The frequency of blink TX can be chosen depending on the expected motion of the item, or dynamically based on its actual (IMU detected) motion.

## Slide 8: Active RLS mode – anchor blink RX reporting
Anchor application selects appropriate (UWB) profile to support RLS.
  Via APP-SAP it invokes the appropriate MPH-SAP primitive
Application configures RLS to report the (blink) frame arrival events
  Via APP-SAP multiplexed into RLSH-SAP
  T.B.D. something like RLSH-BLINK-RX-REPORT-ENABLE.request, or a more general RLSH-RX-EVENT-REPORT-ENABLE.request that can also used to enable the passive mode’s reporting all RX timestamps
RLS needs to be told about the blink frame receptions
  MMI gets MCPS-DATA.indication, identifies the frame as a multipurpose blink and knows this should passed with its RX timestamp to the RLS via the RLSM-SAP.
  In a more general passive mode, the MMI would deliver the RX data to the intended ULI function, but also issue an RX indication to the RLS.
RLS reports the (Blink) RX to the application.
  RLSH-RX-EVENT.indication reports the RX of the (blink) frame with its RX timestamp
  The anchor application can send details of the blink RX timestamp and other location enabling LEI to its location engine solver via an out-of-scope application specific way.
    Will need ID (address) of sending node, RX time, and maybe the sequence number which could be useful to select RX reports for same blink to solve its location.

## Slide 9: Active RLS mode – anchor blink TX flow
This is for the clock tracking / synchronisation for TDOA RTLS
Application (in anchor) requests RLS to send a periodic blink
  Via APP SAP multiplexed into RLSH-SAP
  RLSH-BLINK.request --- parameters select repeated blink with certain period
RLS periodically issues the instruction(s) to send the blink frame
  RLSM-SAP multiplexed into MCPS-SAP invokes MCPS-DATA.request to initiate the sending of the multipurpose blink frame (broadcast) with “Ranging” set.
  Multiplexed MAC Interface (MMI) picks up the MCPS-DATA.confirm and delivers this to the RLS (with the TX timestamp) through the RLSM-SAP.
RLS reports each Blink TX to its application.
  RLSH-TX-EVENT.indication reports that a blink has been is sent and supplies the TX timestamp and other location enabling information (LEI data).
  The application would typically send this to the configured solver via an out-of-scope application specific mechanism.
    TX node (address embedded blink) and TX timestamp are most important.

## Slide 10: Considering the control/data flow for RLS modes:
Active modes to examine:
Ranging
  Single-sided two-way ranging
  Double-sided two-way ranging
Simple blink TX (and RX)
  for Time-Difference-of-Arrival (TDOA) real-time location systems (RTLS)
Passive mode:
RX timestamp (and RSSI, AOA) reporting
TX timestamp reporting
Looking at single sided TWR

## Slide 11: Ranging mechanism: SS-TWR
For single-sided two-way ranging between two devices, A and B, we need a transmitted message from A and a response from B.
For device A to calculate the estimated time of flight, Tprop, device B needs to communicate its reply time, Treply, to device A.
This would normally be done in a subsequent frame, in an IE perhaps.
  Some implementations may be able to predict and set the reply TX time accurately and so be able to pre-compute, Treply, and actually include it in the reply message.
The response from B to A could be an ACK or an independently sent data frame

## Slide 12: Active RLS mode – single sided TWR
Ranging:
Node initiating the SS-TWR sends a frame soliciting a response and asking the responder to tell the initiator the response time.
Initiator, knowing its TX and RX times and the remote’s response times, calculates the TOF.
Location: (example scenario)
For location a mobile tag, knowing which anchors are in its vicinity (and their coordinates), can perform separate SS-TWR exchanges to three (or more) anchors and solve its own location.

## Slide 13: Active RLS mode – SS-TWR initiator control flow
Application selects appropriate (UWB) profile to support RLS.
  Via APP-SAP it invokes the appropriate MPH-SAP primitive
Application selects destination responder node and requests RLS to perform the SS-TWR exchange
  Via APP-SAP it invokes the RLSH-SAP primitive
  RLSH-TWR.request with parameters select destination responder address, and to indicate the “flavour” of ranging to perform, e.g. SINGLE_SIDED_WITH_ACK
RLS issues the instruction to send a data frame as the ranging initiation message.
  RLSM-SAP multiplexed into MCPS-SAP invokes MCPS-DATA.request to initiate the sending a data frame addressed to the target responder, requesting an ACK with “Ranging” set, and including a ranging response request IE to solicit the responder to report its RX/TX response delay in a subsequent frame
  Multiplexed MAC Interface (MMI) picks up the MCPS-DATA.confirm when the ACK is received and delivers this to the RLS through the RLSM-SAP with ranging parameters:
    {RangingCounterStart, RangingCounterStop, RangingTrackingInterval, RangingOffset, etc)
  Multiplexed MAC Interface (MMI) picks up the MCPS-DATA.indication from the responder, and detecting the ranging response time IE, delivers this to the RLS

## Slide 14: Active RLS mode – SS-TWR initiator control flow contd.
RLS now calculates the TOF.
  Tround = RangingCounterStop – RangingCounterStart
  Treply = ranging response time from the IE
  TOF = ½ (Tround – Treply )
  An improved result can be achieved if the Treply is scaled by the clock offset ratio of the responders clock using the RangingTrackingInterval and RangingOffset parameters
RLS reports the ranging result, the TOF, to its application.
  RLSH-TWR.confirm reports result with parameters to indicate the responder ID, the resultant TOF, and the type of ranging performed SINGLE_SIDED_WITH_ACK.
  The application might use this directly (as a proximity measure) or may gather TOF from other selected responder nodes to solve its location. It then may report this via a network IP data message to some location monitoring/consumer application.

## Slide 15: Active RLS mode – SS-TWR responder control flow
Application selects appropriate (UWB) profile to support RLS.
  Via APP-SAP it invokes the appropriate MPH-SAP primitive
  As a responder it needs to be listening for ranging requests so perhaps macRxOnWhenIdle is set TRUE. Otherwise some out of scope scheduling synchronisation is needed to have the responder turn on its receiver when the initiator message is due.
SS-TWR initiator message is received
  Multiplexed MAC Interface (MMI) picks up the MCPS-DATA.indication when the ACK is sent, identifies it as part of a ranging when it finds the ranging response request IE in the message, and informs the conveys it to the RLS through the RLSM-SAP with the initiator’s (source) address and the RangingCounterStart, RangingCounterStop, parameters from MCPS-DATA.indication.
RLS computes the reply time, reports it back the initiator in a data frame
  Treply = RangingCounterStop – RangingCounterStart.
  RLSM-SAP issues the MCPS-DATA.request into MCPS-SAP the frame to the initiator with the ranging response time IE conveying the Treply value

## Slide 16: Other RTS modes of operation
Previous presentations, referenced on slide 2, discussed a number of other RLS modes of operation that have not been examined in this submission
These should be given considered in future submissions, or, revisions of this document.

## Slide 17
DISCUSSION ?