## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Candidate Technology Qualitative Evaluation]
Date Submitted: [16 March, 2017]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This documents describes the proposed qualitative valuation]
Purpose: [Discussion within group.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Candidate Technology Qualitative Evaluation
Joerg Robert FAU Erlangen-Nuernberg

## Slide 3: Motivation
One task of the IG LPWA is the identification of candidate technologies wrt. their applicability in Low Power Wide Area Networks (16/729r0)
Potential use-cases and their requirements have been defined in the use-case list (16/770r3)
This document presents a method to compare the candidate technologies on a qualitative basis

## Slide 4: General Evaluation Proposal
Suitability
Analysis the general suitability of a candidate technology
Qualitative Evaluation
Analysis pros and cons, and dependency on other technologies (this document)
Quantitative Evaluation
Exact performance (only for selected technologies)

## Slide 5: Qualitative Evaluation
If a candidate technology is able to support a specific use-case, the pros and cons of the technology are listed
Furthermore, the dependency on other technology options are given
The following slides show the pros (green) and cons (orange) for the modulation scheme OFDM
Grey indicates that the technology has neither pros nor cons wrt. a technology

## Slide 6: Channel Model
OFDM is robust wrt. multi-path propagation (especially a problem in outdoor channels) when used with high bandwidth
The short Delay Spread of indoor channels in addition to the low data-rates does not require the use OFDM
Indoor
Outdoor Rural
Outdoor Urban

## Slide 7: Typical Power Supply
OFDM has a high PAPR (Peak to Average Power Ratio) that leads to potentially inefficient amplifiers
The cyclic prefix of OFDM requires energy that is not used in the receiver
Higher power consumption that is critical for devices with low energy
CR 2025
2xAA
Energy harvesting
External

## Slide 8: Node Velocity
OFDM has problems at higher Doppler frequencies as the channel has to be almost static within the duration of an OFDM symbol
3 km/h
30 km/h
120 km/h

## Slide 9: Dependencies on Other Technologies
The use of OFDM in frequency selective channels requires the use of a powerful Forward Error Correction to exploit is full benefits
 Dependent on the use of FEC

## Slide 10: Results of the Qualitative Evaluation
OFDM is beneficial in case of outdoor channels
OFDM has disadvantages in case of high mobility and if the power supply is limited
Results can be used to evaluate use-cases in 16/770r3
  This evaluation also has to consider the dependent technologies
  Technologies that have been identified as not suitable (Doc. 15-17/160r1) do not have to be evaluated

## Slide 11: Results of the Suitability Evaluation
Access Control | Public Lighting
Alarms and Security | Smart Grid - Fault Monitoring
Asset Tracking | Smart Grid - Load Control
Assisted Living | Smart Metering
Cattle Monitoring | Smart Parking
Field Monitoring | Smoke Detectors
Global Tracking | Structural Health Monitoring
Industrial Plant Condition Monitoring | Vending Machines - general
Industrial Production Monitoring | Vending Machines - privacy
Light Switch | Waste Management
Pet Tracking | Water Pipe Leakage Monitoring
Pipeline Monitoring - Terrestrial | 

## Slide 12: Thank You!
Comments? Questions?