## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [A user-space application view of 802.15.12 profile interface via ioctl()]
Date Submitted: [16 March 2017]
Source: [Charles Perkins] Company [Futurewei]
Address [Santa Clara, CA]
Voice:[408-330-4586], E-Mail:[charliep@computer.org]
Re: [Development of 802.15.12 management module ideas for profiles]
Abstract: [User-space applications can use ioctl() to execute 802.15.12 profiles in mgmt module.]
Purpose: [consider how programmers will use 802.15.12.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Candidate approaches for TG12 API
Similar to Netconf [RFC4341]
Similar to CoMI [CoAP stuff]
Similar to ioctl() [Unix graybeard stuff]

## Slide 3: Design assumptions / guidelines
All management SAP functions flow through the management module, if only as a pass-through.
base specifications for 6top, L2R, KMP, etc. are not changed.
Operations can be multi-threaded
  unless precluded at a very low level (which seems like a mistake)
  example-bad: xmit blocked until neighbor Ack?

## Slide 4: Candidate netconf API (1)
[See http://www.netconfcentral.org/netconf_docs]
netconf is all about doing stuff over TCP, and TCP isn't in our picture
plus a lot about configuration databases and staging which we may not need
various features for locking to avoid "session" interferences

## Slide 5: Candidate netconf API (2)
pub/sub could be discussed...
Capabilities Exchange
Need for security is drastically reduced
Typically only one instance of each "object" on an 802.15.12 device

## Slide 6: Candidate CoMI API
https://www.ietf.org/id/draft-ietf-core-comi-00.txt
Uses UDP instead of TCP/HTTP
Simple request/reply specification for encoded objects
Restconf-like syntax, with predefined path components (could re-use this)
  http://127.0.0.1/l2r/set_metric_type?6
  coap://127.0.0.1/l2r/set_metric_type?6
specification for events & notifications
specification is still in progress

## Slide 7: CoMI commands
GET: Retrieve the datastore resource or a data resource
FETCH: Retrieve (partial) data resource(s)
POST: Create a data resource, invoke RPC
PUT: Create or replace a data resource
iPATCH: Idem-potently create, replace, and delete data resource(s) (partially)
DELETE: Delete a data resource

## Slide 8: Socket applications in Unix systems
Socket applications: live on top of TCP, UDP, SCTP, TLS, ICMP, or (very rare) IP.
Kinds of applications: reliable bulk transfer, streaming, real-time, interactive, secure, ...
Socket applications are written to have some sort of abstract knowledge of the network, but not necessarily any detailed knowledge of data rate..

## Slide 9: ioctl(), ioctl.h
Definitionally, the interface seems right:
  The ioctl() function manipulates the underlying device parameters of special files. In particular, many operating characteristics of character special files (e.g., terminals) may be controlled with ioctl() requests.
Calling sequence:
  ioctl (fd, request, structure)
http://man7.org/linux/man-pages/man2/ioctl.2.html

## Slide 10: Candidates to place L2R management box
1
2
3

## Slide 11: Ref. Functionalities that higher layer need to manage
No. | item | Page in IEEE802.15.10 | Which box should manage | Description
1 | Short address management | P.27 P.38-39 | 3 | PAN coordinator manages short addresses for all devices within the PAN using PANC DC (PAN coordinator direct connection) that is exchanged by a transport protocol other than L2R or ULI. Application layer manages it.
2 | Source rout management | P.54, P.64, P.66, P.67 | 1 | In no-storing mode, all DS path information is gathered to mesh root. Appropriate path list need to be generated everytime when data is sent.
3 | Procedure through PANC DC | P.38-39, P.77 | 3 | A mesh root with PANC DC (PAN coordinator direct connection) which is up to a higher layer of L2R need to exchange the information with PAN coordinator through PANC DC for the following two functions. 1. Short address management 2. Broadcast to all devices within a PAN
4 | PAN discovery | P.28-31 | 1 | Before starting or joining an L2R mesh, an L2R device does the discovery process in order to find an appropriate PAN to associate to. This process should be controlled by a next higher layer of an L2R sublayer.
5 | Procedure for starting a new L2R mesh | P.26 | 1 | Configuration of an L2R mesh when a device starts a new L2R mesh using profile.
6 | Procedure for joining a L2R mesh | P.32, P34 | 1 | Configuration of an L2R device when a device joins a L2R mesh using profile
7 | Mesh selection procedure | P.33 | 1 | In the case that l2rMeshSelection is FALSE, after mesh discovery process, a next higher layer of a joining L2R device needs to select a mesh to join from discovery results.
8 | Mesh root management | P.26-28 | 1 | Management related to mesh root.
9 | Mesh device management | P.28-37 | 1 | Management for join and leave..
10 | Procedure for detecting a disconnection from the L2R mesh | P.36 | 1 | When a next higher layer of an L2R sublayer is indicated that it is disconnected from the L2R mesh, it should do something.
11 | Procedure for detecting a new L2R mesh | P.43 | 1 | When L2R device finds a new L2R mesh, it should do discovery process in order to get information necessary for add ion of new entry to MT.
12 | Process for detecting an unknown neighbor | P.69 | 1 | L2R sublayer inform to its next higher layer that it detects an unknown neighbor. In this case, the next higher layer should ……
13 | Separation of concatenated frame using Dcat feature | P.73 | 1 | When Dcat is used, L2R sublayer of final destination delivers the concatenated frame to the next higher layer. It should be separated to the individual frames.
14 | Security procedure | P.78-81 | 3 | After key exchange using KMP, the exchanged key is set to the MAC PIB and other necessary security IB is set to the L2IB.

## Slide 12: Connection with profile
Interfaces often have suggestive names
  (e.g., eth0)
Create wsunN, sfoxN, … profiles.
Example
  fd=socket() hooks TCP or UDP up to profN.
  ioctl(fd,…) to insert 6lo and a PHY profile.
  ioctl(fd,…) to set the data rate, etc.
Number of ioctl() calls is arbitrary

## Slide 13: It’s all about the profile parameters…
It is needed to define the per-profile data structures (3rd parameter to ioctl())
Should probably be identical or as close as possible to MCPS.DATA parameter layout