## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IEEE 802.15.4 Update]
Date Submitted: [21 March 2017]
Source: [Pat Kinney] Company [Kinney Consulting]
Address [Lake Zurich, USA]
Voice:[+1.847.960.3715], E-Mail:[pat.kinney@kinneyconsultingllc.com]
Re: [If this is a proposed revision, cite the original document.]
Abstract: [Status updates on 802.15.4 and related standards]
Purpose: [For informational purposes to IETF 6tisch at IETF 98.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE 802.15.4 and related standards update
IEEE 802.15.4 - amendments, corrigendum, and revision
IEEE 802.15.9 – Key Management Protocol
IEEE 802.15.10 – Layer 2 Routing
IEEE 802.15.12 – Upper Layer Interface to 802.15.4

## Slide 3: IEEE 802.15.4 Approved Amendments
IEEE Std 802.15.4n: IEEE Standard for Low-Rate Wireless Networks - Amendment 1: Physical Layer Utilizing China Medical Bands
IEEE Std 802.15.4q: IEEE Standard for Low-Rate Wireless Networks -Amendment 2: Ultra-Low Power Physical Layer
IEEE Std 802.15.4t: IEEE Standard for Low-Rate Wireless Networks – Amendment 4: Higher Rate (2 Mb/s) Physical (PHY) Layer
IEEE Std 802.15.4u: IEEE Standard for Low-Rate Wireless Networks-Amendment 3: Use of the 865 MHz to 867 MHz Band in India
(Latest Revision: IEEE 802.15.4-2015)

## Slide 4: IEEE 802.15.4 amendments in process
IEEE Std 802.15.4s: IEEE Standard for Low-Rate Wireless Networks: Amendment Enabling Spectrum Resource Measurement Capability
    spectrum resource measurements, such as packet error ratio, delay, etc,
    information elements and data structures to capture these measurements,
    procedures for collecting and exchanging spectrum resource measurement information with higher layers or other devices.
IEEE Std 802.15.4v: IEEE Standard for Low-Rate Wireless Networks: Amendment Enabling/Updating the Use of Regional Sub-GHz Bands
    870-876 MHz & 915-921 MHz bands in Europe,
    902-928 MHz band in Mexico,
    902-907.5 MHz & 915-928 MHz bands in Brazil,
    915-928 MHz band in Australia/New Zealand and Asian regional frequency bands that are not in IEEE Std 802.15.4-2015.

## Slide 5: IEEE 802.15.4 Corrigendum
Two corrections are:
  64-bit MAC address transmission order
    Transmission order was reversed from earlier standards, this will be corrected, i.e. changed back to original order
  Missing value for CID in CCM* Nonce for TSCH mode
    IEEE 802.15 CID is called out to be inserted into the nonce when using the short address in TSCH mode
    IEEE 802.15 CID has been approved by IEEE Registration Authority (IEEE RA) with an assigned value of: BA-55-EC
Estimated approval date is February, 2018

## Slide 6: IEEE 802.15.4 Revision
Changes include:
  Roll-up of 6 amendments
  Inclusion of corrigenda and other corrections
  Correct ambiguities and violations of IEEE style guide
  Other?
Major effort will start in July 2017
Estimated approval date is May, 2019

## Slide 7: IEEE 802.15.9 Key Management Protocol (KMP)
KMP Recommended practice for: IEEE 802.1X/MKA, HIP, IKEv2, PANA, Dragonfly, IEEE 802.11/4WH, IEEE 802.11/GKH, ETSI TS 102 887-2.
Describes support for transporting KMP datagrams to support the security functionality present in IEEE Std 802.15.4.
Defines a general purpose multiplexed (MPX) data service
Defines a fragmentation and re-assembly protocol for payloads unable to fit in a single MAC frame.

## Slide 8: IEEE 802.15.10 Layer 2 Routing (L2R)
Recommended Practice for L2R:
  Defines protocols that route packets in a dynamically changing (order of a minute) 802.15.4 network
  Extends the area of coverage as the number of nodes increase
  Supports Data Concatenation
  Supports small, medium and large scale networks
Overview Tutorial on IEEE 802.15.10:https://mentor.ieee.org/802.15/dcn/17/15-17-0205-00-0010-overview-tutorial-on-802-15-10.pptx

## Slide 9: IEEE 802.15.12 Upper Layer Interface for IEEE 802.15.4
802.15.12 Presentation to 6tisch was done 3 February https://mentor.ieee.org/802.15/dcn/17/15-17-0113-00-0012-802-15-12-conceptual-overview.pptx.
Purpose:
  Reduction of the complexity in configuring and using the 802.15.4 device
  Addition of higher layer protocol identification
  Fragmentation of L3 datagrams
  Harmonization of L2 protocols
  Management of 802.15.4 managed objects
Updates since then:
  Configuration
  Network Management

## Slide 10: IEEE 802.15.12 paired with IEEE 802.15.4

## Slide 11: IEEE 802.15.12 Upper Layer Interface
Configuration
  Approved the concept of profiles where a profile defines all configuration parameters (i.e. data objects) necessary for 802.15.4 operation,
  Management protocol module would store the profile(s) for the 802.15.4 device and implement them into the device when instructed by a higher layer app (e.g. Netconf) or by another protocol module,
  Yang data model initially selected using a format of JSON or XML,
  Consensus was that a protocol such as Netconf could provide necessary functionality to extract or install the configuration parameters in an efficient manner, yielding a full, formal application programming interface (API).
Network Management
  Create data objects related to network performance, including those created by 802.15.4s,
  Also would be based use Netconf using a Yang data model.

## Slide 12: IEEE 802.15.12 Participation
To complete 802.15.12 in a timely fashion additional participation is requested
Participation can be via email, conference calls, conference attendance, or all of the above
Email reflector: stds-802-15-12@listserv.ieee.org
Conference call: will be set-up
Conferences:
  May 7-12, 2017, Daejeon Convention Center, Daejeon Korea, 802 Wireless Interim Session.
  July 9-14, 2017, Estrel Hotel and Convention Center, Berlin, Germany, 802 Plenary Session.
  September 10-15, 2017, Hilton Waikoloa Village, Kona, HI, USA, 802 Wireless Interim Session.*