## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Summary of changes to the base standard to support extended mmWave band]
Date Submitted: [4 May 2017]
Source: [Benjamin Rolfe] Company [Blind Creek Associates]
Address [Los Gatos, CA, USA]
Voice:[+1. 408 . 395 . 7207], E-Mail:[ben.rolfe@ieee.org]
Re: [Allocation of usable spectrum between 64GHz to 71 GHz.]
Abstract: [Summarizes the proposed changes needed to the base 802.15.3 standard (802.15.3-2016 + 802.15.3e-2017) to extend the mmWave channelization. ]
Purpose: [Use as all the available license exempt spectrum to send gigabits from point A to point B]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Scope of the project:
Extend the RF channelization of the millimeter wave PHY to allow for use of the spectrum up to 71 GHz.

## Slide 3: Approach:
Change only what needs to be changed to define use of the existing mmWave PHYs to use the spectrum recently added in the US (up to 71GHz).
Using the same channel spacing as the existing channel plan
Adds 2 additional channels to clause 11
Note: amendment 15.3e adds new clause, 11a, and a new channel plan for the HRCP PHY, which already includes channelization up to 71 GHz so no changes are needed in clause 11a.

## Slide 4: Specifics changes:
Clause 4: Change 57.0-66.0 to 57.0-71.0 (4.5.1)
Clause 11, PHY specification for millimeter wave
  Change 57.0-66.0 to 57.0-71.0 (11.1.1)
  Add 2 more channels at the end of Table 11-3 (11.1.5)
  Change phyNumChannelsSupported to remove “Value = 0x04”; already includes reference to 11.1.5
  Correct reference in 11.3.1.1 to Table 11-3
  Add additional channelization to Table 11-44
  And that’s all, folks!