## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Suitability Evaluation of Encryption Schemes]
Date Submitted: [9 July, 2017]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This document presents the suitability evaluation for different encryption schemes that may be used for LPWAN.]
Purpose: [Presentation within IG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Suitability Evaluation of Encryption Schemes
Joerg Robert, FAU Erlangen-Nuernberg

## Slide 3: Potential Options
Secure Element
  More complex device
  Time to boostrap
  More energy
  Cost

## Slide 4: Symmetric Key ( I / II )
Transmitter and receiver know the same key which has to be kept secret
Pros
Basis for many ciphers
Relatively low encoding/decoding complexity
Cons
Difficult key exchange
Secret key on user equipment
Over the air key updates difficult

## Slide 5: Symmetric Key ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Data Security
Layer-2
Layer-3
End-to-End
Secure Authentication
Data Length
<= 16 bytes
<= 64 bytes
<= 256 bytes
> 256 bytes
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour

## Slide 6: Public Key ( I / II )
Transmitter uses public key for the encryption
Decryption with private key that is only known to receiver
Pros
Basis for many authentication algorithms
Private key only known to receiver
Possibility of key exchange (only if uplink / downlink)
Cons
High encoding / decoding complexity

## Slide 7: Public Key ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Data Security
Layer-2
Layer-3
End-to-End
Secure Authentication
Data Length
<= 16 bytes
<= 64 bytes
<= 256 bytes
> 256 bytes
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour

## Slide 8: AES-128/256 ( I / II )
Transmitter and receiver use symmetric key
Pros
Well known algorithms used in many applications
Acceptable encoding / decoding complexity
Hardware acceleration in many embedded systems
Strong protection
Cons
Requires symmetric key  secret key inside user equipment
Fixed block length of 128 bits

## Slide 9: AES-128/256 ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Data Security
Layer-2
Layer-3
End-to-End
Secure Authentication
Data Length
<= 16 bytes
<= 64 bytes
<= 256 bytes
> 256 bytes
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour

## Slide 10: RSA ( I / II )
Transmitter uses public key for the encryption
Decryption with private key that is only known to receiver
System based on prime numbers as trap-door function
Pros
Well known algorithms used in many applications
Strong protection
Method can be used for secure authentication
Allows for key updates
Cons
Approx. 1000 time more complex than AES  normally only used for key exchange
Long key length of several kBit

## Slide 11: RSA ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Data Security
Layer-2
Layer-3
End-to-End
Secure Authentication
Data Length
<= 16 bytes
<= 64 bytes
<= 256 bytes
> 256 bytes
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour

## Slide 12: Elliptic Curves ( I / II )
Transmitter uses public key for the encryption
Decryption with private key that is only known to receiver
Pros
Similiar properties to RSA based on prime numbers
More difficult to hack compared to prime numbers for similar key length  shorter keys
Method can be used for secure authentication
Allows for key updates
Cons
Significantly more complex than AES

## Slide 13: Elliptic Curves ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Data Security
Layer-2
Layer-3
End-to-End
Secure Authentication
Data Length
<= 16 bytes
<= 64 bytes
<= 256 bytes
> 256 bytes
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour

## Slide 14: Over the Air Key Update ( I / II )
Network updates key
Pros
Improved security
Simple reconfiguration
Cons
Requires asymmetric encryption
Requires bi-directional communication

## Slide 15: Over the Air Key Update ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Data Security
Layer-2
Layer-3
End-to-End
Secure Authentication
Data Length
<= 16 bytes
<= 64 bytes
<= 256 bytes
> 256 bytes
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour

## Slide 16: Any Questions or Comments?