## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Suitability Evaluation of Network Topologies]
Date Submitted: [9 July, 2017]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This document presents the suitability evaluation for different network topologies that may be used for LPWAN.]
Purpose: [Presentation within IG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Suitability Evaluation of Network Topologies
Joerg Robert, FAU Erlangen-Nuernberg

## Slide 3: Star (single hop) ( I / II )
One central base-station receives data of user devices
Pros
Simple user devices
Only few powerful base-stations
No additional latency due relaying
Cons
User devices have to be able to achieve the required cell radius  low bit-rates

## Slide 4: Star (single hop) ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
July 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 5: Extended Star (single hop) ( I / II )
Multiple base-stations receive data of user devices
Pros
Simple user devices
Only few powerful base-stations
No additional latency due relaying
Additional diversity
Possibility for upgrading the network in case of increased traffic
Cons
Multiple distributed base-stations are required

## Slide 6: Extended Star (single hop) ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
July 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 7: Device to Device ( I / II )
Only communication between devices
Pros
No infrastructure
Cons
Only short range

## Slide 8: Device to Device ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
July 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 9: Mesh ( I / II )
Only communication between devices
Pros
No base stations required
Cons
Devices have to relay data for other devices  unpredictable latency, power consumption, etc.
Devices have to support transmission and reception
Configuration of network is time demanding, synchronization of the network required
Ultra long latency in case of long data periods

## Slide 10: Mesh ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
July 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 11: Any Questions or Comments?