## Slide 1
Project: IEEE P802.15 Interest Group for Wireless Personal Area Networks (WPANs)
Submission Title: [S2-PSK for V2V communication]
Date Submitted: [July, 2017]
Source: [Md. Tanvir Hossan, Trang Nguyen, Amirul Islam, and Yeong Min Jang]
Company [Kookmin University]
Address [Seoul, Korea]
Voice:[+82-2-910-5068], FAX: [+82-2-910-4449], E-Mail: [yjang@kookmin.ac.kr]
Re: []
Abstract: [Implementation optical camera communication (OCC) in transportation system to ensure detect and communicate with other vehicles]
Purpose: [Report progress to WG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE 802.15 IG VAT Spatial 2-Phase Shift Keying (S2-PSK) for vehicle-to-vehicle (V2V) communication

## Slide 3: Introduction
V2V communication and vehicle detection plays an increasingly important role in traffic control, surveillance applications, and autonomous driving.
These are more challenging in both day and night time due to the low contrast and luminosity.
Region-of-interest (RoI) signaling techniques applied to camera (Rx) ton achieve high frame rate for RoI based V2V communication and vehicles detection.

## Slide 4: RoI signaling system using S2-PSK (1/2)
The transmission of RoI is beneficial when the camera Rx knows the area in which the communication link should be setup.
The light source Tx shall continuously inform the camera Rx via a known signal for differentiating the light source Tx from other non-interested light sources and other objects.
The transmission of the known signal is a type of light source identification.

## Slide 5: RoI signaling system using S2-PSK (2/2)

## Slide 6: RoI signaling S2-PSK waveform (1/2)
The camera Rx first detects the RoI from the light source identification signal, and then selects the RoI to accelerate the frame rate and achieve high-speed data link.
The low frame-rate (e.g. 30fps) camera shall be used to detect the RoI to reduce cost.

## Slide 7: RoI signaling S2-PSK waveform (2/2)