## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Demand of Highly Reliable Wireless Network and Future Vision for Car Manufacturing Line in Factory
Date Submitted: July 11, 2017
Source: Hiroshi Kobayashi(Nissan Motors, Co.)
Voice: :+81-50-2029-4907, E-Mail: h-kobayashi@mail.nissan.co.jp
Re: IG DEP 15-15-0221-00-Development of Wireless Sensing System for Factory
IG DEP 15-17-0077-00-Updated Development of Wireless Sensing System for Factory
Abstract Update of previous presentation of Nissan Automotive representative
Development of Wireless Sensing System for Factory
Purpose: This document is presented to support promotion of a new standard making by IG-DEP(Dependability) as a representative of association of factory facilities.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
A Response to Call for Interest(CFI) of IEEE 802.15 IG DEP
Demand of Highly Reliable Wireless Network and Future Vision for Car Manufacturing Line in Factory
Ref. 15-15-0221-00-IG-DEP-Development-of- Wireless-Sensing-System-for-Factory & 15-17-0077-00-its updated version
Berlin, Germany July, 2017
Hiroshi Kobayashi, Nissan Motors, Co.

## Slide 3: Agenda
Background
Updated New Type of Equipment Diagnosis System by using wireless sensor devices
Required specification
Future Activity

## Slide 4: Agenda
Background
Updated New Type of Equipment Diagnosis System by using wireless sensor devices
Required specification
Future Activity

## Slide 5: Background
Improve OEE
Reduce Cost
Reliability
MBD

## Slide 6: 1) Example of Major Breakdown
Crack

## Slide 7
2) Example of Major Breakdown
Cable
Disconnection
Cable
Disconnection

## Slide 8: TBM: Time Based Maintenance
Chronic Failures
Deterioration
Factors to deteriorate
Occurred Failures
Reactive Maintenance
MBD
Sporadic Failures
Potential Failures
Proactive Maintenance
New Equipment
Manual Inspection
Periodical check
Preventive Maint.
Stress!
We need a lot of man power of maintenance.
Slide 8

## Slide 9: Other reasons why we need to improve “Equipment Reliability” a) Equipment automation rate is increasing. => No operator and More maint. tech. b) Production volume is increasing => No or less maintenance window & maintenance time ( 2shift => 3 shift) c) Lack of skill for maintenance => We need new equipment diagnosis system that does not require us new skill.

## Slide 10: Agenda
Background
Updated New Type of Equipment Diagnosis System by using wireless sensor devices
Required specification
Future Activity

## Slide 11
< Condition Monitoring System >
< Periodical Manual Inspection >
Ex. Cable deterioration
Ｕ
＋
－
Cable Tester
Disconnection Ratio
CBM Server
OA－LAN
Intranet
FA-LAN
Ｕ
＋
－
Alarm
Monitor of Cable Resistance
Ｕ
＋
－
Sensor to detect cable deterioration
Concept for Equipment Diagnosis System
Failure
Notes: •a diameter

## Slide 12
Time Axis
Cost Minimum and High Reliability
< Condition Monitoring System for Cable Disconnection >
Very sensitive
Good Reliability to detect potential failure
Extend Life Time
Parts Life Time
Real –Time Diagnosis
Maintenance Worker’s job
CBM
Real-time CBM
Failure
TBM
Cable Disconnection Ratio
Ｕ
＋
－
We need Good Real-Time Diagnosis System
Concept for Equipment Diagnosis System
Condition Based Maintenance
Time Based Maintenance

## Slide 13
< Conventional Development Procedure >
Ordinary approach to develop “Diagnosis system”
Cable Disconnection
Deteriorated Reducers
Failure mode, Failure type
Deteriorated Power Supply
Breakdown time
Sensor
Data Logger
Diagnosis
Logic
Individual system
This method requires us a lot of
time and cost to develop.

## Slide 14
Courtesy of Prof. Jay Lee, NSF I/UCRC on Intelligent Maintenance Systems (IMS),
Univ, of Cincinnati
To accelerate Development Speed
We have to consider a new approach to develop!

## Slide 15
< Conventional Development Procedure >
New approach to develop “Diagnosis system”
Cable Disconnection
Deteriorated Reducers
Failure mode, Failure type
Deteriorated Power Supply
Breakdown time
Sensor
Data Logger
Diagnosis
Logic
Individual system
Receiver
PC
Rooter
To cover whole area！
Multi-sensor
Sensor
Storage & Logic
①AE
②Vibration
③Thermal
④Current
⑤ Voltage
・・・・

## Slide 16
Comparison between “wired system”and “wireless system”
< Conventional Development Procedure >
Sensor
Data Logger
Diagnosis
Logic
Individual system
Receiver
PC
Multi-sensor
PC
Installation Cost
Restriction of installation
Installation Issues
Reliability of wires
< New Development Procedure >
Sensor
Storage & Logic

## Slide 17: Agenda
Background
Updated New Type of Equipment Diagnosis System by using wireless sensor devices
Required specification
Future Activity

## Slide 18: Required specification
3 type of Diagnosis System
  Equipment Diagnosis System in Real-time with rea-time feedback
    Real-time measuring
    Judge immediately with a certain threshold level
  Equipment Diagnosis System in Real-time (1)
    Real-time measuring and sending data in real-time
    Judge based on the comparison with the past data
  Equipment Diagnosis System in Real-time (2)
    Real-time measuring and sending data intermittently
    Judge based on the comparison with the past data
A
B
C

## Slide 19: Required specification
3 type of Diagnosis System
  Equipment Diagnosis System in Real-time with rea-time feedback
    Real-time measuring
    Judge immediately with a certain threshold level
  Equipment Diagnosis System in Real-time (1)
    Real-time measuring and sending data in real-time
    Judge based on the comparison with the past data
  Equipment Diagnosis System in Real-time (2)
    Real-time measuring and sending data intermittently
    Judge based on the comparison with the past data
A
B
C

## Slide 20
20
Versatile Sensor
Cloud Server
AP
CBM Server
１： Historical data analysis
２：
A
B
C
Alarm
Monitor of Cable Resistance
AP

## Slide 21
IMS Sensor
A
Alarm

## Slide 22: Required specification
3 type of Diagnosis System
  Equipment Diagnosis System in Real-time with rea-time feedback
    Real-time measuring
    Judge immediately with a certain threshold level
    Send alarm
  Equipment Diagnosis System in Real-time (1)
    Real-time measuring and sending data in real-time
    Judge based on the comparison with the past data
  Equipment Diagnosis System in Real-time (2)
    Real-time measuring and sending data intermittently
    Judge based on the comparison with the past data
A
B
C

## Slide 23
23
Versatile Sensor
Cloud Server
AP
CBM Server
１： Historical data analysis
２：
A
B
C
Alarm
Monitor of Cable Resistance
AP
Alarm

## Slide 24: Required specification
3 type of Diagnosis System
  Equipment Diagnosis System in Real-time with rea-time feedback
    Real-time measuring
    Judge immediately with a certain threshold level
    Send alarm
  Equipment Diagnosis System in Real-time (1)
    Real-time measuring and sending data in real-time
    Judge based on the comparison with the past data
  Equipment Diagnosis System in Real-time (2)
    Real-time measuring and sending data intermittently
    Judge based on the comparison with the past data
A
B
C

## Slide 25
25
Versatile Sensor
Cloud Server
AP
CBM Server
１： Historical data analysis
２：
A
B
C
Alarm
Monitor of Cable Resistance
AP
Alarm

## Slide 26
< Conventional Development Procedure >
Cable Disconnection
Deteriorated Reducers
Failure mode, Failure type
Deteriorated Power Supply
Breakdown time
Sensor
Data Logger
Diagnosis
Logic
Individual system
To cover whole area！
Cloud Server
AP
Multi-sensor
Alarm
New approach to develop “Diagnosis system”

## Slide 27: Required specification
Specification for Equipment Diagnosis System
  Response
    Real-time measuring function to communicate with receiver in real-time
    Judge immediately with a certain threshold level
  Energy consumption
    In order to prolong a life time of measuring device save energy and have good efficiency regarding communication power * At least 1 year or more
  Bilateral communication ability
    In order to change some parameters and firmware in the device
    and give some triggers to start and end measuring from outside
Notes: Intermittent 間欠な

## Slide 28: Required specification
Specification for Equipment Diagnosis System
  4. Distance to communicate with devices
    In order to reduce the number of receivers, device have to have some distance to communicate. At least 20m or more
  5. Data transfer speed
    This sensor will have multi-sensors. So data transfer speed is very important.
  6. Communication capability with many sensors
    How many sensors can communicate at the same time
  7. Kinds of Sensors
  ① Vibration sensor ② Thermal sensor
  ③ Voltage ④ Current
  ⑤ AE （Acoustic Emission）
Notes: Intermittent 間欠な

## Slide 29: Agenda
Background
New Type of Equipment Diagnosis System by using wireless sensor devices
Required specification
Future Activity

## Slide 30: Future Activity
  Prototyping Equipment Diagnosis System in Real-time with rea-time feedback with Dependable Short Range Wireless Networks
    Highly reliable real-time measuring with short range radio sensor network
    Highly secure decision immediately with measured data by wireless network of various sensors and past recorded data
    Strongly protected alarm and commands to equipment in a line for dependable remote monitoring and maintenance
  IoT/Big Data/Mining through Cloud Network Using Equipment Diagnosis System in Real-time with rea-time feedback
    Build up Nissan in-house equipment diagnosis system in real-time sensing and controlling with dependable wireless feedback network
    Entire remote sensing and controlling FA equipment diagnosis system with IoT/Data Mining server through cloud network
  International Standard Establishment with All other Institutes and Companies
    Though associations of automotive industries and other manufactures, common standard equipment diagnosis system using wireless dependable short range sensing and controlling will be established.
    IEEE802.15 may be the best venue of establishing a standard of dependable wireless feedback network for global common equipment diagnosis system.

## Slide 31: Future Activity
Sensor
Data Logger
Diagnosis
Logic
Individual system
1) Takes a lot of time to develop
Issues of traditional method
2) Difficult to deploy
3) Cost issue
4) Some special person just use
Sensor
Storage & Logic
Versatile
Sensor
Cloud
31
31
Versatile Sensor
1) Multi-sensor Wire-less ⇒ Shorten Dvpmt. time
Versatile Sensor （Standardized Diagnosis System）
2) Easy to deploy because of same structure
3) Cost minimum and reduce developing cost
4) Everybody can create a diagnosis logic
①AE
②Vibration
③Thermal
④Current
⑤ Voltage