## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: System Issues for Vehicular OWC Applications
Date Submitted: July 2017
Source: Soo-Young Chang (SYCA), Jaesang Cha (SNUST)
Address:
Contact Information: 530 574 2741 [sychang@ecs.csus.edu], +82-2-970-6431 [chajs@seoultech.ac.kr]
Re:
Abstract: Some system requirements/issues for vehicular OWC applications are identified in this document.
Purpose: To suggest some technical requirements/issues for vehicular applications.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Contents
Problems to be solved for ITS
Reference

## Slide 3: PROBLEMS TO BE SOLVED FOR ITS (1)
Link set-up time <10 ms
  The most crucial and time-consuming part in a multi-node environment is the link-setup procedure.
  Especially in a free space situation with unpredictable and fast changing link conditions.
  TDMA Scheme enables a very fast link set-up.
    The protocol establishes a new communication link, exchanges data on this link, and closes the link within only one frame.
    Furthermore it provides a very fast link re-establishment within one frame after short break-outs.

## Slide 4: PROBLEMS TO BE SOLVED FOR ITS (2)
Beam forming and zone sectoring
  Appropriate beam forming and/or zone sectoring may be needed to share communication resources and to exchange information with right communication partners by directing in right directions with appropriate beam widths.
  Focusing
  Beam shaping
  Multi beam antennas
  Defining communication zones
  Supporting multiple links at the same time

## Slide 5: PROBLEMS TO BE SOLVED FOR ITS (3)
Few milliseconds latencies and communication delays.
Need of distance estimation of the communicating party (?)
Interference mitigation to be provided (?)
Adaptive data speed with minimum speed of 1 Mbps
  The data transmission speed is negotiated at the set-up of the link and can be changed during the communication session.
  Adaptive modulation schemes to data rates
Handover needed (?)
  A Handover is possible in the same medium (visible light to visible light) as well as between different media (e.g. visible light to IR or Microwave) to guarantee the continuity of the communication session.

## Slide 6: PROBLEMS TO BE SOLVED FOR ITS (4)
Multiple types of communications
  Point-to-Point
  Point-to-Multipoint
  Multiple Point-to-Multipoint
  Broadcast
  Multicast
  Anycast
  Master-Slave
Master-slave setting for TDMA management
  802.22.1 PPD-SPD set-up procedure may be applied.
New node registration to the network
Collision problem to be solved

## Slide 7: REFERENCES
International Standard ISO 21214. Intelligent transport systems – Continuous air interface, long and medium range (CALM) – Infrared systems. July 2006
Rumpf, S. (2006). CALM-general – presentation for the South Korean CALM meeting 2004 in Seoul.
Werner Rom et al., The novel International Standard ISO 21214: Intelligent transport systems – Continuous air interface, long and medium range (CALM) – Infrared systems.