## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Discussion dimming methods
Date Submitted: July, 2017
Source: Hideki Aoyama Panasonic Corporation contact: aoyama.hideki@jp.panasonic.com
Abstract: Reorganizing dimming subclause
Purpose: Support drafting the standard document
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Original 15.7 dimming
Idle pattern
  Any in-band or out-of-band patterns during idle time (= between PHY frames)
Compensation symbol
  ON or OFF
Visibility pattern
  In-band pattern in CVD frame
CSK dimming
  Amplitude dimming
OOK dimming
  Compensation symbol followed by resync field
VPPM dimming

## Slide 3: New dimming subclauses (PHY 4 and 5)
8.5.2.4.1 UFSOOK dimming
  PWM dimming
8.5.2.4.2 Offset-VPWM dimming
  Not supported
8.5.2.4.3 S2-PSK dimming
  Amplitude dimming
8.5.2.4.4 Hybrid Spatial PSK dimming
  ???
8.5.2.5.1 Twinkle VPPM dimming
  Amplitude dimming
8.5.2.5.2 RS-FSK dimming
  PWM dimming
8.5.2.5.3 FSK dimming
  PWM dimming
8.5.2.5.4 C-OOK OOK dimming
  Amplitude dimming
8.5.2.5.5 3 Packet PWM/PPM dimming (MPM dimming)
  Amplitude dimming, Out-of-band dimming, PWM dimming, idle time dimming
PWM dimming:
Dimming by controlling when light intensity drops off, utilizing that the protocols do not concern it.
Out-of-band dimming:
Dimming by controlling duty cycle at frequency out of the protocol frequency band, which a receiver cannot recognize or can ignore it.

## Slide 4: New dimming subclauses (PHY 6)
8.5.2.6.1 IDE Dimming
  “Dimming is supported by controlling visual scene high frequency background color.”
8.5.2.6.2 A-QL dimming
  Not supported
8.5.2.6.3 VTASC dimming
  Not supported
8.5.2.6.4 Hidden A-QL dimming
  “Dimming is hence supported by controlling the background color.”
8.5.2.6.5 SS2DC Dimming
  Not supported
How to realize dimming by controlling background color?

## Slide 5: Suggested combined dimming methods
Idle time dimming
  Any in-band or out-of-band patterns during idle time
CVD frame dimming
  Using visibility patterns
Amplitude dimming
  Controlling light intensity of ON and/or OFF state
OOK dimming
  Compensation symbol followed by resync field
VPPM dimming
  Controlling duty cycle of VPPM
PWM dimming
  Controlling when light intensity drops off
Out-of-band dimming
  Controlling duty cycle at frequency out of a protocol frequency band

## Slide 6: Original 15.7 dimming
Idle pattern
Compensation symbol
  Deleted and moved to OOK dimming subclause
Visibility pattern
CSK dimming
  Changed to amplitude dimming
OOK dimming
VPPM dimming

## Slide 7
 | Idle time | CVD frame | Amplitude | OOK | VPPM | PWM | Out-of-band
PHY I | x | x | X |  |  |  | 
PHY II | x | x | x |  |  |  | 
PHY III | x | X | x |  |  |  | 
UFOOSK | X |  | X |  |  |  | 
S2-PSK | X |  | X |  |  |  | 
S8-PSK | X |  | X |  |  |  | 
HS-PSK | X |  | X |  |  |  | 
Offset-VPWM | X |  | x |  |  |  | 
Twinkle VPPM | X |  | X |  |  |  | 
RS-FSK | X |  | X |  |  |  | 
CM-FSK | X |  | X |  |  |  | 
C-OOK | X |  | X |  |  |  | 
MPM | x |  | X |  |  |  | 
(PHY VI) |  |  |  |  |  |  | 

## Slide 8: Subclause 4.4.3 and 8.5
Original 15.7 was also confusing what is described in 4.4.3 and 8.5 (and there are some duplications)
My suggestions are:
  Show only dimming method list (in slide 5) in 4.4.3
  Describe in detail in 8.5