## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IG DEP Discussion on Necessity of a New Standard for Enhanced Dependability in Wireless Networks for focused applications]
Date Submitted: [12 July 2017]
Source: [Ryuji Kohno1,2,3, Jussi Haapola2] [1;Yokohama National University, 2;Centre for Wireless Communications(CWC), University of Oulu, 3;University of Oulu Research Institute Japan CWC-Nippon]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501
2; Linnanmaa, P.O. Box 4500, FIN-90570 Oulu, Finland FI-90014
3; Yokohama Mitsui Bldg. 15F, 1-1-2 Takashima, Nishi-ku,Yokohama, Japan 220-0011]
Voice:[1; +81-45-339-4115, 2:+358-8-553-2849], FAX: [+81-45-338-1157],
Email:[kohno@ynu.ac.jp, ryuji.kohno@oulu.fi, jhaapola@ee.oulu.fi] Re: []
Abstract: [This document describes discussion on necessity of a new standard for enhanced dependability in wireless networks for focused applications mainly in automotive industry by summarized review of responses for CFI and interviews for prospective users of the standard.]
Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE 802.15 IG DEP Discussion on Necessity of a New Standard for Enhanced Dependability in Wireless Networks for Focused Applications Ryuji Kohno(YNU/CWC-Nippon) Jussi Haapola(CWC)

## Slide 3: Summary of Previous and Current Discussion
By surveying responses for Call for Interests (CFI) and interviews for prospective users, IG-DEP has confirmed demands for a new standard and chosen the focused applications.
For the focused applications or use cases, IG-DEP has been summarized technical requirements for a new standard.
In order to satisfy some unique and mandatory technical requirements in the focused use cases, IG-DEP has been discussing on possibility of current existing standards good enough for expecting users.
To make sure uniqueness for expecting new standard and relationship with other groups who are dealing some common applications and different approach to similar target to IG-DEP such as 802.1 FFPJ, 802.24, 802.15.4s, and IETF 6TiSCH with managing by 802.12 etc.
IG-DEP would like to propose to make a new standard in IEEE802.15 to satisfy such requirements by collaborating with other groups which have been covering the same or related subjects.

## Slide 4: Proposed applications
Remote healthcare monitoring
Remote sensing and controlling
Vehicle internal sensing and controlling
Collision avoidance radar
Inter-vehicle communications and ranging
Wearable and implant wireless medical sensing and controlling
Applications for ultra wideband radio
Reliable and robust radio control
Wearable healthcare sensing
Secure remote healthcare and medicine
Wireless sensing system for Factory with feedback control
Dependable multi-hop inter-vehicle communications
Inter-navigation and inter-vehicle information sharing in normal and emergency conditions
Single wireless communication network solution that functions both in normal and in disaster environments
Disaster prevention, emergency rescue and recovery
July 2017

## Slide 5
Fitness, Massage
& Sauna
Sports: Walking, Jogging,
Bicycling, Hiking, Skiing etc
Public Safety
Inter-Vehicle M2M
Highly Life Critical Uses(High QoS)
Less Life Critical Uses(Low QoS)
Home &
Consumer
Uses
Industrial &
Governmental
Uses
Internal Car Dependable M2M
Inter-Vehicle M2M
Home Medical Therapy
Government Infrastructure
Visualizing Portfolio of Focused Applications
Remote Diagnosis
for Factory Automation
Hospital Clinical Service
Remote Wellness
& Well-being
QoS 3; Relatively Lower Priority for
Demand of Dependability
  Life Line
  (Water/Gas/Electricity Supply)
Car, Bldg Care
business
Entertainment business
Regulatory Compliance
Test
Big Data Mining
Remote Sensing
& Controlling Mobile Robots
Disaster Analysis
& Prevention
Remote Diagnose
s of Infra(bridge/bldg./train)
QoS 2; Middle Priority of Demand of Dependability
QoS 1; Highest Priority of Demand
of Dependability

## Slide 6: Selected Focused Applications
According to a scale of demand and priority of QoS, IG-DEP has chosed the following three major use cases in automotive industry.
Wireless intra-vehicle communications (car bus supplement) to support CAN and RIM or providing better performance by wireless and wired integration for M2M inside a car.
Wireless inter-vehicle (V2V) and vehicle to infrastructure communications (V2I) to support safe driving and traffic management by wireless ranging and communication.
Wireless remote sensing and control in car manufacturing factory to maintain stable, safe and efficient management by dependable wireless networks.
July 2017

## Slide 7: Technical Challenges for Enhanced Dependability
First of all, we should recognize that any technology in PHY and MAC cannot guarantee full dependability in every use case.
However, we can design a new standard which can guarantee a certain level of enhanced dependability in a specific defined use case.
As an analogy of informed consent in medical doctor to a patient, a manufacturer of a dependable wireless network can describe such a specific defined use case that the manufacture can guarantee a defined level of dependability showing necessary cost and remained uncertainty. This is an honest manner and much better than no guarantee for any use case.
Therefore, an expecting standard describes a specific use case in which worst performance can be guaranteed enough high while most of exiting standards have been designed with average performance base.
Technical requirement for the specific use case can be guaranteed.
July 2017

## Slide 8: Discussion on Uniqueness for an expecting new standard in IG-DEP different from existing IEEE802.11 & 15 standards
MAC protocol for around packets and recursive access for feedback loop in remote sensing and controlling;
Level of dependability can be defined with showing necessary cost and remained uncertainty. This is an honest manner and much better than no guarantee for any use case.
Worst performance can be guaranteed enough high while most of exiting standards have been designed with average performance base.
Others
July 2017

## Slide 9: Uniqueness for an expecting new standard in IG-DEP different from existing IEEE802.11 & 15 standards(1/2)
MAC protocol for around packets and recursive access for feedback loop in remote sensing and controlling;
  Most of major use cases taken care in IG-DEP assume feedback loop for remote monitoring sensors or radars and feedback controlling actuators such as robotics and a brake. IG-DEP defines a new MAC protocol for such around packets that are pairs of corresponding packets in between uplink from sensor nodes to a coordinator and downlink from a coordinator to actuator nodes.
  Such around packets are used to access recursively to make a system stable convergence.
  So such MAC as to guarantee maximum feedback around or loop delay should be less than a threshold.

## Slide 10: Uniqueness for an expecting new standard in IG-DEP different from existing IEEE802.11 & 15 standards(2/2)
2. PHY technologies to satisfy technical requirement for enhanced dependability in the focused applications of in automotive industry.
  In feedback loop for remote monitoring sensors or radars and feedback controlling actuators, real-time cognition of varying condition on site and adaptive reconfiguration in relatively messy, small, and dense areas are requested to guarantee worst performance with permissible delay and errors.
  Within a permissible limited feedback delay, propagation paths connecting between nodes and coordinator should be found to keep connectivity by diversity, channel switching etc. .
  For such a dynamic environment and QoS requirement changing situation, sophisticated PHY technologies are requested to guarantee minimum requirement of performance.

## Slide 11: Four main points to address
1. Cross-layer information exchange and management PHY&MAC <-> higher layers
- To guarantee service levels
- To know flow characteristics
- To know dynamic media characteristics
- Be energy aware
2. Application of metrics at specific layers and cognition in layers
- To improve stability
- To improve predictability
- To enable feedback loops
3. Forwarding protocol
- To apply path diversity and redundancy adaptively
o Routing and forwarding time scales are vastly different
o Application stability is yet another order of magnitude longer time scale, but may change over time.
4. Coordination and management across independent PANs
- Other PAN interference mitigation
Task is to reflect the above to the key three applications in vehicular automation.
(c.f. 802.15.9 PAR)

## Slide 12: Contributions
Every application may not be comprehensively described but major applications must be covered.
If you can offer further details, any updated parameters or free comments are always welcome.
Send content contributions to
Jussi Haapola <jussi.haapola@ee.oulu.fi> and
Ryuji Kohno <kohno@ynu.ac.jp>

## Slide 13
Thank You !
Any Questions ?