## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Discussion on PHY Attributes
Date Submitted: July 2017
Source: Jaesang Cha, Vinayagam Mariappan (SNUST), Soo-Young Chang (CSUS)
Address: Contact Information: +82-2-970-6431, FAX: +82-2-970-6123, E-Mail: chajs@seoultech.ac.kr Re:
Abstract: This documents describes how to the reorganizing PHY Attribute Table and introduce the supporting tables . This proposed. This proposed PHY attributes used for IoT/IoL, LEDIT, Digital Signage with Advertisement Information etc..
Purpose: To support drafting the standard document
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Table 125 - PHY PIB attributes
Attribute | Identifier | Type | Range | Description
phyOccMcsID |  | int | 0~255 | This attribute define the identifier for OCC modulation. Refer Table 125-EXT1
phyOccOpticalClock- Rate |  | int | 0~TBD | This attribute use to specify the optical clock rate used in the modulation method
phyOccRLLCode |  | int | 0~255 | This specifies the RLL coding corresponding to the specific OCC modulation. Refer Table 125-EXT2
phyOccFec |  | int | 0~255 | This attribute specifies FEC corresponding to the specific OCC modulation. Refer Table 125-EXT3

## Slide 3: Table 125-EXT1 – PHY OCC MCSID Attribute Configuration
phyOccMcsID | PHY Modulation
0 | S2-PSK
1 | HS-PSK
2 | CM-FSK
3 | MPM
4 | A-QL
5 | Hidden A-QL (HA-QL)
6 | VTASC
7 | IDE
8~255 | Reserved

## Slide 4: Table 125-EXT1 – PHY RLL Code Attribute Configuration
phyOccRLLCode | RLL Code
0 | None
1 | Differential code ½ rate
2 | 3 bits Grey code
3 | 1/2 code rate
4 | Manchester
5 | 4B6B coding
8~255 | Reserved

## Slide 5: Table 125-EXT1 – PHY FEC Attribute Configuration
phyOccFec | PHY Modulation
0 | None
1 | RS(15,11)
2 | RS(15,2)
3 | RS(15,4)
4 | Temporal repeating code with DS rate=100
5 | Temporal repeating code with DS rate=60
6 | XOR FEC
7 | Hamming (11,15)
8~255 | Reserved