## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Qualitative Use-Case Evaluation]
Date Submitted: [11. Sept, 2017]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This document presents the first version of the qualitative use-case evaluation]
Purpose: [Prensentation in IG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Qualitative Use-Case Evaluation
Joerg Robert (FAU Erlangen-Nuernberg)

## Slide 3: General Evaluation Procedure
Suitability
  Analysis the general suitability of a candidate technology
Qualitative Evaluation
  Analysis pros and cons, and dependency on other technologies
Quantitative Evaluation
  Exact performance (only for selected technologies)
This document

## Slide 4: Motivation
Analyze the remaining use-cases
  Derive a set of combined technology options that are able to cover the requirements according to the suitability evaluation documents in an optimal way
  Figure out whether existing IEEE standards offer the combined technology options
Analyze the communalities between the reaming uncovered use-cases

## Slide 5: Uncovered or Potentially Improvable Use-Cases
Domain | Use-Cases
Agriculture and Environmental | 
Consumer/Medical | Pet Tracking
Industrial | Industrial Plant Condition Monitoring
Infrastructure | Pipeline Monitoring – Terrestrial, Smart Grid - Fault Monitoring, Smart Grid - Load Control, Smart Metering, Structural Health Monitoring
Logistics | Global Tracking, Fast Asset Tracking
Smart Building | 
Smart City | Public Lighting, Smart Parking, Vending Machines – general, Vending Machines - Point of Sale, Waste Management

## Slide 6: Industrial: Industrial Plant Condition Monitoring
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | None
Active Interfering Users | Medium
Communication Mode | Uplink/Broadcast Downlink
Data Period | Occasionally 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <10s
LP-WAN Localization Precision | <10m
Typical Power Supply | Energy Harvesting
Frequency Regulation | NA
Cell Radius | <50km
Data Security | Layer-3

## Slide 7: Industrial: Industrial Plant Condition Monitoring
Modulation:
  Precise localization requires broadband signal
  No interference (licensed spectrum) and low number of users
   spreading modulation
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Low number of users
  Latency < 10s
   fully synchronized network

## Slide 8: Industrial: Industrial Plant Condition Monitoring
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Medium number of active users
  Latency < 10s
  Full synchronized network
All requirements are already fulfilled by 802.15.4

## Slide 9: Infrastructure: Pipeline Monitoring – Terrestrial
Channel Model | Parameter
Channel Model | Outdoor Rural
Interference Model | None
Active Interfering Users | Low
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | <100m
Typical Power Supply | Energy Harvesting
Frequency Regulation | NA
Cell Radius | <50km
Data Security | Layer-2

## Slide 10: Infrastructure: Pipeline Monitoring – Terrestrial
Modulation:
  Precise localization requires broadband signal
  No interference (licensed spectrum) and low number of users
   spreading modulation
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Low number of users
  Latency < 10s
   fully synchronized network

## Slide 11: Infrastructure: Pipeline Monitoring – Terrestrial
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Low number of active users
  Latency < 1min
  Extended star
All requirements are already fulfilled by 802.15.4

## Slide 12: Infrastructure: Smart Grid - Fault Monitoring
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | <100m
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <50km
Data Security | Layer-2

## Slide 13: Infrastructure: Smart Grid - Fault Monitoring
Modulation:
  Localization precision <100m
  Strong interference and many users
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1min
   only ALOHA may work

## Slide 14: Infrastructure: Smart Grid - Fault Monitoring
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  High number of active users with interference
  Latency < 1min
  Extended star
Not covered by existing standards

## Slide 15: Infrastructure: Smart Grid - Load Control
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | None
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Occasionally, more than 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1s
LP-WAN Localization Precision | Not required
Typical Power Supply | External
Frequency Regulation | NA
Cell Radius | <10km
Data Security | Secure Authentication

## Slide 16: Infrastructure: Smart Grid - Load Control
Modulation:
  Localization precision <100m
  No interference
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, no interference
  Uplink and downlink
  Latency < 1s
   Fully synchronized network

## Slide 17: Infrastructure: Smart Grid - Load Control
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  High number of active users no interference
  Latency < 1min
  Star or extended star
Covered by 802.15.4

## Slide 18: Infrastructure: Smart Metering
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Broadcast Downlink
Data Period | Periodically 1/day
Data Length (Uplink) | <=16bytes
Availability | Medium
Latency | <1day
LP-WAN Localization Precision | Not required
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | End-to-end

## Slide 19: Infrastructure: Smart Metering
Modulation:
  Localization not required an high interference
  High interference and many users
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Very high number of users, strong interference
  Uplink and broadcast downlink
  Latency < 1day
   Not covered yet

## Slide 20: Infrastructure: Smart Metering
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1day
  Star or extended star
Not covered by existing standard

## Slide 21: Infrastructure: Structural Health Monitoring
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | Not required
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-2

## Slide 22: Infrastructure: Structural Health Monitoring
Modulation:
  Localization not required an high interference
  High interference and many users
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Very high number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work

## Slide 23: Infrastructure: Structural Health Monitoring
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1min
  Star or extended star
Not covered by existing standard

## Slide 24: Logistics: Global Tracking
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Periodically 1/hour
Data Length (Uplink) | <=16bytes
Availability | Best effort
Latency | <10min
LP-WAN Localization Precision | <100m
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-3

## Slide 25: Logistics: Global Tracking
Modulation:
  High interference and many users
  Localization < 100m
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Very high number of users, strong interference
  Uplink only
  Latency < 10min
   Only ALOHA may work

## Slide 26: Logistics: Global Tracking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 10min
  Extended star
Not covered by existing standard

## Slide 27: Logistics: Fast Asset Tracking
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | High
Communication Mode | Uplink
Data Period | more than 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1 min
LP-WAN Localization Precision | <10m
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-2

## Slide 28: Logistics: Fast Asset Tracking
Modulation:
  High interference and many users
  Localization < 10m
   Spreading modulation, but only if many base stations are used
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work

## Slide 29: Logistics: Fast Asset Tracking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Precise localization
  Latency < 1min
  Extended star
Potentially covered by 802.15.4

## Slide 30: Smart City: Public Lighting
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Occasionally 1/hour
Data Length (Uplink) | <=16bytes
Availability | Medium
Latency | <1min
LP-WAN Localization Precision | Not required
Typical Power Supply | External
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Secure Authentication

## Slide 31: Smart City: Public Lighting
Modulation:
  High interference and many users
  Localization not required
   FHSS (or other schemes in case of mesh)
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only and downlink
  Latency < 1min
   Not covered yet (or CSMA and unsynchronized mesh)

## Slide 32: Smart City: Public Lighting
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1min
  Unsynchronized mesh
Potentially covered by 802.15.4

## Slide 33: Smart City: Smart Parking
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally, more than 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | Not required
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Layer-2

## Slide 34: Smart City: Smart Parking
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work

## Slide 35: Smart City: Smart Parking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1min
  Star or extended star
Not covered by existing standards

## Slide 36: Smart City: Vending Machines – general
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=64bytes
Availability | Medium
Latency | <60min
LP-WAN Localization Precision | Not required
Typical Power Supply | Energy Harvesting
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Layer-3

## Slide 37: Smart City: Vending Machines – general
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 64 bytes
  convolutional code or Turbo or Polar codes
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1h
   Only ALOHA may work

## Slide 38: Smart City: Vending Machines – general
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 60min
  Star or extended star
Not covered by existing standards

## Slide 39: Smart City: Vending Machines - Point of Sale
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Occasionally, more than 1/hour
Data Length (Uplink) | >256bytes
Availability | High
Latency | <10s
LP-WAN Localization Precision | Not required
Typical Power Supply | External
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Secure Authentication

## Slide 40: Smart City: Vending Machines - Point of Sale
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 256 bytes
  Turbo or Polar codes
MAC:
  Very high number of users, strong interference
  Uplink and downlink
  Latency < 10s
   ALOHA or fully synchronized network may work

## Slide 41: Smart City: Vending Machines - Point of Sale
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 10s
  Star or extended star, or unsynchronized mesh
Potentially covered by 802.15.4

## Slide 42: Smart City: Waste Management
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | Best effort
Latency | <60min
LP-WAN Localization Precision | Not required
Typical Power Supply | Energy Harvesting
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Layer-2

## Slide 43: Smart City: Waste Management
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1h
   Only ALOHA may work

## Slide 44: Smart City: Waste Management
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 60min
  Star or extended star
Not covered by existing standards

## Slide 45: Consumer/Medial: Pet Tracking
Channel Model | Parameter
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Periodically, more than 1/hour
Data Length (Uplink) | <=64bytes
Availability | Best effort
Latency | <1min
LP-WAN Localization Precision | <100m
Typical Power Supply | CR2025
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-2
Node Velocity | 3km/h

## Slide 46: Consumer/Medial: Pet Tracking
Modulation:
  High interference and many users
  Localization <100mt required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 64 bytes
  convolutional code or Turbo or Polar code
MAC:
  High number of users, strong interference
  Uplink only/downlink
  Latency < 1min
   Fully synchronized

## Slide 47: Consumer/Medial: Pet Tracking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 60min
  Multiple stations for localization
  Extended star or mesh
Really useful to employ LPWAN localization

## Slide 48: Remaining Uncovered Use-Cases
Domain | Use-Cases
Agriculture and Environmental | 
Consumer/Medical | Pet Tracking
Industrial | 
Infrastructure | Smart Grid - Fault Monitoring, Smart Metering, Structural Health Monitoring
Logistics | Global Tracking
Smart Building | 
Smart City | Smart Parking, Vending Machines – general, Waste Management

## Slide 49: Communalities of Uncovered Use-Cases
Communalities:
  Mainly focusing on uplink communication with limited downlink traffic
  Require large cells
  Are operated outdoors
  Have to support many users
  Suffer from interference
  Typically require LPWAN localization < 100m
  Require data length <= 16 bytes
  Have a latency requirement <1min

## Slide 50: Thank You for Your Interest!